## Slide 1: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 2: Agenda
Stored-Program Concept
R-Format
I-Format
S-Format
SB-Format
U-Format
UJ-Format

## Slide 3
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so assembler string “add x10,x11,x0” is meaningless to hardware

## Slide 4: Big Idea: Stored-Program Concept INSTRUCTIONS ARE DATA
programs can be stored in memory as numbers
Before: a number can mean anything
Now: make convention for interpreting numbers as instructions

## Slide 5
top
system reserved
stack
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
code (text)
static data
dynamic data (heap)
*Layout in 295
On actual hw code starts at
0x00400000

## Slide 6: Instructions as Numbers
Divide the 32 bits of an instruction into “fields”
  regular field sizes → simpler hardware
  will need some variation….
31
0
By convention, RISCV instructions are each 1 word = 4 bytes = 32 bits
Notes: 6 formats to memorize, but 4 formats to internalize (R with three registers, I with two registers and an immediate, S with two registers and an address, U with a big immediate/address)

## Slide 7: The 6 Instruction Formats
R-Format: instructions using 3 register inputs
  add, xor, mul —arithmetic/logical ops
I-Format: instructions with immediates, loads
  addi, lw, jalr, slli
S-Format: store instructions: sw,sb
SB-Format: branch instructions: beq, bge
U-Format: instructions with upper immediates
  lui, auipc —upper immediate is 20-bits
UJ-Format: the jump instruction: jal
Notes: lui: load upper immediate
auipc: adding an upper immediate to PC and putting the result in a register

## Slide 8: R-Format Example
RISCV Instruction: add x5,x6,x7
  Field representation (decimal):
  Field representation (binary):
two
0
0x33
7
6
0
5
31
0
0000000
0110011
00111
00110
000
00101
31
0
  hex representation: 0x 0073 02B3
  decimal representation: 7,537,331
  Called a Machine Language Instruction
Notes: x5 = t0, x6 = t1, x7 = t2

## Slide 9: I-Format Instructions (3/4)
opcode (7): uniquely specifies the instruction
rs1 (5): specifies a register operand
rd (5): specifies destination register that receives result of computation
imm[11:0]
func3
rd
opcode
31
0
rs1

## Slide 10: I-Format Instructions (4/4)
immediate (12): 12 bit number
  All computations done in words, so 12-bit immediate must be extended to 32 bits
  always sign-extended to 32-bits before use in an arithmetic operation
imm[11:0]
func3
rd
opcode
31
0
rs1
Can represent 212 different immediates
  imm[11:0] can hold values in range [-211 , +211)

## Slide 11: I-Format Example (1/2)
???
  addi x15,x1,-50
rd = x15
rs1 = x1
???
?
???
???
31
0
00001
imm[11:0]
func3
rd
opcode
rs1
111111001110
01111
0
0x13

## Slide 12: Load Instructions are also I-Type
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address, not to create final result
Value loaded from memory is stored in rd
imm[11:0]
func3
rd
opcode
31
0
rs1
offset[11:0]
width
dst
LOAD
base

## Slide 13: I-Format Load Example
imm[11:0]
func3
rd
opcode
31
0
rs1
offset[11:0]
width
dst
LOAD
base
lw x14, 8(x2)
000000001000
010
01110
0000011
00010
imm=+8
LW
rd=14
LOAD
rs1=2

## Slide 14: S-Format Used for Stores
Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well as need immediate offset!
Can’t have both rs2 and immediate in same place as other instructions!
Note: stores don’t write a value to the register file, no rd!
RISC-V design decision is move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
register names more critical than immediate bits in hardware design
imm[11:5]
opcode
rs2
rs1
func3
imm[4:0]
31
0

## Slide 15: S-Format Example
sw x14, 8(x2)
imm[11:5]
opcode
rs2
rs1
func3
imm[4:0]
31
0
00000000
0100011
01110
00010
010
01000
off[11:5] = 0
STORE
rs2=14
rs1=2
SW
off[4:0] = 8

## Slide 16: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -212 to +212-2 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
imm[12|10:5]
opcode
rs2
rs1
func3
imm[4:1|11]
31
0
7
7
5
5
3
5

## Slide 17: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Branch offset =
(Branch with offset of 0, branches to itself)
Start counting from instruction AFTER the branch
1
2
3
4
4×32-bit instructions = 16 bytes

## Slide 18: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Start counting from instruction AFTER the branch
1
2
3
4
???????
1100011
01010
10011
000
?????
31
0
7
7
5
5
3
5
BRANCH
rs2=10
rs1=19
BEQ

## Slide 19: Branch Example (1/2)
  beq x19,x10,offset = 16 bytes
  13-bit immediate, imm[12:0], with value 16 0000000010000
0 000000
1100011
01010
10011
000
1000 0
31
0
imm[12|10:5]
imm[4:1|11]
imm[0] discarded, always zero

## Slide 20: U-Format for “Upper Immediate” instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate
  AUIPC – Add Upper Immediate to PC
imm[31:12]
opcode
rd
31
0
20
U-immediate[31:12]
7
LUI/AUIPC
5
dest

## Slide 21: LUI to create long immediates
lui writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits
Together with an addi to set low 12 bits, can create any 32-bit value in a register using two instructions (lui/addi).
lui x10, 0x87654 # x10 = 0x87654000
addi x10, x10, 0x321 # x10 = 0x87654321

## Slide 22: UJ-Format Instructions (2/3)
jal saves PC+4 in register rd (the return address)
Set PC = PC + offset (PC-relative jump)
Target somewhere within ±219 locations, 2 bytes apart
±218 32-bit instructions
Reminder: “j” jump is a pseudo-instruction—the assembler will instead use jal but sets rd=x0 to discard return address
Immediate encoding optimized similarly to branch instruction to reduce hardware cost
imm[20|10:1|11|19:12]
opcode
rd
31
0
20
offset[31:12]
7
JAL
5
dest

## Slide 23: Uses of jalr
# ret and jr psuedo-instructions
ret = jr ra = jalr x0, ra, 0
# Call function at any 32-bit absolute address
lui x1, <hi 20 bits>
jalr ra, x1, <lo 12 bits>
# Jump PC-relative with 32-bit offset
auipc x1, <hi 20 bits>
jalr x0, x1, <lo 12 bits>
imm[11:0]
func3
rd
opcode
31
0
rs1
offset
0
dest
JALR
base

## Slide 24: Summary of RISC-V Instruction Formats