## Slide 1: Digital Logic - Combinational

## Slide 2: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 3: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 4: Why is this important?
Why study hardware design?
  Background for other more in-depth classes
  Only course in CMPT that deals with hardware
  We need some digital systems knowledge to build our own processor

## Slide 5: Why is this important?
We need some digital systems knowledge to build our own processor
Why build our own processor?
  Because we believe computer scientists should have an answer to the question “How does a computer work?”
  So you can understand how code is actually executed on a computer

## Slide 6: Why is this important?
So you can understand how code is actually executed on a computer
Why do we care about how code executes?
  Reliability
  Performance
  Security

## Slide 7: Hardware Design
Why study hardware design and processors and computers if you only care about high-level software?
Example of the power of layered abstractions
  Transistors -> Combinational Logic
  Combinational Logic -> Sequential Logic
  Sequential Logic -> Processors
  Processors -> Machine Language
  Machine Language -> Assembly
  Assembly -> High-level Programming Languages
  High-level Programming Languages -> Word,Minecraft,Twitter
At each step we can “abstract away” the lower steps and (mostly) forget they exist

## Slide 8: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system! (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    1 and 0 are complements of each other
  High/Low voltage for True/False, 1/0
Hardware of a processor, such as a RISC-V processor, is an example of a Synchronous Digital System

## Slide 10: Historical Trend
Trend:
Hardware gets more powerful every year.
  (Really due to hard work of thousands of engineers)
Therefore:
Software gets more resources and faster compute!
  (And has to keep up with ever-changing hardware)

## Slide 11: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 12: Type of Circuits
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 13: Logic Gates (1/2)
Special names and symbols:
NOT
AND
OR
a | b | c
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | c
0 | 1
1 | 0
Circle means NOT!

## Slide 14: Logic Gates (2/2)
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | c
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | c
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 15: Combining Multiple Logic Gates
A
B
C
D
(NOT(A AND B)) AND (A OR (NOT B AND C))

## Slide 16: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 17: Representations of Combinational Logic
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 18: Truth Tables
Table that relates the inputs to a combinational logic circuit to its output
  Output only depends on current inputs
  Use abstraction of 0/1 instead of high/low V
  Shows output for every possible combination of inputs
How big?
  0 or 1 for each of N inputs, so 2N rows

## Slide 19: General Form
F
Y
A
B
C
If N inputs, how many distinct functions F do we have?
Function maps each row to 0 or 1, so possible functions
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Y
F(0,0,0)
F(0,0,1)
F(0,1,0)
F(0,1,1)
F(1,0,0)
F(1,0,1)
F(1,1,0)
F(1,1,1)
0
1
0
0
0
1
1
0
2N
Notes: Circle the output, use variables/animations, talk about the output as a bit combination (integer?) Maybe 3 inputs?

## Slide 20: Multiple Outputs
For 3 outputs, just three indep. functions: X(A,B,C,D), Y(A,B,C,D), and Z(A,B,C,D)
  Can show functions in separate columns without adding any rows!
F
Y
A
B
C
D
X
Z

## Slide 21
Question: Convert the following statements into a Truth Table for: (x XOR y) OR (NOT z)
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 22
Question: Convert the following statements into a Truth Table for: (x XOR y) OR (NOT z)
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 23: More Complicated Truth Tables
3-Input Majority
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
2-bit Adder
A |  | B |  | C |  | 
a1 | a0 | b1 | b0 | c2 | c1 | c0
 |  |  | . |  |  | 
 |  |  | . |  |  | 
 |  |  | . |  |  | 
+
c1
a1
a0
b1
b0
c2
c0
How many
rows?

## Slide 24: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 25: My Hand Hurts…
Truth tables are huge
  Write out EVERY combination of inputs and outputs (thorough, but inefficient)
  Finding a particular combination of inputs involves scanning a large portion of the table
There must be a shorter way to represent combinational logic
  Boolean Algebra to the rescue!

## Slide 26: Boolean Algebra
Represent inputs and outputs as variables
  Each variable can only take on the value 0 or 1
Overbar or ¬ is NOT: “logical complement”
  e.g. if A is 0, A is 1. If A is 1, then ¬A is 0
Plus (+) is 2-input OR: “logical sum”
Product (·) is 2-input AND: “logical product”
  All other gates and logical expressions can be built from combinations of these ¬AB + A¬B == (NOT(A AND B)) OR (A AND NOT B)
For slides, will use ¬A

## Slide 27: Laws of Boolean Algebra
These laws allow us to perform simplification:
Notes: Demorgan’s law example

## Slide 28: Truth Table to Boolean Expression
We can show that these are equivalent!
Read off of table
  For 1, write variable name
  For 0, write complement of variable
Sum of Products (SoP)
  Take rows with 1’s in output column, sum products of inputs
  c=
Product of Sums (PoS)
  Take rows with 0’s in output column, product the sum of the complements of the inputs
  c =
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
¬a
b
+
a
¬b
(a + b) · (¬a + ¬b)
Notes: Choice between the two generally comes down to whether the output function has more 0’s or 1’s. Choosing the conversion (SoP/PoS) with less items will result in a shorter expression!
(This example happens to be balanced: 2 0’s and 2 1’s)

## Slide 29: Faster Hardware?
Recall: Everything we are dealing with is just an abstraction of transistors and wires
  Inputs propagating to the outputs are voltage signals passing through transistor networks
  There is always some delay before a CL’s output updates to reflect the inputs
Simpler Boolean expressions ↔ smaller transistor networks ↔ smaller circuit delays ↔ faster hardware

## Slide 30: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Finite State Machines
Functional Units
Summary
Bonus Slides
Logisim Intro
Notes: Should be at no later than 10

## Slide 31: Data Multiplexor
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this wire has n bits

## Slide 32: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 33: 1-bit 4-to-1 MUX (1/2)
Schematic:
Truth Table: How many rows?
Boolean Expression: e = ¬s1¬s0a + ¬s1s0b + s1¬s0c + s1s0d
26

## Slide 34: 1-bit 4-to-1 MUX (2/2)
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:

## Slide 35: Bonus slides (not testable)

## Slide 36: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 37: Manipulating Boolean Algebra
SoP and PoS expressions can still be long
  We wanted to have shorter representation than a truth table!
Boolean algebra follows a set of rules that allow for simplification
  Goal will be to arrive at the simplest equivalent expression
  Allows us to build simpler (and faster) hardware

## Slide 38: Boolean Algebraic Simplification Example
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = b
= ab + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 39: Circuit Simplification
(Transistors and/or Gates)
1)
2)
3)
4)

## Slide 40: Representations of Combinational Logic
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 41: Converting Combinational Logic
Try all input
combinations
SoP or PoS
Propagate signals through gates
Try all input combinations
Truth
Table
Boolean
Expression
Circuit
Diagram
This is difficult to do efficiently!
Wire inputs to proper gates
(easiest to use AND, OR, and NOT)

## Slide 42: Circuit Simplification Example (1/4)
Simplify the following circuit:
Options:
  Test all combinations of the inputs and build the Truth Table, then use SoP or PoS
  Write out expressions for signals based on gates
    Will show this method here
A
B
C
D

## Slide 43: Circuit Simplification Example (2/4)
Simplify the following circuit:
Start from left, propagate signals to the right
A
B
C
D
A
C
¬B
B
A
AB
¬BC
¬(AB)
A+¬BC
Arrive at D = ¬(AB)(A + ¬BC)

## Slide 44: Circuit Simplification Example (3/4)
Simplify Expression:
D = ¬(AB)(A + ¬BC)
= (¬A + ¬B)(A + ¬BC) DeMorgan’s
= ¬AA + ¬A¬BC + ¬BA + ¬B¬BC Distribution
= 0 + ¬A¬BC + ¬BA + ¬B¬BC Complementarity
= ¬A¬BC + ¬BA + ¬BC Idempotent Law
= (¬A + 1)¬BC + ¬BA Distribution
= ¬BC + ¬BA Law of 1’s
= ¬B(A + C) Distribution
Which of these is “simpler”?

## Slide 45: Circuit Simplification Example (4/4)
Draw out final circuit:
  D = ¬BC + ¬BA = ¬B(A + C)
Simplified Circuit:
  Reduction from 6 gates to 3!
How many gates do we need for each?
5
3
A
B
C
D
Notes: Also only has to go through 2 “stages” worth of gates as opposed to 4 previously.
Longest path here is B → NOT → AND → D. Before one of the longest paths was B → NOT → AND → OR → AND → D.