## Slide 1: Digital Logic - Sequential

## Slide 2: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 3: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Finite State Machines
Functional Units
Summary
Bonus Slides
Logisim Intro

## Slide 4: Type of Circuits
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 5: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 6: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: ‘S=0’?
Feedback
X

## Slide 7: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder

## Slide 8: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISCV)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 9: Registers
Same as registers in assembly:
small memory storage locations
Clock input (inputs active only on a clock “tick”)
Data input (can be various bit widths)
Data output (can be various bit widths)
Reset (sets value to zero)
Write Enable (can it be written to)

## Slide 10: Signals and Waveforms: Clocks
Signals transmitted over wires continuously
Transmission is effectively instantaneous
  Implies that any wire only contains one value at any given time
Rising Edge
Falling Edge
Clock period (CPU cycle time)

## Slide 11: Signals and Waveforms
  All signals change after clock “triggers”
Stack signals on top of each other

## Slide 12: Dealing with Waveform Diagrams
Easiest to start with CLK on top
  Solve signal by signal, from inputs to outputs
  Can only draw the waveform for a signal if all of its input waveforms are drawn
When does a signal update?
  A state element updates based on CLK triggers
  A combinational element updates ANY time ANY of its inputs changes

## Slide 13: Signals and Waveforms: Grouping
A group of wires when interpreted as a bit field is called a bus
X
Time

## Slide 14: Second Try: How About This?
Rough timing …
Time
Delay through Adder

## Slide 15: Register Internals
n instances of a “Flip-Flop”
  Output flips and flops between 0 and 1
Specifically this is a “D-type Flip-Flop”
  D is “data input”, Q is “data output”
  In reality, has 2 outputs (Q and Q), but we only care about 1
http://en.wikibooks.org/wiki/Practical_Electronics/Flip-flops
Notes: Can see Wikipedia page for gate internals and other types of flip-flops.

## Slide 16: Flip-Flop Timing Behavior (1/2)
Edge-triggered D-type flip-flop
  This one is “rising edge-triggered”
“On the rising edge of the clock, input d is sampled and transferred to the output. At other times, the input d is ignored and the previously sampled value is retained.”
Example waveforms:

## Slide 17: Flip-Flop Timing Terminology (1/3)
Camera Analogy: non-blurry digital photo
  Don’t move while camera shutter is opening
  Don’t move while camera shutter is closing
  Wait until image appears on the display

## Slide 18: Flip-Flop Timing Terminology (2/3)
Camera Analogy: Taking a photo
  Setup time: don’t move since about to take picture (open camera shutter)
  Hold time: need to hold still after shutter opens until camera shutter closes
  Time to data: time from open shutter until image appears on the output (viewfinder)

## Slide 19: Flip-Flop Timing Terminology (3/3)
Now applied to hardware:
  Setup Time: how long the input must be stable before the clock trigger for proper input read
  Hold Time: how long the input must be stable after the clock trigger for proper input read
  “Clock-to-Q” Delay: how long it takes the output to change, measured from the clock trigger

## Slide 20: Flip-Flop Timing Behavior

## Slide 21: Flip-Flop Timing Behavior
Setup Time

## Slide 22: Flip-Flop Timing Behavior
Hold Time

## Slide 23: Flip-Flop Timing Behavior
Clock-to-Q

## Slide 24: Accumulator Revisited Proper Timing
reset signal shown
In practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
“Undefined” (unknown) signal

## Slide 25: Review of Timing Terms
Clock: steady square wave that synchronizes system
Register: several bits of state that samples on rising edge of Clock (positive edge-triggered); also has RESET
Setup Time: when input must be stable before Clock trigger
Hold Time: when input must be stable after Clock trigger
Clock-to-Q Delay: how long it takes output to change from Clock trigger
Notes: STOP HERE

## Slide 26: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Finite State Machines
Functional Units
Summary
Bonus Slides
Logisim Intro

## Slide 27: Model for Synchronous Systems
Combinational logic blocks separated by registers
  Clock signal connects only to sequential logic elements
  Feedback is optional depending on application
How do we ensure proper behavior?
  How fast can we run our clock?

## Slide 28: When can the input change?
Needs to be stable for duration of setup time + hold time
Often unstable until at least clock-to-q time has passed
  Because register output isn’t ready yet
Needs to account for all combinational logic delay too

## Slide 29: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 30: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
Critical Path =
CLK-to-Q Delay
+ CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay
+ Setup Time

## Slide 31: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one.

## Slide 32: Pipelining and Clock Frequency (1/2)
Clock period limited by propagation delay of adder and shifter
  Add an extra register to reduce the critical path!
Timing:

## Slide 33: Pipelining and Clock Frequency (2/2)
Reduced critical path → allows higher clock freq.
Extra register → extra (shorter) cycle to produce first output
Notes: Notice anything weird?
Register with two inputs? (variable widths)
How is an adder or shifter implemented?

## Slide 34: Pipelining Basics
By adding more registers, break path into shorter “stages”
  Aim is to reduce critical path
  Signals take an additional clock cycle to propagate through each stage
New critical path must be calculated
  Affected by placement of new pipelining registers
  Faster clock rate → higher throughput (outputs)
  More stages → higher startup latency
Pipelining tends to improve performance
  More on this (and application to CPUs) later

## Slide 35
Question: Want to run on 1 GHz processor. tadd = 100 ps. tmult = 200 ps. tsetup = thold = 50 ps. What is the maximum clock-to-q time?
550 ps
(A)
750 ps
(B)
500 ps
(C)
700 ps
(D)
Notes: Spend 2-3 min on

## Slide 36
550 ps
(A)
750 ps
(B)
500 ps
(C)
700 ps
(D)
Bottom path is critical path:
clock-to-q + 100 + 200 + 100 + 50 < 1000 ps = 1ns
clock-to-q + 450 < 1000 ps
clock-to-q < 550
Question: Want to run on 1 GHz processor. tadd = 100 ps. tmult = 200 ps. tsetup = thold = 50 ps. What is the maximum clock-to-q time?

## Slide 37: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Functional Units
Summary
Bonus Slides
FSMs

## Slide 38: Functional Units (a.k.a. Execution Unit)
Now that we know sequential logic, we can explore some pieces of a processor!
Functional Units are a part of the processor that perform operations and calculations based on the running program
  Arithmetic Logic Unit
  Floating Point Unit
  Load/Store Unit
  and several more...
Invented by John Von Neumann
He also invented
Stored Program Concept
Mergesort
Mutually Assured Destruction
Notes: Should be at no later than 10

## Slide 39: Arithmetic Logic Unit (ALU)
Most processors contain a special logic block called the “Arithmetic Logic Unit” (ALU)
  We’ll show you an easy one that does ADD, SUB, bitwise AND, and bitwise OR
Schematic:
when S=00, R = A + B
when S=01, R = A – B
when S=10, R = A AND B
when S=11, R = A OR B

## Slide 40: Simple ALU Schematic
Notice that 3 values are ALWAYS calculated in parallel, but only 1 makes it to the Result

## Slide 41: Adder/Subtractor Design
Combinational Logic design we’ve seen before:
  write out truth table
  convert to boolean logic
  minimize logic
  then implement
How big might truth table and/or Boolean expression get?

## Slide 42: Adder/Subtractor Design
Break down the problem into smaller pieces that we can cascade or hierarchically layer
  Let’s try this approach instead

## Slide 43: Adder/Subtractor: 1-bit LSB Adder
Carry-out bit

## Slide 44: Adder/Subtractor: 1-bit Adder
Here defining XOR of many inputs to be 1 when an odd number of inputs are 1
Possible carry-in c1

## Slide 45: Adder/Subtractor: 1-bit Adder
Circuit Diagrams:

## Slide 46: N x 1-bit Adders → N-bit Adder
+
+
+
b0
Connect CarryOuti-1 to CarryIni to chain adders:

## Slide 47: Two’s Complement Adder/Subtractor
+
+
+
Subtraction accomplished by adding negated number:
x ^ 1 = x’
(flips the bits)
This signal is only high when you perform subtraction
Add 1
Where did this come from?

## Slide 48: Detecting Overflow
Unsigned overflow
  On addition, if carry-out from MSB is 1
  On subtraction, if carry-out from MSB is 0
    This case is a lot harder to see than you might think
Signed overflow
  Overflow from adding “large” positive numbers
  Overflow from adding “large” negative numbers
Notes: Unsigned: still use signed subtraction procedure (flip bits & add 1). When doing x-x, get all 1s plus 1, which leads to carry-out. If y>x in x-y, then fewer 1s in sum, so no carry-out.

## Slide 49: Signed Overflow Examples (4-bit)
Overflow from two positive numbers:
  0111 + 0111, 0111 + 0001, 0100 + 0100.
  Carry-out from the 2nd MSB (but not MSB)
    pos + pos ≠ neg
Overflow from two negative numbers:
  1000 + 1000, 1000 + 1111, 1011 + 1011.
  Carry-out from the MSB (but not 2nd MSB)
    neg + neg ≠ pos
Expression for signed overflow: Cn XOR Cn-1

## Slide 50: Simple ALU Schematic

## Slide 51: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Finite State Machines
Functional Units
Summary
Bonus Slides
Logisim Intro

## Slide 52: Summary
Hardware systems are constructed from Stateless Combinational Logic and Stateful Sequential Logic (includes registers)
Circuits have a delay to them, and the critical path (longest delay between registers) determines the maximum clock frequency

## Slide 53: Non Testable Material

## Slide 54: Back to representations
How do we represent sequential logic?
  Truth tables could account for history
  We could do boolean logic with prior state as a variable
We can also use a new representation: Finite State Machines

## Slide 55: Finite State Machines (FSMs)
A convenient way to conceptualize computation over time
Function can be represented with a state transition diagram
With combinational logic and registers, any FSM can be implemented in hardware!

## Slide 56: FSM Overview
An FSM (in this class) is defined by:
  A set of states S (circles)
  An initial state s0 (only arrow not between states)
  A transition function that maps from the current input and current state to the output and the next state (arrows between states)
State transitions are controlled by the clock:
  On each clock cycle the machine checks the inputs and generates a new state (could be same) and new output

## Slide 57: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
States: S0, S1, S2
Initial State: S0
Transitions of form:
input/output

## Slide 58: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 59: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 60: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 61: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 62: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 63: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 64: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 65: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue

## Slide 66: Example: 3 Ones FSM
FSM to detect 3 consecutive 1’s in the Input
Starting state in red
Resulting state in Blue
And so on...

## Slide 67: Hardware Implementation of FSM
Register holds a representation of the FSM’s state
  Must assign a unique bit pattern for each state
  Output is present/current state (PS/CS)
  Input is next state (NS)
Combinational Logic implements transition function (state transitions + output)
+
=

## Slide 68: FSM: Combinational Logic
Read off transitions into Truth Table!
  Inputs: Current State (CS) and Input (In)
  Outputs: Next State (NS) and Output (Out)
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
Notes: In lecture: Implement logic for Out (1 NOT, 2 AND gates)

## Slide 69: Unspecified Output Values
Our FSM has only 3 states
  2 entries in truth table are undefined/unspecified
Use symbol ‘X’ to mean it can be either a 0 or 1
  Make choice to simplify final expression
  Any choice is correct
CS | In | NS | Out
00 | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 0 | 00 | 0
01 | 1 | 10 | 0
10 | 0 | 00 | 0
10 | 1 | 00 | 1
11 | 0 | XX | X
11 | 1 | XX | X

## Slide 70: 3 Ones FSM in Hardware
  2-bit Register needed for state
  CL: NS1 = CS0In, NS0 = ¬CS1¬CS0In, Out = CS1In
Notes: 1050 cutoff