## Slide 1: Digital Logic - Combinational

## Slide 2: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system! (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    1 and 0 are complements of each other
  High/Low voltage for True/False, 1/0
Hardware of a processor, such as a RISC-V processor, is an example of a Synchronous Digital System

## Slide 3: Type of Circuits
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    e.g. circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    a.k.a. “State Elements”
    e.g. memory and registers (Registers)

## Slide 4: Logic Gates (1/2)
Special names and symbols:
NOT
AND
OR
a | b | c
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | c
0 | 1
1 | 0
Circle means NOT!

## Slide 5: Logic Gates (2/2)
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | c
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | c
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 6: Combining Multiple Logic Gates
A
B
C
D
(NOT(A AND B)) AND (A OR (NOT B AND C))

## Slide 7: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 8: General Form
F
Y
A
B
C
If N inputs, how many distinct functions F do we have?
Function maps each row to 0 or 1, so possible functions
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Y
F(0,0,0)
F(0,0,1)
F(0,1,0)
F(0,1,1)
F(1,0,0)
F(1,0,1)
F(1,1,0)
F(1,1,1)
0
1
0
0
0
1
1
0
2N
Notes: Circle the output, use variables/animations, talk about the output as a bit combination (integer?) Maybe 3 inputs?

## Slide 9: More Complicated Truth Tables
3-Input Majority
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
2-bit Adder
A |  | B |  | C |  | 
a1 | a0 | b1 | b0 | c2 | c1 | c0
 |  |  | . |  |  | 
 |  |  | . |  |  | 
 |  |  | . |  |  | 
+
c1
a1
a0
b1
b0
c2
c0
How many
rows?

## Slide 10: Agenda
Combinational Logic
  Combinational Logic Gates
  Truth Tables
  Boolean Algebra
  Circuit Simplification

## Slide 11: Boolean Algebra
Represent inputs and outputs as variables
  Each variable can only take on the value 0 or 1
Overbar or ¬ is NOT: “logical complement”
  e.g. if A is 0, A is 1. If A is 1, then ¬A is 0
Plus (+) is 2-input OR: “logical sum”
Product (·) is 2-input AND: “logical product”
  All other gates and logical expressions can be built from combinations of these ¬AB + A¬B == (NOT(A AND B)) OR (A AND NOT B)
For slides, will use ¬A

## Slide 12: Laws of Boolean Algebra
These laws allow us to perform simplification:
Notes: Demorgan’s law example

## Slide 13: Agenda
Muxes
Sequential Logic Timing
Maximum Clock Frequency
Finite State Machines
Functional Units
Summary
Bonus Slides
Logisim Intro
Notes: Should be at no later than 10

## Slide 14: Data Multiplexor
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this wire has n bits

## Slide 15: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 16: 1-bit 4-to-1 MUX (1/2)
Schematic:
Truth Table: How many rows?
Boolean Expression: e = ¬s1¬s0a + ¬s1s0b + s1¬s0c + s1s0d
26

## Slide 17: 1-bit 4-to-1 MUX (2/2)
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:

## Slide 18: Circuit Simplification
(Transistors and/or Gates)
1)
2)
3)
4)

## Slide 19: Circuit Simplification Example (2/4)
Simplify the following circuit:
Start from left, propagate signals to the right
A
B
C
D
A
C
¬B
B
A
AB
¬BC
¬(AB)
A+¬BC
Arrive at D = ¬(AB)(A + ¬BC)

## Slide 20: Circuit Simplification Example (3/4)
Simplify Expression:
D = ¬(AB)(A + ¬BC)
= (¬A + ¬B)(A + ¬BC) DeMorgan’s
= ¬AA + ¬A¬BC + ¬BA + ¬B¬BC Distribution
= 0 + ¬A¬BC + ¬BA + ¬B¬BC Complementarity
= ¬A¬BC + ¬BA + ¬BC Idempotent Law
= (¬A + 1)¬BC + ¬BA Distribution
= ¬BC + ¬BA Law of 1’s
= ¬B(A + C) Distribution
Which of these is “simpler”?

## Slide 21: Circuit Simplification Example (4/4)
Draw out final circuit:
  D = ¬BC + ¬BA = ¬B(A + C)
Simplified Circuit:
  Reduction from 6 gates to 3!
How many gates do we need for each?
5
3
A
B
C
D
Notes: Also only has to go through 2 “stages” worth of gates as opposed to 4 previously.
Longest path here is B → NOT → AND → D. Before one of the longest paths was B → NOT → AND → OR → AND → D.

## Slide 22: Digital Logic - Sequential

## Slide 23: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 24: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder

## Slide 25: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISCV)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 26: Registers
Same as registers in assembly:
small memory storage locations
Clock input (inputs active only on a clock “tick”)
Data input (can be various bit widths)
Data output (can be various bit widths)
Reset (sets value to zero)
Write Enable (can it be written to)

## Slide 27: Signals and Waveforms: Clocks
Signals transmitted over wires continuously
Transmission is effectively instantaneous
  Implies that any wire only contains one value at any given time
Rising Edge
Falling Edge
Clock period (CPU cycle time)

## Slide 28: Review of Timing Terms
Clock: steady square wave that synchronizes system
Register: several bits of state that samples on rising edge of Clock (positive edge-triggered); also has RESET
Setup Time: when input must be stable before Clock trigger
Hold Time: when input must be stable after Clock trigger
Clock-to-Q Delay: how long it takes output to change from Clock trigger
Notes: STOP HERE

## Slide 29: Model for Synchronous Systems
Combinational logic blocks separated by registers
  Clock signal connects only to sequential logic elements
  Feedback is optional depending on application
How do we ensure proper behavior?
  How fast can we run our clock?

## Slide 30: When can the input change?
Needs to be stable for duration of setup time + hold time
Often unstable until at least clock-to-q time has passed
  Because register output isn’t ready yet
Needs to account for all combinational logic delay too

## Slide 31: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 32: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
Critical Path =
CLK-to-Q Delay
+ CL Delay 1
+ CL Delay 2
+ CL Delay 3
+ Adder Delay
+ Setup Time

## Slide 33: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one.

## Slide 34: Pipelining and Clock Frequency (1/2)
Clock period limited by propagation delay of adder and shifter
  Add an extra register to reduce the critical path!
Timing:

## Slide 35: Pipelining and Clock Frequency (2/2)
Reduced critical path → allows higher clock freq.
Extra register → extra (shorter) cycle to produce first output
Notes: Notice anything weird?
Register with two inputs? (variable widths)
How is an adder or shifter implemented?

## Slide 36: Pipelining Basics
By adding more registers, break path into shorter “stages”
  Aim is to reduce critical path
  Signals take an additional clock cycle to propagate through each stage
New critical path must be calculated
  Affected by placement of new pipelining registers
  Faster clock rate → higher throughput (outputs)
  More stages → higher startup latency
Pipelining tends to improve performance
  More on this (and application to CPUs) later