## Slide 1: Control Signals: Big picture!
Control signals are how we get the same hardware to behave differently and produce different instructions
For every instruction, all control signals are set to one of their possible values (Not always 0 or 1!) or an indeterminate (*) value indicating the control signal doesn’t affect the instruction’s execution
Each control signal has a sub-circuit based on ~nine bits from the instruction format:
  Upper 5 func7 bits (lower 2 are the same for all 295 instructions)
  All func3 bits
  “2nd” upper opcode bit (others are the same for all 295 instructions)

## Slide 2: Let’s try an example!
Design PCSel yourself!
I recognise this is hard, given you don’t all have logic simulator in front of you :( describe the circuit and its dependencies as best you can !
Might help to split it into three cases:
Regular (non-control) instructions
Branches
Jumps
You may assume PCSel = 0 → PC = PC + 4, and PCSel = 1 → PC = ALUout

## Slide 3: Control Signals: ADD
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 4: ADD: Control Signals
Here are the signals and values we’ve compiled for our ADD instruction:
(green = left 3 cols = control INPUTS)
(orange = right 9 cols = control OUTPUTS)
Inst[31:0] | BrEq | BrLT | PCSel | ImmSel | BrUn | ASel | BSel | ALUSel | MemRW | RegWEn | WBSel
add | * | * | +4 | * | * | Reg | Reg | Add | Read | 1 (Y) | ALU

## Slide 5: addi datapath
Control Logic
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrLT | BrEq | BSel | ASel | ALUSel | MemRW | WBSel
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU

## Slide 6: lw datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem

## Slide 7: Br datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *

## Slide 8: Jal datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4

## Slide 9
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 10: Agenda
Quick Datapath Review
Control Implementation
Performance Analysis
Pipelined Execution
Pipelined Datapath

## Slide 11: Instruction Timing
IF | ID | EX | MEM | WB | Total
IMEM | Reg Read | ALU | DMEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 12: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time! ex. “IF” active every 600ps
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  | X | 600ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps
Instruction 1
Instruction 2
ID
MEM
WB
ALU
IF
ID
MEM
WB
ALU
IF
Clk

## Slide 13: Performance Measures
In our example, CPU executes instructions at 1.25 GHz
  1 instruction every 800 ps
Can we improve its performance?
  What do we mean with this statement?
  Not so obvious:
    Quicker response time, so one job finishes faster?
    More jobs per unit time (e.g. web server returning pages)?
    Longer battery life?

## Slide 14: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 15: Speed Trade-off Example
For some task (e.g. image compression) …
 | Processor A | Processor B
# Instructions | 1 Million | 1.5 Million
Average CPI | 2.5 | 1
Clock rate f | 2.5 GHz | 2 GHz
Execution time | 1 ms | 0.75 ms
Processor B is faster for this task, despite executing more instructions and having a lower clock rate! Why? Each instruction is less complex! (~2.5 B instructions = 1 A instruction)

## Slide 16: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Performance Analysis
Pipelined Execution
Pipelined Datapath

## Slide 17: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
1 load finishes every half hour (after the first load, which takes 2 hours)
T
a
s
k
O
r
d
e
r
B
N
A
M
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 18: Pipelining Lessons (1/2)
Pipelining doesn’t decrease latency of single task; it increases throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup ~ number of pipeline stages
Speedup reduced by time to fill and drain the pipeline: 8 hours/3.5 hours which gives 2.3X speedup v. potential 4X in this example
6 PM
7
8
9
Time
30
30
30
30
30
30
30
B
N
A
M
T
a
s
k
O
r
d
e
r

## Slide 19: Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep = 100 … 200 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Notes: Tc = “Time between completion of instructions”

## Slide 20: RISC-V Pipeline
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
Resource use by instruction over time
Resource use in a particular time slot

## Slide 21: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 22: Instruction Level Parallelism (ILP)
Pipelining allows us to execute parts of multiple instructions at the same time using the same hardware!
  This is known as instruction level parallelism
Later: Other types of parallelism
  DLP: same operation on lots of data (SIMD)
  TLP: executing multiple threads “simultaneously” (OpenMP)

## Slide 23
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be 1.25x slower.
The throughput will be 3x faster.
F F
(A)
F T
(B)
T F
(C)
T T
(D)
1 2
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access
throughput:
(IF+ID+EX+WB) = 600 →
(4*max_stage)/4 = 200
old/new = 600/200 = 3x faster
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 24
F F
(A)
F T
(B)
T F
(C)
T T
(D)
1 2
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access! Latency:
IF+ID+EX+WB = 600 →
4*max_stage = 800
old/new = 600/800 = negative speedup! 800/600 = 1.33x slower!
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be 1.25x slower.
The throughput will be 3x faster.
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 25
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be 1.25x slower.
The throughput will be 3x faster.
F F
(A)
F T
(B)
T F
(C)
T T
(D)
1 2
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 26: Summary
Implementing controller for your datapath
  Ask yourself the questions on the beginning slides!
  Work in stages, put everything together at the end!
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for RV32I: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  Each instruction has the same latency, but there’s better throughput
  Think: what problems does pipelining introduce? (more on this next lecture)