## Slide 1: Agenda
RISC-V Pipeline
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors
Hazards Ahead!

## Slide 2: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data write
Control hazard
  Flow of execution depends on previous instruction

## Slide 3: Structural Hazard: Regfile!
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
Time (clock cycles)
RegFile: Used in ID and WB!

## Slide 4: Regfile Structural Hazards
Each instruction:
  can read up to two operands in decode stage
  can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 5: Regfile Structural Hazards
Two alternate solutions:
  Build RegFile with independent read and write ports (what you will do in the project; good for single-stage)
  Double Pumping: split RegFile access in two! Prepare to write during 1st half, write on falling edge, read during 2nd half of each clock cycle
    Will save us a cycle later...
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
Conclusion: Read and Write to registers during same clock cycle is okay

## Slide 6: Structural Hazard: Memory Access
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Instruction and data memory used simultaneously
  Use two separate memories

## Slide 7: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory unit
  Load/store requires data access
  Without separate memory units, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memory units
  Or separate instruction/data caches
RISC ISAs (including RISC-V) designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 8: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add s0, s1, s2
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
Stored
during WB
Read during ID

## Slide 9: 2. Data Hazards (2/2)
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2
Time (clock cycles)
Identifying data hazards:
Where is data WRITTEN?
Where is data READ?
Does the WRITE happen AFTER the READ?

## Slide 10: Solution 1: Stalling
Problem: Instruction depends on result from previous instruction
  add s0, s1, s2 sub s4, s0, s3
Bubble:
  effecsively NOP: affecsed pipeline ssages do “nothing” (add x0 x0 x0)

## Slide 11: Data Hazard Solution: Forwarding
Forward result as soon as it is available, even though it’s not stored in RegFile yet
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2
Forwarding: grab operand from pipeline stage, rather than register file

## Slide 12
In our 5-stage pipeline, how many subsequent instructions do we need to look at to detect data hazards for this add? Assume we have double-pumping.
1 instruction
2 instructions
3 instructions
4 instructions
5 instructions
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2

## Slide 13: Data Hazard: Loads (1/4)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load (sub), then forward after the load is done (more hardware)
sub t3, t0, t2
lw t0, 0(t1)

## Slide 14: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware will stall for one cycle
  Equivalent to inserting an explicit nop in the slot
    except the latter uses more code space
  Performance loss
Idea: Let the compiler/assembler put an unrelated instruction in that slot → no stall!

## Slide 15: 3. Control Hazards
Branch (beq, bne,...) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Result isn’t known until end of execute
Simple Solution: Stall or flush on every branch until we have the new PC value
  How long must we stall?

## Slide 16
How many instructions after beq are affected by the control hazard?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4

## Slide 17: Branch Stall
How many bubbles required for branch?
beq
Instr 1
Instr 2
Instr 3
Instr 4
Time (clock cycles)

## Slide 18: 3. Control Hazard: Branching
RISC-V Solution: Branch Prediction – guess outcome of a branch, fix afterwards if necessary
  Must cancel (flush) all instructions in pipeline that depended on guess that was wrong
  How many instructions do we end up flushing?

## Slide 19: Kill Instructions after Branch if Taken
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
label: xxxxxx
PC updated reflecting branch outcome
Taken branch
Convert to NOP
Convert to NOP
Two instructions are affected by an incorrect branch, just like we’d have to insert two NOP’s/stalls in the pipeline to wait on the correct value!

## Slide 20: Branch Prediction
beq t0, t1, label
label: …..
…..
Taken branch
Guess next PC!
Check guess correct
In the correct case, we don’t have any stalls/NOP’s at all!
Prediction, if done correctly, is better on average than stalling