## Slide 1: Aside: Registers are Inside the Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 2: RISC V Integer Registers – 32 bits wide
Notes: Names are largely arbitrary, reasons behind them are not super relevant to us
But there are conventions about how they are used
One is particularly important to not misuse: %sp
  Stack pointer; we’ll get to this when we talk about procedures
Each is 4-bytes wide

## Slide 3: RISCV Instructions (1/2)
Instruction Syntax is rigid:
op dst, src1, src2
  1 operator, 3 operands
    op = operation name (“operator”)
    dst = register getting result (“destination”)
    src1 = first register for operation (“source 1”)
    src2 = second register for operation (“source 2”)
Keep hardware simple via regularity

## Slide 4: RISCV Instructions Example
Your very first instructions! (assume here that the variables a, b, and c are assigned to registers s1, s2, and s3, respectively)
Integer Addition (add)
  C: a = b + c
  RISCV: add s1, s2, s3
Integer Subtraction (sub)
  C: a = b - c
  RISCV: sub s1, s2, s3

## Slide 5: RISCV Instructions Example
Ordering of instructions matters (must follow order of operations)
Utilize temporary registers
Suppose a → s0,b → s1,c → s2,d → s3 and e → s4. Convert the following C statement to RISCV:
a = (b + c) - (d + e);
add t1, s3, s4
add t2, s1, s2
sub s0, t2, t1
Notes: add s0, s1, s2
add t0, s3, s4
sub s0, s0, t0
Suppose a -> s0, b->s1, c-> s2, d->s3 and e->s4. Convert the following C statement to RISCV:
a = (b + c) - (d + e);
add t1, s3, s4
add t2, s1, s2
sub s0, t2, t1

## Slide 6: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic operation on register or memory data
  c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
    Remember: Memory is indexed just like an array of bytes!

## Slide 7: Immediates
Numerical constants are called immediates
Separate instruction syntax for immediates:
opi dst, src, imm
  Operation names end with ‘i’, replace 2nd source register with an immediate
Example Uses:
  addi s1, s2, 5 # a=b+5
  addi s3, s3, 1 # c++
Why no subi instruction?
Notes: Goal of RISC is to minimize instruction set. subi dst, src, imm = addi dst, src, -imm.

## Slide 8: Load from Memory to Register
C code
int A[100];
g = h + A[3];
Using Load Word (lw) in RISC-V:
lw x10,12(x15) # Reg x10 gets A[3]
add x11,x12,x10 # g = h + A[3]
Note: x15 – base register (pointer to A[0])
12 – offset in bytes
Offset must be a constant known at assembly time
Data flow

## Slide 9: Store from Register to Memory
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in RISC-V:
lw x10,12(x15) # Temp reg x10 gets A[3]
add x10,x12,x10 # Temp reg x10 gets h + A[3]
sw x10,40(x15) # A[10] = h + A[3]
Note: x15 – base register (pointer)
12,40 – offsets in bytes
x15+12 and x15+40 must be multiples of 4
Data flow
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 10: Decision Making Instructions
Branch If Equal (beq)
  beq reg1,reg2,label
  If value in reg1 = value in reg2, go to label
Branch If Not Equal (bne)
  bne reg1,reg2,label
  If value in reg1 ≠ value in reg2, go to label
Jump (j)
  j label
  Unconditional jump to label

## Slide 11: Branching on Conditions other than (Not) Equal
Set Less Than (slt)
  slt dst, reg1,reg2
  If value in reg1 < value in reg2, dst = 1, else 0
Set Less Than Immediate (slti)
  slti dst, reg1,imm
  If value in reg1 < imm, dst = 1, else 0

## Slide 12: Branching on Conditions other than (Not) Equal
Branch Less Than (blt)
  blt reg1,reg2, label
  If value in reg1 < value in reg2, go to label
Branch Greater Than or Equal (bge)
  bge reg1,reg2, label
  If value in reg1 >= value in reg2, go to label

## Slide 13: “And in Conclusion…”
Memory is byte-addressable, but lw and sw access one word at a time.
A pointer (used by lw and sw) is just a memory address, we can add to it or subtract from it (using offset).
A Decision allows us to decide what to execute at run-time rather than compile-time.
C Decisions are made using conditional statements within if, while, do while, for.
RISC-V Decision making instructions are the conditional branches: beq and bne.
New Instructions:
  lw, sw, lb, sb, lbu, beq, bne, blt, bltu, bge, j

## Slide 14: Breaking Down the If Else
C Code:
if(i<j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
RISCV (???):
# i→s0, j→s1
# a→s2, b→s3
slt t0 s0 s1
beq t0,x0,else
then:
add s2, s3, x0
j end
else:
sub s2, x0, s3
end:
???
???

## Slide 15: Branching on Conditions other than (Not) Equal
Branch Less Than (blt)
  blt reg1,reg2, label
  If value in reg1 < value in reg2, go to label
Branch Greater Than or Equal (bge)
  bge reg1,reg2, label
  If value in reg1 >= value in reg2, go to label

## Slide 16: Breaking Down the If Else
C Code:
if(i<j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
RISCV (???):
# i→s0, j→s1
# a→s2, b→s3
bge s0,s1,else
then:
add s2, s3, x0
j end
else:
sub s2, x0, s3
end:
???

## Slide 17: C to RISCV Practice
Let’s put our all of our new RISCV knowledge to use in an example: “Fast String Copy”
C code is as follows:
/* Copy string from p to q */
char *p, *q;
while((*q++ = *p++) != ‘\0’) ;
What do we know about its structure?
  Single while loop
  Exit condition is an equality test

## Slide 18: C to RISCV Practice
Start with code skeleton:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
# t0 = *p
# *q = t0
# p = p + 1
# q = q + 1
# if *p==0, go to Exit
# go to Loop

## Slide 19: C to RISCV Practice
Fill in lines:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # t0 = *p
sb $t0,0($s1) # *q = t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
lb t0,0(s0)
sb t0,0(s1)
addi s0,s0,1
addi s1,s1,1
beq t0,0,Exit

## Slide 20: C to RISCV Practice
Finished code:
# copy String p to q
# p→$s0, q→$s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
beq t0,x0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
Notes: Is this the only way to write out this function? Of course not.

## Slide 21: C to RISCV Practice
Alternate code using bne:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
bne t0,x0,Loop # if *p!=0, go to Loop
# N chars in p => N*5 instructions
Notes: Used fewer instructions!
Instead of “exit when equal to zero”, we are now using “loop when not equal to zero.”

## Slide 22: RISCV Bitwise Instructions
Note: a→s1, b→s2, c→s3
Instruction | C | RISCV
And | a = b & c; | and s1,s2,s3
And Immediate | a = b & 0x1; | andi s1,s2,0x1
Or | a = b ¦ c; | or s1,s2,s3
Or Immediate | a = b ¦ 0x5; | ori s1,s2,0x5
Exclusive Or | a = b ^ c; | xor s1,s2,s3
Exclusive Or Immediate | a = b ^ 0xF; | xori s1,s2,0xF

## Slide 23: Shifting Instructions
Instruction Name | RISCV
Shift Left Logical | sll s1,s2,s3
Shift Left Logical Imm | slli s1,s2,imm
Shift Right Logical | srl s1,s2,s3
Shift Right Logical Imm | srli s1,s2,imm
Shift Right Arithmetic | sra s1,s2,s3
Shift Right Arithmetic Imm | srai s1,s2,imm
When using immediate, only values 0-31 are practical
When using variable, only lowest 5 bits are used (read as unsigned)

## Slide 24: Shifting Instructions
Example 1:
# lb using lw: lb s1,1(s0)
lw s1,0(s0) # get word
andi s1,s1,0xFF00 # get 2nd byte
srli s1,s1,8 # shift into lowest

## Slide 25: Shifting Instructions
Example 2:
# sb using sw: sb s1,3(s0)
lw t0,0(s0) # get current word
andi t0,t0,0xFFFFFF # zero top byte
slli t1,s1,24 # shift into highest
or t0,t0,t1 # combine
sw t0,0(s0) # store back

## Slide 26: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
Implemented with:
  Jump table
  Indirect jump instruction
long switch_ex
(long x, long y, long z)
{
long w = 1;
switch (x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 27: Jump Table Structure
Code
Block 0
Targ0:
Code Block 1
Targ1:
Code Block 2
Targ2:
Code Block n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
target = JTab[x];
goto target;
switch (x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 28: Jump Table Structure
switch (x) {
case 1: <some code>
break;
case 2: <some code>
case 3: <some code>
break;
case 5:
case 6: <some code>
break;
default: <some code>
}
Code
Blocks
Memory
Use the jump table when x 6:
if (x <= 6)
target = JTab[x];
goto target;
else
goto default;
C code:
0
1
2
3
4
5
6
Jump
Table

## Slide 29: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
declaring data, not instructions
8-byte memory alignment
this data is 64-bits wide
Notes: .rodata – read-only data section

## Slide 30: Handling Fall-Through
long w = 1;
. . .
switch (x) {
. . .
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
. . .
}
case 3:
w = 1;
case 2:
w = y/z;
goto merge;
merge:
w += z;
More complicated choice than “just fall-through” forced by “migration” of w = 1;
  Example compilation trade-off