## Slide 1: More RISC-V, RISC-V Functions

## Slide 2: Summary
RISC Design Principles
  Smaller is faster: 32 registers, fewer instructions
  Keep it simple: rigid syntax
RISC-V Registers: s0-s11, t0-t6, x0
  No data types, just raw bits, operations determine how they are interpreted
Memory is byte-addressed
  no types → no automatic pointer arithmetic

## Slide 3
RISC-V Instructions
  Arithmetic: add, sub, addi, mult,div
  Data Transfer: lw, sw, lb, sb, lbu
  Branching: beq, bne, j, bge, blt,
jal;
  Bitwise: and, or, xor, andi, ori, xori
  Shifting: sll, srl, sra, slli, srli, srai
i = “immediate” (constant integer)
Notes: Instructions shown in orange were presented in bonus slides from last lecture.

## Slide 4: Memory and Variable Size
So Far:
  lw reg, off(bAddr)
  sw reg, off(bAddr)
What about characters (1B) and shorts (sometimes 2B), etc?
Want to be able to use interact with memory values smaller than a word.
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
lw reg off(bAddr)
sw reg off(bAddr)
Notes: lb/sb have same syntax as lw/sw
Aside: also load/store halfword (lh/sh)

## Slide 5: Trading Bytes with Memory (2 approaches)
Method 1: Move words in and out of memory using bit-masking and shifting
lw s0,0(s1)
andi s0,s0,0xFF # lowest byte
Method 2: Load/store byte instructions
lb s1,1(s0)
sb s1,0(s0)
00 | 00 | 01 | 80
*(s0) = 0x00000180
Notes: If it’s not aligned, which part of the word are we pulling from?!

## Slide 6: Endianness
Big Endian: Most-significant byte at least address of word
  word address = address of most significant byte
Little Endian: Least-significant byte at least address of word
  word address = address of least significant byte
msb
lsb
3(s0) 2(s0) 1(s0) 0(s0)
0(s0) 1(s0) 2(s0) 3(s0)
big endian
little endian
00 | 00 | 01 | 80
*(s0) = 0x00000180
RISC-V is Little Endian

## Slide 7: Byte Instructions
lb/sb utilize the least significant byte of the register
  On sb, upper 24 bits are ignored
  On lb, upper 24 bits are filled by sign-extension
For example, let *(s0) = 0x00000180:
lb s1,1(s0)
lb s2,0(s0)
sb s2,2(s0)
# s1=0x00000001
# s2=0xFFFFFF80
# *(s0)=0x00800180

## Slide 8: Half-Word Instructions Unsigned Instructions
lh reg, off(bAddr) “load half”
sh reg, off(bAddr) “store half”
  On sh, upper 16 bits are ignored
  On lh, upper 16 bits are filled by sign-extension
lhu reg, off(bAddr)“load half unsigned”
lbu reg, off(bAddr)“load byte unsigned”
  On l(b/h)u, upper bits are filled by zero-extension
Why no s(h/b)u? Why no lwu?

## Slide 9: Agenda
More Memory Instructions
Inequalities
Pseudo-Instructions
Bonus: Memory Address Convention
Bonus: Alternate Register Convention Analogy
Notes: do additional slt stuff
Then do additional memory instructions
then summarize unsigned?

## Slide 10: Inequalities in RISC-V
Set Less Than (slt)
  slt dst,reg1,reg2
  if value in reg1 < value in reg2, dst = 1, else 0
Set Less Than Immediate (slti)
  slti dst,reg1,imm
  If value in reg1 < imm, dst = 1, else 0
These values are all interpreted as signed values
What if we want to compare unsigned numbers?

## Slide 11: Unsigned Inequalities
# s0=0xFFFFFFFF
# t0=1 (-1 < 1)
# t1=0 (232-1 >>> 1)
Unsigned versions of slt(i):
  sltu dst,src1,src2: unsigned comparison
  sltiu dst,src,imm: unsigned comparison against constant
Example:
addi s0,x0,-1
slti t0,s0,1
sltiu t1,s0,1
Notes: Do this first

## Slide 12: Aside: RISC-V Signed vs. Unsigned
RISC-V terms “signed” and “unsigned” appear in 2 different contexts:
  Signed vs. unsigned bit extension
    lb,lh
    lbu,lhu
  Signed vs. unsigned comparison
    slt, slti
    sltu, sltiu

## Slide 13
j < 2 || j < i
(A)
j ≥ 2 && j < i
(B)
j < 2 || j ≥ i
(C)
j < 2 && j ≥ i
(D)
Question: What C code properly fills in the
following blank?
do {i--; } while((z = ____________));
Loop: # i→s0, j→s1
addi s0,s0,-1 # i = i - 1 slti t0,s1,2 # t0 = (j < 2)
bne t0,x0 Loop # goto Loop if t0!=0
slt t0,s1,s0 # t1 = (j < i) bne t0,x0 ,Loop # goto Loop if t0!=0
Notes: !False = true comic

## Slide 14
j < 2 || j < i
(A)
j ≥ 2 && j < i
(B)
j < 2 || j ≥ i
(C)
j < 2 && j ≥ i
(D)
Question: What C code properly fills in the
following blank?
do {i--; } while((z = ____________));
Loop: # i→s0, j→s1
addi s0,s0,-1 # i = i - 1 slti t0,s1,2 # t0 = (j < 2)
bne t0,x0 Loop # goto Loop if t0!=0
slt t0,s1,s0 # t1 = (j < i) bne t0,x0 ,Loop # goto Loop if t0!=0
Notes: !False = true comic

## Slide 15: Agenda
More Memory Instructions
Inequalities
Administrivia
Pseudo-Instructions
Bonus: Memory Address Convention
Bonus: Alternate Register Convention Analogy
Notes: do additional slt stuff
Then do additional memory instructions
then summarize unsigned?

## Slide 16: Assembler Pseudo-Instructions
more intuitive for programmers, but NOT directly implemented in hardware
translated later into instructions which are directly implemented in hardware
Example:
mv dst,reg1 translated into
addi dst,reg1,0 or add dst,reg1,x0
Full list of RISC-V supported pseudo instructions are on the greensheet

## Slide 17: More Pseudo-Instructions
Load Immediate (li)
  li dst,imm
  Loads 32-bit immediate into dst
  translates to: addi dst x0 imm
Load Address (la)
  la dst,label
  Loads address of specified label into dst
  (translation omitted)

## Slide 18: J is a Pseudo-Instruction
Even the j instruction is actually a pseudo-Instruction
  We will see what this converts to later this lecture
Pseudo-Instructions are core to writing RISC assembly code and you will see it in any RISC assembly code you read

## Slide 19: True Assembly vs RISC-V
True Assembly Language
  The instructions a computer understands and executes (directly implemented in hardware!)
RISC-V Assembly Language
  Instructions the assembly programmer can use (includes pseudo-instructions)
  Each RISC-V Assembly instruction becomes 1 or more True Assemblt instructions
True Assembly ⊂ RISC-V Assembly