## Slide 1: Caches III
https://what-if.xkcd.com/111/

## Slide 2: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 3: General Cache Organization (, , )
= blocks/lines per set
= # sets
=
set
“line” (block plus management bits)
0
1
2
K-1
Tag
V
valid bit
= bytes per block
Cache size:
data bytes
(doesn’t include V or Tag)
Notes: “Layers” of a cache:
Block (data)
Line (data + management bits)
Set (many lines based on associativity)
Cache (many sets based on cache size & associativity)
Valid bit lets us know if this line has been initialized (“is valid”).

## Slide 4: Notation Review
We just introduced a lot of new variable names!
  Please be mindful of block size notation when you look at past exam questions or are watching videos
Variable | This Quarter | Formulas
Block size | ( in book) | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width | ( in book) | 
Variable | This Quarter | Formulas
Block size |  | 
Cache size |  | 
Associativity |  | 
Number of Sets |  | 
Address space |  | 
Address width |  | 
Tag field width |  | 
Index field width |  | 
Offset field width |  | 
Notes: Review this on your own
DON’T MEMORIZE FORUMLAS

## Slide 5: Example Cache Parameters Problem
4 KiB address space, 125 cycles to go to memory. Fill in the following table:
Cache Size | 256 B
Block Size | 32 B
Associativity | 2-way
Hit Time | 3 cycles
Miss Rate | 20%
Tag Bits | 
Index Bits | 
Offset Bits | 
AMAT | 
Notes: Tag bits = 5
Index bits = 2
Offset bits = 5
AMAT = 3 + 0.2(125) = 28 cycles

## Slide 6: Cache Read
0
1
2
K-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 7: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 8: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 9: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 10: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B
Notes: 1 fewer s bit, 2x fewer sets

## Slide 11: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 12: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B

## Slide 13: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid) and sum is stored in a register, calculate the miss rate:
  = 12 bits, = 256 B, = 32 B, = 2
#define SIZE 8
long ar[SIZE][SIZE], sum = 0; // &ar=0x800
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += ar[i][j];
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)

## Slide 14: What about writes?
Multiple copies of data exist:
  L1, L2, possibly L3, main memory
What to do on a write-hit?
  Write-through: write immediately to next level
  Write-back: defer write to next level until line is evicted (replaced)
    Must track which cache lines have been modified (“dirty bit”)
What to do on a write-miss?
  Write-allocate: (“fetch on write”) load into cache, update line in cache
    Good if more writes or reads to the location follow
  No-write-allocate: (“write around”) just write immediately to memory
Typical caches:
  Write-back + Write-allocate, usually
  Write-through + No-write-allocate, occasionally
Notes: Why? Reuse is common
  Typically you would read, then write (incr)
  Or after you initialize a value (say, to 0), likely read and write it again soon

## Slide 15: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
dirty bit
tag (there is only one set in this tiny cache, so the tag is the entire block address!)
In this example we are sort of ignoring block offsets. Here a block holds 2 bytes (16 bits, 4 hex digits).
Normally a block would be much bigger and thus there would be multiple items per block. While only one item in that block would be written at a time, the entire line would be brought into cache.
Contents of memory stored at address G
Notes: Valid bit not shown
Tiny cache, 1 set, tag is G
Dirty bit because write back

## Slide 16: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xCAFE
0xBEEF
0
F
G
STORE 0xFACE, F
dirty bit
Notes: Miss, need to maybe write back
But not dirty, so I don’t have to
Pull in F

## Slide 17: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xCAFE
0
Step 1: Bring F into cache
STORE 0xFACE, F
Notes: Pull in F, then write

## Slide 18: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
dirty bit
0xFACE
1
Step 2: Write 0xFACE to cache only and set dirty bit
STORE 0xFACE, F
Notes: Write, make dirty (write-back)

## Slide 19: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
mov 0xFEED, F
dirty bit
0xFACE
1
Write hit!
Write 0xFEED to cache only
STORE 0xFACE, F
Notes: Another write hit, don’t need to go to mem

## Slide 20: Write-back, write-allocate example
0xBEEF
U
0
0xCAFE
Cache
Memory
F
0xCAFE
0xBEEF
F
G
LOAD G, %t1
dirty bit
0xFEED
1
STORE 0xFEED, F
STORE 0xFACE, F
Notes: Read miss, and my line is dirty! Write back

## Slide 21: Write-back, write-allocate example
0xBEEF
Cache
Memory
G
0xFEED
0xBEEF
0
F
G
dirty bit
1. Write F back to memory since it is dirty 2. Bring G into the cache so we can copy it into %t1
LOAD G, %t1
STORE 0xFEED, F
STORE 0xFACE, F