## Slide 1: Processes
http://xkcd.com/1854/

## Slide 2: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 3: Leading Up to Processes
System Control Flow
  Control flow
  Exceptional control flow
  Asynchronous exceptions (interrupts)
  Synchronous exceptions (traps & faults)

## Slide 4: Control Flow
So far: we’ve seen how the flow of control changes as a single program executes
Reality: multiple programs running concurrently
  How does control flow across the many components of the system?
  In particular: More programs running than CPUs
Exceptional control flow is basic mechanism used for:
  Transferring control between processes and OS
  Handling I/O and virtual memory within the OS
  Implementing multi-process apps like shells and web servers
  Implementing concurrency

## Slide 5: Control Flow
Processors do only one thing:
  From startup to shutdown, a CPU simply reads and executes (interprets) a sequence of instructions, one at a time
  This sequence is the CPU’s control flow (or flow of control)
<startup>
instr1
instr2
instr3
…
instrn
<shutdown>
Physical control flow
time

## Slide 6: Altering the Control Flow
Up to now, two ways to change control flow:
  Jumps (conditional and unconditional)
  Call and return
  Both react to changes in program state
Processor also needs to react to changes in system state
  Unix/Linux user hits “Ctrl-C” at the keyboard
  User clicks on a different application’s window on the screen
  Data arrives from a disk or a network adapter
  Instruction divides by zero
  System timer expires
Can jumps and procedure calls achieve this?
  No – the system needs mechanisms for “exceptional” control flow!

## Slide 7: Exceptional Control Flow
Exists at all levels of a computer system
Low level mechanisms
  Exceptions
    Change in processor’s control flow in response to a system event (i.e. change in system state, user-generated interrupt)
    Implemented using a combination of hardware and OS software
Higher level mechanisms
  Process context switch
    Implemented by OS software and hardware timer
  Signals
    Implemented by OS software
    We won’t cover these – see CMPT 300

## Slide 8: Exceptions
An exception is transfer of control to the operating system (OS) kernel in response to some event (i.e. change in processor state)
  Kernel is the memory-resident part of the OS
  Examples: division by 0, page fault, I/O request completes, Ctrl-C
How does the system know where to jump to in the OS?
User Code
OS Kernel Code
exception
exception processing by exception handler, then:
return to current_instr,
return to next_instr, OR
abort
current_instr
next_instr
event

## Slide 9: Exception Table
A jump table for exceptions (also called Interrupt Vector Table)
  Each type of event has a unique exception number
  = index into exception table (a.k.a interrupt vector)
  Handler is called each time exception occurs
0
1
2
...
n-1
Exception
Table
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers
This is extra (non-testable) material
Notes: (Jump tables for switch statements: x86 Programming III slides)
The book calls this an Exception table. I am using that at the top of the slide to be consistent with the book and with the previous slide.

## Slide 10: Exception Table (Excerpt)
Exception Number | Description | Exception Class
0 | Divide error | Fault
13 | General protection fault | Fault
14 | Page fault | Fault
18 | Machine check | Abort
32-255 | OS-defined | Interrupt or trap
This is extra (non-testable) material
Notes: According to the book: Ones in gray are Intel-defined, Others are OS-defined
Intel® 64 and IA-32 Architectures Software Developer's Manual, Volume 1: Basic Architecture - Describes the architecture and programming environment of processors supporting IA-32 and Intel 64 Architectures.
“Systems often use an interrupt controller to group the device interrupts together before passing on the signal to a single interrupt pin on the CPU. This saves interrupt pins on the CPU…” http://www.tldp.org/LDP/tlk/dd/interrupts.html
This is why cat /proc/interrupts doesn’t match this slide - /proc/interrupts shows APIC’s “IRQ numbers”, not the OS’s exception numbers

## Slide 11: Leading Up to Processes
System Control Flow
  Control flow
  Exceptional control flow
  Asynchronous exceptions (interrupts)
  Synchronous exceptions (traps & faults)

## Slide 12: Asynchronous Exceptions (Interrupts)
Caused by events external to the processor
  Indicated by setting the processor’s interrupt pin(s) (wire into CPU)
  After interrupt handler runs, the handler returns to “next” instruction
Examples:
  I/O interrupts
    Hitting Ctrl-C on the keyboard
    Clicking a mouse button or tapping a touchscreen
    Arrival of a packet from a network
    Arrival of data from a disk
  Timer interrupt
    Every few milliseconds, an external timer chip triggers an interrupt
    Used by the OS kernel to take back control from user programs
Notes: Also:
  Hard reset interrupt
    hitting the reset button on front panel
  Soft reset interrupt
    hitting Ctrl-Alt-Delete on a PC

## Slide 13: Synchronous Exceptions
Caused by events that occur as a result of executing an instruction:
  Traps
    Intentional: transfer control to OS to perform some function
    Examples: system calls, breakpoint traps, special instructions
    Returns control to “next” instruction
  Faults
    Unintentional but possibly recoverable
    Examples: page faults, segment protection faults, integer divide-by-zero exceptions
    Either re-executes faulting (“current”) instruction or aborts
  Aborts
    Unintentional and unrecoverable
    Examples: parity error, machine check (hardware failure detected)
    Aborts current program

## Slide 14: Summary
Exceptions
  Events that require non-standard control flow
  Generated externally (interrupts) or internally (traps and faults)
  After an exception is handled, one of three things may happen:
    Re-execute the current instruction
    Resume execution with the next instruction
    Abort the process that caused the exception

## Slide 15: Processes
Processes and context switching
Creating new processes
  fork(), exec*(), and wait()
Zombies

## Slide 16: What is a process?
Process 1
CPU
Registers
%rip
Memory
Stack
Heap
Code
Data
Disk
Chrome.exe
It’s an illusion!

## Slide 17: What is a process?
Another abstraction in our computer system
  Provided by the OS
  OS uses a data structure to represent each process
  Maintains the interface between the program and the underlying hardware (CPU + memory)
What do processes have to do with exceptional control flow?
  Exceptional control flow is the mechanism the OS uses to enable multiple processes to run on the same system
What is the difference between:
  A processor? A program? A process?
Notes: The data structure is the process control block (PCB).

## Slide 18: Processes
A process is an instance of a running program
  One of the most profound ideas in computer science
  Not the same as “program” or “processor”
Process provides each program with two key abstractions:
  Logical control flow
    Each program seems to have exclusive use of the CPU
    Provided by kernel mechanism called context switching
  Private address space
    Each program seems to have exclusive use of main memory
    Provided by kernel mechanism called virtual memory
CPU
Registers
Memory
Stack
Heap
Code
Data

## Slide 19: What is a process?
Computer
Disk
/Applications/
Chrome.exe
Slack.exe
PowerPoint.exe
CPU
Process 2
Process 3
Process 4
Process 1
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
It’s an illusion!

## Slide 20: What is a process?
Computer
Disk
/Applications/
Chrome.exe
Slack.exe
PowerPoint.exe
CPU
Process 1
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 2
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 3
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 4
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Operating
System
It’s an illusion!

## Slide 21: Multiprocessing: The Illusion
Computer runs many processes simultaneously
  Applications for one or more users
    Web browsers, email clients, editors, …
  Background tasks
    Monitoring network & I/O devices
CPU
Registers
Memory
Stack
Heap
Code
Data
CPU
Registers
Memory
Stack
Heap
Code
Data
…
CPU
Registers
Memory
Stack
Heap
Code
Data

## Slide 22: Multiprocessing: The Reality
Single processor executes multiple processes concurrently
  Process executions interleaved, CPU runs one at a time
  Address spaces managed by virtual memory system (later in course)
  Execution context (register values, stack, …) for other processes saved in memory
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 23: Multiprocessing
Context switch
  Save current registers in memory
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 24: Multiprocessing
Context switch
  Save current registers in memory
  Schedule next process for execution
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 25: Multiprocessing
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…
Context switch
  Save current registers in memory
  Schedule next process for execution
  Load saved registers and switch address space

## Slide 26: Multiprocessing: The (Modern) Reality
Multicore processors
  Multiple CPUs (“cores”) on single chip
  Share main memory (and some of the caches)
  Each can execute a separate process
    Kernel schedules processes to cores
    Still constantly swapping processes
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…
CPU
Registers

## Slide 27: Concurrent Processes
Each process is a logical control flow
Two processes run concurrently (are concurrent) if their instruction executions (flows) overlap in time
  Otherwise, they are sequential
Example: (running on single core)
  Concurrent: A & B, A & C
  Sequential: B & C
Process A
Process B
Process C
time
Assume only one CPU

## Slide 28: User’s View of Concurrency
Control flows for concurrent processes are physically disjoint in time
  CPU only executes instructions for one process at a time
However, the user can think of concurrent processes as executing at the same time, in parallel
Assume only one CPU
Process A
Process B
Process C
time
Process A
Process B
Process C
User View

## Slide 29: Context Switching
Processes are managed by a shared chunk of OS code called the kernel
  The kernel is not a separate process, but rather runs as part of a user process
In x86-64 Linux:
  Same address in each process refers to same shared memory location
Assume only one CPU

## Slide 30: Context Switching
Processes are managed by a shared chunk of OS code called the kernel
  The kernel is not a separate process, but rather runs as part of a user process
Context switch passes control flow from one process to another and is performed using kernel code
Process A
Process B
user code
kernel code
user code
kernel code
user code
context switch
context switch
time
Exception
Assume only one CPU

## Slide 31: Processes
Processes and context switching
Creating new processes
  fork() , exec*(), and wait()
Zombies

## Slide 32: Creating New Processes & Programs
Process 2
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Chrome.exe
Process 1
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
fork()
exec*()

## Slide 33: Creating New Processes & Programs
fork-exec model (Linux):
  fork() creates a copy of the current process
  exec*() replaces the current process’ code and address space with the code for a different program
    Family: execv, execl, execve, execle, execvp, execlp
  fork() and execve() are system calls
Other system calls for process management:
  getpid()
  exit()
  wait(), waitpid()
Notes: Review: system calls are traps (intentional exception).
http://en.wikipedia.org/wiki/Fork-exec: “Microsoft Windows does not support the fork-exec model, as it does not have a system call analogous to fork(). The spawn() family of functions declared in process.h can replace it in cases where the call to fork() is followed directly by exec().”

## Slide 34: fork: Creating New Processes
pid_t fork(void)
  Creates a new “child” process that is identical to the calling “parent” process, including all state (memory, registers, etc.)
  Returns 0 to the child process
  Returns child’s process ID (PID) to the parent process
Child is almost identical to parent:
  Child gets an identical (but separate) copy of the parent’s virtual address space
  Child has a different PID than the parent
fork is unique (and often confusing) because it is called once but returns “twice”
pid_t pid = fork();
if (pid == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}

## Slide 35: Understanding fork()
Process X (parent; PID X)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
Process Y (child; PID Y)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}

## Slide 36: Understanding fork()
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
fork_ret = Y
Process X (parent; PID X)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
Process Y (child; PID Y)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
fork_ret = 0

## Slide 37: Understanding fork()
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
Process X (parent; PID X)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
Process Y (child; PID Y)
pid_t fork_ret = fork();
if (fork_ret == 0) {
printf("hello from child\n");
} else {
printf("hello from parent\n");
}
hello from parent
hello from child
Which one appears first?
fork_ret = Y
fork_ret = 0

## Slide 38: Summary
Processes
  At any given time, system has multiple active processes
  On a one-CPU system, only one can execute at a time, but each process appears to have total control of the processor
  OS periodically “context switches” between active processes
    Implemented using exceptional control flow
Process management
  fork: one call, two returns
  execve: one call, usually no return
  wait or waitpid: synchronization
  exit: one call, no return