## Slide 1: Virtual Memory III
https://xkcd.com/648/

## Slide 2: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory requesting data
5) Cache/memory sends data to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU

## Slide 3: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 4: Hmm… Translation Sounds Slow
The MMU accesses memory twice: once to get the PTE for translation, and then again for the actual memory request
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 1-3 cycles
What can we do to make this faster?
  Solution: add another cache! 🎉

## Slide 5: Speeding up Translation with a TLB
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
    Split VPN into TLB Tag and TLB Index based on # of sets in TLB
  Maps virtual page numbers to physical page numbers
  Stores page table entries for a small number of pages
    Modern Intel processors have 128 or 256 entries in TLB
  Much faster than a page table lookup in cache/memory
Virtual Page Number
Page offset
TLBT
TLBI
TLB
PTE
TLBT
PTE
PTE
PTE
Set
0
1
V
TLBT
V
TLBT
V
V
TLBT
Notes: “The architecture of the IBM System/370” R.P. Case and A. Padegs Communications of the ACM. 21:1, 73-96, January 1978.
Perhaps the first paper to use the term translation lookaside buffer. The name arises from the historical name for a cache, which was a lookaside buffer as called by those developing the Atlas system at the University of Manchester; a cache of address translations thus became a translation lookaside buffer. Even though the term lookaside buffer fell out of favor, TLB seems to have stuck, for whatever reason.
“x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 6: TLB Hit
A TLB hit eliminates a memory access!
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
TLB
VPN
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→

## Slide 7: TLB Miss
A TLB miss incurs an additional memory access (the PTE)
  Fortunately, TLB misses are rare
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
Notes: Does a TLB miss require disk access?

## Slide 8: Fetching Data on a Memory Read
Check TLB
  Input: VPN, Output: PPN
  TLB Hit: Fetch translation, return PPN
  TLB Miss: Check page table (in memory)
    Page Table Hit: Load page table entry into TLB
    Page Fault: Fetch page from disk to memory, update corresponding page table entry, then load entry into TLB
Check cache
  Input: physical address, Output: data
  Cache Hit: Return data value to processor
  Cache Miss: Fetch data value from memory, store it in cache, return it to processor

## Slide 9: Address Translation
Virtual Address
TLB Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Hit
Miss
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 10: Address Manipulation
Page offset
Page Offset
Virtual Page Number
TLB Index
request from CPU:
-bit physical address:
split to access TLB:
(on TLB miss) access PT:
-bit virtual address
Page offset
Physical Page Number
Offset
Cache Index
TLB Tag
Cache Tag
split to access cache:
TRANSLATION
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 11: Context Switching Revisited
What needs to happen when the CPU switches processes?
  Registers:
    Save state of old process, load state of new process
    Including the Page Table Base Register (PTBR)
  Memory:
    Nothing to do! Pages for processes already exist in memory/disk and protected from each other
  TLB:
    Invalidate all entries in TLB – mapping is for old process’ VAs
  Cache:
    Can leave alone because storing based on PAs – good for shared data

## Slide 12: Summary of Address Translation Symbols
Basic Parameters
  Number of addresses in virtual address space
  Number of addresses in physical address space
  Page size (bytes)
Components of the virtual address (VA)
  VPO Virtual page offset
  VPN Virtual page number
  TLBI TLB index
  TLBT TLB tag
Components of the physical address (PA)
  PPO Physical page offset (same as VPO)
  PPN Physical page number

## Slide 13: Address Translation
VM is complicated, but also elegant and effective
  Level of indirection to provide isolated memory & caching
  TLB as a cache of page tables avoids two trips to memory for every memory access
Virtual Address
TLB
Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 14: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Virtual Page Number
Virtual Page Offset
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
Physical Page Number
Physical Page Offset

## Slide 15: Simple Memory System: Page Table
Only showing first 16 entries (out of _____)
  Note: showing 2 hex digits for PPN even though only 6 bits
  Note: other management bits not shown, but part of PTE
VPN | PPN | Valid
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | Valid
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: Size of page table = 2^(n-p) entries

## Slide 16: Simple Memory System: TLB
16 entries total
4-way set associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Why does the TLB ignore the page offset?
Notes: Calculate VPN for valid TLB entry using Tag & Set

## Slide 17: Simple Memory System: Cache
Direct-mapped with = 4 B, = 16
Physically addressed
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
Note: It is just coincidence that the PPN is the same width as the cache Tag
Index | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –

## Slide 18: Current State of Memory System
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: TLB and Cache are separate pieces of hardware; page table stored in memory
Show correlation between TLB & page table (VPN 0x0D and 0x0F in particular)

## Slide 19: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 20: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, page fault

## Slide 21: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, Page Table Hit, Cache Miss

## Slide 22: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 23: Memory Overview
Disk
Main memory
(DRAM)
Cache
CPU
Page
Page
Line
Block
requested 32-bits
LD t1, 0 (sp)
TLB
MMU

## Slide 24: Practice VM Question
Our system has the following properties
  1 MiB of physical address space
  4 GiB of virtual address space
  32 KiB page size
  4-entry fully associative TLB with LRU replacement
Fill in the following blanks:
________ | Entries in a page table | ________ | Minimum bit-width of PTBR
________ | TLBT bits | ________ | Max # of valid entries in a page table

## Slide 25: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
What is the largest stride (in bytes) between successive memory accesses (in the VA space)?

## Slide 26: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
Assuming all of mat[] starts on disk, what are the following hit rates for the execution of the for-loop?
________ | TLB Hit Rate | ________ | Page Table Hit Rate

## Slide 27: Page Table Reality
Just one issue… the numbers don’t work out for the story so far!
The problem is the page table for each process:
  Suppose 64-bit VAs, 8 KiB pages, 8 GiB physical memory
  How many page table entries is that?
  About how long is each PTE?
  Moral: Cannot use this naïve implementation of the virtual→physical page mapping – it’s way too big
This is extra (non-testable) material
Notes: 2^64/2^13 = 2^51
PPN = 20 bits; plus Valid, R/W/X; so ~ 3 B per PTE
So each page table takes up 2^52 + 2^51 B!

## Slide 28: A Solution: Multi-level Page Tables
Page table base register
(PTBR)
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
Virtual Address
Physical Address
...
...
Level 1
page table
Level 2
page table
Level k
page table
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→
This is called a page walk
This is extra (non-testable) material

## Slide 29: Multi-level Page Tables
A tree of depth where each node at depth has up to children if part of the VPN has bits
Hardware for multi-level page tables inherently more complicated
  But it’s a necessary complexity – 1-level does not fit
Why it works: Most subtrees are not used at all, so they are never created and definitely aren’t in physical memory
  Parts created can be evicted from cache/memory when not being used
  Each node can have a size of ~1-100KB
But now for a -level page table, a TLB miss requires cache/memory accesses
  Fine so long as TLB misses are rare – motivates larger TLBs
This is extra (non-testable) material