## Slide 1
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
You may learn the material just by doing other coursework, but hopefully these slides will help clarify the material.
BONUS SLIDES

## Slide 2: C to RISCV Practice
Let’s put our all of our new RISCV knowledge to use in an example: “Fast String Copy”
C code is as follows:
/* Copy string from p to q */
char *p, *q;
while((*q++ = *p++) != ‘\0’) ;
What do we know about its structure?
  Single while loop
  Exit condition is an equality test

## Slide 3: C to RISCV Practice
Start with code skeleton:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
# t0 = *p
# *q = t0
# p = p + 1
# q = q + 1
# if *p==0, go to Exit
# go to Loop

## Slide 4: C to RISCV Practice
Fill in lines:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # t0 = *p
sb $t0,0($s1) # *q = t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
lb t0,0(s0)
sb t0,0(s1)
addi s0,s0,1
addi s1,s1,1
beq t0,0,Exit

## Slide 5: C to RISCV Practice
Finished code:
# copy String p to q
# p→$s0, q→$s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
beq t0,x0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
Notes: Is this the only way to write out this function? Of course not.

## Slide 6: C to RISCV Practice
Alternate code using bne:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
bne t0,x0,Loop # if *p!=0, go to Loop
# N chars in p => N*5 instructions
Notes: Used fewer instructions!
Instead of “exit when equal to zero”, we are now using “loop when not equal to zero.”

## Slide 7: RISCV Arithmetic Instructions
Multiplication (mul and mulh)
  mul dst, src1, src2
  mulh dst, src1, src2
  src1*src2: lower 32-bits through mul, upper 32-bits in mulh
Division (div)
  div dst, src1, src2
  rem dst, src1, src2
  src1/src2: quotient via div, remainder via rem

## Slide 8: RISCV Bitwise Instructions
Note: a→s1, b→s2, c→s3
Instruction | C | RISCV
And | a = b & c; | and s1,s2,s3
And Immediate | a = b & 0x1; | andi s1,s2,0x1
Or | a = b ¦ c; | or s1,s2,s3
Or Immediate | a = b ¦ 0x5; | ori s1,s2,0x5
Exclusive Or | a = b ^ c; | xor s1,s2,s3
Exclusive Or Immediate | a = b ^ 0xF; | xori s1,s2,0xF

## Slide 9: Shifting Instructions
In binary, shifting an unsigned number left is the same as multiplying by the corresponding power of 2
  Shifting operations are faster
  Does not work with shifting right/division
Logical shift: Add zeros as you shift
Arithmetic shift: Sign-extend as you shift
  Only applies when you shift right (preserves sign)
Shift by immediate or value in a register

## Slide 10: Shifting Instructions
Instruction Name | RISCV
Shift Left Logical | sll s1,s2,s3
Shift Left Logical Imm | slli s1,s2,imm
Shift Right Logical | srl s1,s2,s3
Shift Right Logical Imm | srli s1,s2,imm
Shift Right Arithmetic | sra s1,s2,s3
Shift Right Arithmetic Imm | srai s1,s2,imm
When using immediate, only values 0-31 are practical
When using variable, only lowest 5 bits are used (read as unsigned)

## Slide 11: Shifting Instructions
# sample calls to shift instructions
addi t0,x0 ,-256 # t0=0xFFFFFF00
slli s0,t0,3 # s0=0xFFFFF800
srli s1,t0,8 # s1=0x00FFFFFF
srai s2,t0,8 # s2=0xFFFFFFFF
addi t1,x0 ,-22 # t1=0xFFFFFFEA
# low 5: 0b01010
sll s3,t0,t1 # s3=0xFFFC0000
# same as slli s3,t0,10

## Slide 12: Shifting Instructions
Example 1:
# lb using lw: lb s1,1(s0)
lw s1,0(s0) # get word
andi s1,s1,0xFF00 # get 2nd byte
srli s1,s1,8 # shift into lowest

## Slide 13: Shifting Instructions
Example 2:
# sb using sw: sb s1,3(s0)
lw t0,0(s0) # get current word
andi t0,t0,0xFFFFFF # zero top byte
slli t1,s1,24 # shift into highest
or t0,t0,t1 # combine
sw t0,0(s0) # store back

## Slide 14: Shifting Instructions
Extra for Experts:
  Rewrite the two preceding examples to be more general
  Assume that the byte offset (e.g. 1 and 3 in the examples, respectively) is contained in s2
Hint:
  The variable shift instructions will come in handy
  Remember, the offset can be negative

## Slide 15: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
Implemented with:
  Jump table
  Indirect jump instruction
long switch_ex
(long x, long y, long z)
{
long w = 1;
switch (x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 16: Jump Table Structure
Code
Block 0
Targ0:
Code Block 1
Targ1:
Code Block 2
Targ2:
Code Block n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
target = JTab[x];
goto target;
switch (x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 17: Jump Table Structure
switch (x) {
case 1: <some code>
break;
case 2: <some code>
case 3: <some code>
break;
case 5:
case 6: <some code>
break;
default: <some code>
}
Code
Blocks
Memory
Use the jump table when x 6:
if (x <= 6)
target = JTab[x];
goto target;
else
goto default;
C code:
0
1
2
3
4
5
6
Jump
Table

## Slide 18: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
declaring data, not instructions
8-byte memory alignment
this data is 64-bits wide
Notes: .rodata – read-only data section