## Slide 1: Combinational Logic Sequential Logic CPU Datapath
CMPT 295 Week 10

## Slide 2: Combinational Logic

## Slide 3: Hardware Design
This week’s goals:
1. Understand how processors work
  Requires digital systems knowledge
2. Understand how code is actually executed on a computer to analyze reliability, performance & security
Layered abstractions
  Transistors → Gates → Combinational Logic → Sequential Logic → Processors → Machine Language → Assembly → High-level Programming Languages → Application programs
  At each step we can “abstract away” the lower layers

## Slide 4: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    High/Low voltage represent True/False, 1/0
Hardware of a processor (e.g., RISC-V) is an example of a Synchronous Digital System

## Slide 5: Moore’s Law
Original Version (1965): Since the integrated circuit was invented, the number of transistors in an integrated circuit has roughly doubled every year; this trend would continue for the foreseeable future
1975: Revised - circuit complexity doubles every two years

## Slide 7: Moore’s Law
Original Version (1965): Since the integrated circuit was invented, the number of transistors in an integrated circuit has roughly doubled every year; this trend would continue for the foreseeable future
1975: Revised - circuit complexity doubles every two years
Hardware Trend: Hardware gets more powerful every year (due to technology advancement and the hard work of many engineers)
Software Trend: Software gets faster and uses more resources (And has to keep up with ever-changing hardware)
Digital circuits are used to build hardware

## Slide 8: Transistors to Gates Example: Inverter
CMOS technology
Two transistors:
  NMOS (top): turns on when input is 0 (low V)
  PMOS (bottom): turns on when input is 1 (high V)
IN
OUT
GND
VDD

## Slide 9: Transistors to Gates Example: Inverter
Input = 0
Top transistor turned on, bottom transistor turned off -> Output connected to VDD, capacitor charged
Output = 1
0
1
GND
VDD

## Slide 10: Transistors to Gates Example: Inverter
Input = 1
Top transistor turned off, bottom transistor turned on -> Output connected to GND, capacitor discharged
Output = 0
1
0
GND
VDD
Inverter is commonly called “NOT gate”

## Slide 11: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 12: Simple Logic Gates
Special names and symbols:
NOT
AND
OR
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | A OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | NOT a
0 | 1
1 | 0
Circle means NOT!
= NOT a
= a AND b
= a OR b
True if input is false
True if both inputs are true
True if at least one input is true
Truth Table
12

## Slide 13: More Simple Logic Gates
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | a NOR b
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | a NAND b
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
= a NAND b
= a NOR b
= a XOR b
True if both inputs are false
True if exactly one input is true
(or if odd number of inputs are true for > 2 inputs)
True if at least one input is false

## Slide 14: Combining Multiple Logic Gates
A
B
C
D
D = (NOT(A AND B)) AND (A OR (NOT B AND C))

## Slide 15: How to Represent Combinational Logic?
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 16: Truth Tables
Table that relates the inputs to a combinational logic circuit to its output
  Output only depends on current inputs
  Use abstraction of 0/1 (F/T) instead of high/low Voltage
  Shows output for every possible combination of inputs
How big is a truth table with N inputs?
  0 or 1 for each of N inputs, so 2N rows

## Slide 17: N-input Truth Tables
F
Y
A
B
C
For N inputs, how many distinct functions F do we have?
Function maps each row to 0 or 1, so possible functions
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Y
F(0,0,0)
F(0,0,1)
F(0,1,0)
F(0,1,1)
F(1,0,0)
F(1,0,1)
F(1,1,0)
F(1,1,1)
0
1
0
0
0
1
1
0
Notes: Circle the output, use variables/animations, talk about the output as a bit combination (integer?) Maybe 3 inputs?

## Slide 18: Truth Tables with Multiple Outputs
For 3 outputs, just three indep. functions: X(A,B,C,D), Y(A,B,C,D), and Z(A,B,C,D)
  Can show functions in separate columns (no additional rows)
F
Y
A
B
C
D
X
Z

## Slide 19
Question: Which of the columns A-D is the correct output of the Truth Table for: (X XOR Y) OR (NOT Z)
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 20
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1
Question: Which of the columns A-D is the correct output of the Truth Table for: (X XOR Y) OR (NOT Z)

## Slide 21: More Complex Truth Tables
3-Input Majority
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
2-bit Adder
A |  | B |  | C |  | 
a1 | a0 | b1 | b0 | c2 | c1 | c0
 |  |  | . |  |  | 
 |  |  | . |  |  | 
 |  |  | . |  |  | 
+
c1
a1
a0
b1
b0
c2
c0
How many
rows?

## Slide 22: Truth Tables Don’t Scale
Truth tables are huge
  Write out EVERY combination of inputs and outputs (thorough, but inefficient)
  Finding a particular combination of inputs involves scanning a large portion of the table
Boolean Algebra is a shorter way to represent combinational logic

## Slide 23: Boolean Algebra
Represent inputs and outputs as variables
  Each variable can only take on the value 0 or 1
Overbar, ¬, ’ mean NOT: “logical complement”
  e.g., if A = 0, A = 1. If A = 1, then A = ¬A = A’ = 0
Plus (+) is 2-input OR: “logical sum”
Product (·) is 2-input AND: “logical product”
  Sometimes omitted
All other gates and logical expressions can be built from combinations of these
AB + AB == (NOT(A AND B)) OR (A AND (NOT B))

## Slide 24: Laws of Boolean Algebra
These laws allow us to simplify Boolean expressions:
Notes: Demorgan’s law example

## Slide 25: Converting Truth Table to Boolean Expression
We can show that these are equivalent!
Read off of table
  For 1, write variable name
  For 0, write complement of variable
Sum of Products (SoP)
  Take rows with 1’s in output column, sum products of inputs
  c=
Product of Sums (PoS)
  Take rows with 0’s in output column, product the sum of the complements of the inputs
  c =
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a
b
+
a
b
(a + b) · (a + b)
Notes: Choice between the two generally comes down to whether the output function has more 0’s or 1’s. Choosing the conversion (SoP/PoS) with less items will result in a shorter expression!
(This example happens to be balanced: 2 0’s and 2 1’s)

## Slide 26: Simplifying Boolean Expressions
Logic Delay: Everything we are dealing with is just an abstraction of transistors and wires
  Inputs propagating to the outputs are voltage signals passing through transistor networks
  There is always some delay before a CL’s output updates to reflect the inputs
  Critical Path is longest delay from any input to output. Could be represented as “n gate delays”
Simpler Boolean expressions ↔ smaller transistor networks ↔ smaller circuit delays ↔ faster hardware

## Slide 27: Simplifying Boolean Expressions: Example
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = b
= ab + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 28: Karnaugh Maps
Used to simplify Boolean expressions of 2-4 variables
Table composed of squares each representing a unique combination of all variable (1 if true, else blank)
Two variable Map:
0
1
0
1
x + y
Example: Boolean Expression?
x | y | ?
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 29: Three Variable Karnaugh Maps
0
1
Question: Simplify

## Slide 30: Example: Simplify 3-Variable Expression
 | 1 | 1 | 1
 | 1 | 1 | 
0
1
Question: Simplify
Answer:

## Slide 31: Four Variable Karnaugh Maps
00
01
11
10
Question: Simplify

## Slide 32: Example: Simplify 4-Variable Expression
 | 1 | 1 | 1
 | 1 | 1 | 1
 |  | 1 | 
 |  | 1 | 1
00
01
11
10
Simplify
Solution:

## Slide 33: Useful Combinational Circuits

## Slide 34: Data Multiplexor (MUX)
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this input has n bits
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 35: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
A
B
S
0
1
C
‘n
‘n
‘n
s

## Slide 36: 1-bit 4-to-1 MUX
Schematic:
Truth Table: How many rows?
Boolean Expression: E = S1S0A + S1S0B + S1S0C + S1S0D
26
A
D
S= S1S0
00
11
E
‘2
01
10
B
C

## Slide 37: Another Design for 4-to-1 MUX
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:
A
B
0
1
C
D
S0
0
1
S1
0
1
E

## Slide 38: Decoder
Enable one of 2N outputs based on N input
Example: 2-to-4 decoder
Use case: Choose ALU operation based on instruction op-code
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 39: Demultiplexer (Demux)
Similar to decoder with an enable signal
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 40: Single-Bit Binary Adder (Half Adder)
Add A + B to get Sum (S) and Carry (C)
Truth Table:
Boolean Expressions:
  S = AB; C = AB
Circuit:
By inductiveload - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1023090
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 41: What is this Circuit?
S = A ⊕ B ⊕ C; C = AB + C(A ⊕ B)
0
1
1
0
1
0
0
1
Truth table:
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
1
1
1
3-bit
Addition!
A
B
C
Q. What’s the propagation delay?
C
S
3 gate delays (highlighted)
Q. What does the circuit accomplish?
Algebra:
S = A ⊕ B ⊕ C
C S
Full Adder
Half Adder
Half Adder
FA
S
C
C
A
B

## Slide 42: Computing with Combinational Circuits
Definition: A combinational circuit computes a pure function, i.e., its outputs react only based on its inputs. There are no feedback loops and no state information (memory) is maintained.
Theorem: Every Boolean function can be implemented with NAND and NOT. Circuits are modular
FA
FA
FA
FA
A3
B3
A2
B2
A1
B1
A0
B0
S3
S2
S1
S0
C3
C2
C1
C0
C4
… a 4-bit ripple carry adder!
  Adds by columns
  Propagation delay
= 9
(2n + 1)
Adder-4
A
B
4
4
4
S
C
C
Notes: Orally: We used to spend ⅔ of CMPT 150 on the design techniques to minimize circuit size, gate delay, etc …
The point in CMPT 295 is only that it is possible to do so, and that gate delay is a thing
Orally: This is why additions is slow. And why mul is even slower.
Orally: How to make an Adder-8?

## Slide 43: Functional Unit
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A + 1
1101 B
32
Hardware circuits are fixed
Can’t adjust wires / gates while running
Build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:

## Slide 44: Functional Unit: Adder-Subtractor
32
Adder-32
32
32
A
32
B
S
C
FS
if FS == 0 then
S = A + B
if FS == 1 then
= A − B
S = A + B + 1

## Slide 45: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 46: Sequential Logic

## Slide 47: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 48: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: ‘S=0’?
Feedback
X
+
S

## Slide 49: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder
Xi
+
S
register
Load/Clk
reset

## Slide 50: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISCV)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 51: Registers
Same as registers in assembly:
Small memory storage locations
Clock input (inputs active only on a clock “tick”)
Data input (can be various bit widths)
Data output (can be various bit widths)
Reset (sets value to zero)
Write Enable (can it be written to?)

## Slide 52: First State Element: RS Latch
By Napalm Llama - Modification of Wikimedia Commons file R-S.gif (shown below), CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=4845402
When R = 1 and S = 0 → Q is 0
When S = 1 and R = 0 → Q is 1
When both S and R are 0 → Q stays the same
When both S and R are 1 → Undefined
Recall:
NOR outputs 1 if
both inputs are 0

## Slide 53: RS Latch with Enable
Only changes state when E = 1.
Stays the same when E = 0
By Inductiveload - Own Drawing in Inkscape 0.43, Public Domain, https://commons.wikimedia.org/w/index.php?curid=873598

## Slide 54: D Latch
Avoids undefined state of RS Latch when R=S=1
Q is set to D when E = 1; Q stays the same when E = 0
By Inductiveload - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=6712572
Circuit
By Inductiveload - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=6712594
Schematic

## Slide 55: D Flip-Flop
Changes state only on falling edge of Clock (i.e., Clock changes from 1 to 0)
Use Clock to change on rising edge
By Nolanjshettle at English Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=40852395

## Slide 56: Signals and Waveforms: Clocks
Signals transmitted over wires continuously
Transmission is effectively instantaneously
  Implies that any wire only contains one value at any given time
Rising Edge
Falling Edge
Clock period (CPU cycle time)
T
T =
Time
Voltage
High
Low

## Slide 57: Dealing with Waveform Diagrams
Easiest to start with CLK on top
  Solve signal by signal, from inputs to outputs
  Can only draw the waveform for a signal if all of its input waveforms are drawn
When does a signal update?
  A state element updates based on CLK triggers
  A combinational element updates ANY time ANY of its inputs changes

## Slide 58: Accumulator 2nd Try: How About This?
Delay through Adder
Xi
+
S
register
Load/Clk
reset
Load/Clk
X0
X0+X1
X0+X1+X2
X0+X1+X2+X3
X0
X1
X2
X3
Xi
S
Time

## Slide 59: Register Internals
N-bit register  n instances of a “Flip-Flop”
  Output flips and flops between 0 and 1
Specifically this is a “D-type Flip-Flop”
  D is “data input”, Q is “data output”
  A group of wires when interpreted as a bit field is called a bus
FF
d0
q0
CLK
FF
d1
q1
CLK
FF
dn-1
qn-1
CLK
Register
D (n-bit)
Q(n-bit)
CLK
…


## Slide 60: Flip-Flop Timing Behavior
FF
d
q
CLK

## Slide 61
Setup Time
FF
d
q
CLK
Flip-Flop Timing Behavior

## Slide 62
Hold Time
FF
d
q
CLK
Flip-Flop Timing Behavior

## Slide 63
Clock-to-Q
Flip-Flop Timing Behavior
FF
d
q
CLK

## Slide 64: Accumulator Revisited: Proper Timing
Reset signal shown
In practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
Xi
+
Si
register
Clk
reset
Si-1
“Undefined” (unknown) signal
X0
X0+X1
X0+X1+X2
X0+X1+X2+X3
X0
X1
X2
X3
Xi
Si
0
X0
X0+X1
X0+X1 +X2
Si-1
Reset
CLK

## Slide 65: Timing Terms
Clock: Steady square wave that synchronizes system
Register: Several bits of state that samples on rising edge of Clock (positive edge-triggered); also has RESET
Setup Time: When input must be stable before Clock trigger
Hold Time: When input must be stable after Clock trigger
Clock-to-Q Delay: How long it takes output to change from Clock trigger
Notes: STOP HERE

## Slide 66: Digital State Machines
Memory holds state information
memory
combinational
circuit
current
state
inputs
next state
outputs
compute next state based on (current state, inputs)
compute outputs based on (current state, inputs)
Q. What does this imply about the clock period?
clock period must exceed (tpd of combinational circuit + tpd of registers) where tpd is propagational delay

## Slide 67: Waveform Example: RS Latch
By Napalm Llama - Modification of Wikimedia Commons file R-S.gif (shown below), CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=4845402
Q
R
S
Time
a | b | a NOR b
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 68: Waveform Example: D Flip-Flop
Q
D
Time
By Nolanjshettle at English Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=40852395
Clock

## Slide 69: CPU Hardware
Goal: Given an instruction set architecture, construct a machine that reliably executes instructions.
Design choices will influence speed of instructions:
Some instructions will be faster than others
Order of instructions may matter
Order of memory accesses may matter
“conflicts” or “hazards”

## Slide 70: Model for Synchronous Systems
Combinational logic blocks separated by registers
  Clock signal connects only to sequential logic elements
  Feedback is optional depending on application
How do we ensure proper behavior?
  How fast can we run our clock?

## Slide 71: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 72: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register
72

## Slide 73: How to get faster clock frequency?
Pipelining!
Split operation into smaller parts and add registers between each two consecutive parts (next week).

## Slide 74: RISC-V CPU Datapath, Control Intro
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 75: CPU Design Principles
Analyze instruction set → datapath requirements
Select set of datapath components & establish clock methodology
Assemble datapath meeting the requirements
Analyze implementation of each instruction to determine setting of control points that effects the register transfer
Assemble the control logic
  Formulate Logic Equations
  Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 76: RISC-V Single-Cycle CPU
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF (Instruction Fetch), ID (Instruction Decode), EX (Execute), MEM (Memory), WB (Write Back)
  Not all instructions are active in all phases (except for loads!)
Controller specifies how to execute instructions

## Slide 77: RISC-V CPU in two parts
Central Processing Unit (CPU):
  Datapath: Contains the hardware necessary to perform operations required by the processor
    Reacts to what the controller tells it. (i.e., “I was told to do an add, so I”ll feed these arguments through an adder)
  Control: Decides what each piece of the datapath should do
    What operation am I performing? Do I need to get info from memory? Should I write to a register? Which register?
    Has to make decisions based on the input instruction only.

## Slide 78: Design Principles
Determining control signals
  Any time a datapath element has an input that changes behavior, it requires a control signal (e.g. ALU operation, read/write)
  Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector (e.g. next PC, ALU input, register to write to)
Control signals will change based on exact datapath
Datapath will change based on ISA

## Slide 79: Storage Element: Register File
Register File consists of 32 registers:
  Output ports portA and portB
  Input port portW
Register selection
  Place data of register RA (number) onto portA
  Place data of register RB (number) onto portB
  Store data on portW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK is passed to all internal registers so they can be written to if they match RW and Write Enable is 1
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 80: Implementing R-Types
Perform operation
New hardware: ALU (Arithmetic Logic Unit)
Abstraction for adders, multipliers, dividers, etc.
How do we know what operation to execute?
  Our first control bit! ALUSel(ect)
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel = add
inst[31:0]
31
0
func7(7)
opcode(7)
rs2(5)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
25 24

## Slide 81: Implementing R-Types
ALUSel = add
Perform operation
Write ALU result to rd
Control
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
inst[31:0]
31
0
func7(7)
opcode(7)
rs2(5)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
25 24
DataD
RegWEn=1
alu
ALUSel = add

## Slide 82: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel
31
0
imm(12)
opcode(7)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
82
alu

## Slide 83: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb
31
0
offset(12)
opcode
base
width
dst
7 6
12 11
15 14
20 19

## Slide 84: Storage Element: Idealized Memory
Memory (idealized)
  One input port: Data In
  One output port: Data Out
Memory access:
  Read: Write Enable = 0, data at Address is placed on Data Out
  Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: Address valid → Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

## Slide 85: Current Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
ALU
mem
wb
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
BSel
ALUSel
MemRW
WBSel
wb
pc+4

## Slide 86: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”
31
0
imm(11:5)
opcode
rs2
rs1
func3
imm(4:0)
7 6
12 11
15 14
20 19
25 24
86

## Slide 87: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb
31
0
imm(12|10:5)
opcode
rs2
rs1
func3
imm(4:1|11)
7 6
12 11
15 14
20 19
25 24
87

## Slide 88: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb
31
0
offset
opcode
base
Func3
dest
7 6
12 11
15 14
20 19
Writes PC+4 to dest (return address)
Sets PC = base + offset
88

## Slide 89: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb
imm[20|10:1|11|19:12]
opcode
rd
31
0
jal saves PC+4 in register rd (the return address)
Set PC = PC + offset (PC-relative jump)
7 6
12 11
89

## Slide 90: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc
imm[31:12]
opcode
rd
31
0
lui writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits
7 6
12 11
90

## Slide 91: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc
imm[31:12]
opcode
rd
31
0
Adds upper immediate value to PC and places result in destination register
7 6
12 11
91