## Slide 1: Combinational Logic Sequential Logic CPU Datapath
CMPT 295 Week 10

## Slide 2: Software vs. Hardware
Hardware is all about signals (0/1) flowing through gates.
  Each gate/block is like a pure function.
Wires are the “plumbing” that move signals between blocks (ala. Args or return values)
Larger circuits are built up by combining blocks, just like software is built by calling functions
Memory elements (flip-flops, registers) hold state, much like variables do in code (more on this later…).
 | Software | Hardware
Basic operation | Functions (input → output) | Gates/Block (I/O wires)
Wiring | Function calls or passing arguments | Wires that carry 0/1 signals between gates
Composition | Compose functions f(g(x)) | Organize flow of blocks
State | Variables, memory | Flip-flops, registers
Execution | Step-by-step | Continous flow except at clocked edge (more later)
tmp1 = f1(arg1)
tmp2 = f2(tmp1)
tmp3 = f3(tmp2)
return f(tmp1,tmp2,tmp3)
arg1
f1()
f2()
f3()
return
tmp1
tmp2
tmp3

## Slide 3: Software vs. Hardare
No conditional statements
Software
Hardware
  Do all statements and pick
switch (instruction.rtype.funct3) {
case 0x0:
switch (instruction.rtype.funct7) {
case 0x0:
// Add
processor->R[instruction.rtype.rd] =
((sWord)processor->R[instruction.rtype.rs1]) +
((sWord)processor->R[instruction.rtype.rs2]);
break;
case 0x1:
// Mul
processor->R[instruction.rtype.rd] =
((sWord)processor->R[instruction.rtype.rs1]) *
((sWord)processor->R[instruction.rtype.rs2]);
break;
Tmp1 =
((sWord)processor->R[instruction.rtype.rs1]) +
((sWord)processor->R[instruction.rtype.rs2]);
// Mul
Tmp2 =
((sWord)processor->R[instruction.rtype.rs1]) *
((sWord)processor->R[instruction.rtype.rs2]);
Select(tmp1,tmp2….) # SEL

## Slide 4
Field | Shared Among | Bits | Notes
instr[31] | I/S/B/J | sign bit | sign-extend source
instr[30:25] | I/S/B | high field | common for load/store/branch
instr[11:7] | S | low field | destination offset
instr[19:12] | U/J | upper byte | long immediates
instr[20] | I/J | single control bit | mid-immediate for JAL/JALR
int32_t getImmediate(uint32_t instr) {
// Common bitfields
uint32_t ins_31 = (instr >> 31) & 0x1; // sign bit
uint32_t ins_30_= (instr >> 25) & 0x3F; // shared upper field for I/S/B
uint32_t ins_24_21 = (instr >> 21) & 0xF; // used in J-type
uint32_t ins_20 = (instr >> 20) & 0x1; // shared mid-bit (I/J)
uint32_t ins_19_12 = (instr >> 12) & 0xFF; // U/J upper byte
uint32_t ins_11_8 = (instr >> 8) & 0xF; // B-type middle nibble
uint32_t ins_7 = (instr >> 7) & 0x1; // S/B lower link
imm_i = ins_31 << 11 | (ins_30_25 << 5) | (ins_20 << 4) | ((instr >> 21) & 0xF);
imm_s = (ins_30_25 << 5) | ((instr >> 7) & 0x1F);

## Slide 5: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    High/Low voltage represent True/False, 1/0
Hardware of a processor (e.g., RISC-V) is an example of a Synchronous Digital System

## Slide 6: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 7: Simple Logic Gates
Special names and symbols:
NOT
AND
OR
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | A OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | NOT a
0 | 1
1 | 0
Circle means NOT!
= NOT a
= a AND b
= a OR b
True if input is false
True if both inputs are true
True if at least one input is true
Truth Table
7

## Slide 8: More Simple Logic Gates
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | a NOR b
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | a NAND b
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
= a NAND b
= a NOR b
= a XOR b
True if both inputs are false
True if exactly one input is true
(or if odd number of inputs are true for > 2 inputs)
True if at least one input is false

## Slide 9: Computing with Combinational Circuits
Definition: A combinational circuit computes a pure function, i.e., its outputs react only based on its inputs. There are no feedback loops and no state information (memory) is maintained.
Theorem: Every Boolean function can be implemented with NAND and NOT. Circuits are modular
FA
FA
FA
FA
A3
B3
A2
B2
A1
B1
A0
B0
S3
S2
S1
S0
C3
C2
C1
C0
C4
… a 4-bit ripple carry adder!
  Adds by columns
  Propagation delay
= 9
(2n + 1)
Adder-4
A
B
4
4
4
S
C
C
Notes: Orally: We used to spend ⅔ of CMPT 150 on the design techniques to minimize circuit size, gate delay, etc …
The point in CMPT 295 is only that it is possible to do so, and that gate delay is a thing
Orally: This is why additions is slow. And why mul is even slower.
Orally: How to make an Adder-8?

## Slide 10: How to Represent Combinational Logic?
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 11: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 12: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register

## Slide 13: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one.

## Slide 14: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register

## Slide 15: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISCV)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 16: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 17: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: ‘S=0’?
Feedback
X
+
S

## Slide 18: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder
Xi
+
S
register
Load/Clk
reset

## Slide 19: Accumulator Revisited: Proper Timing
Reset signal shown
In practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
Xi
+
Si
register
Clk
reset
Si-1
“Undefined” (unknown) signal
X0
X0+X1
X0+X1+X2
X0+X1+X2+X3
X0
X1
X2
X3
Xi
Si
0
X0
X0+X1
X0+X1 +X2
Si-1
Reset
CLK

## Slide 20: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 21: RISC-V CPU Datapath, Control Intro
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 22: Design Principles
Five steps to design a processor:
  Analyze instruction set → datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 23: Summary !
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF (Instruction Fetch), ID (Instruction Decode), EX (Execute), MEM (Memory), WB (Write Back)
  Not all instructions are active in all phases (except for loads!)
Controller specifies how to execute instructions
  Worth thinking about: what new instructions can be added with just most control?

## Slide 24: Your CPU in two parts
Central Processing Unit (CPU):
  Datapath: contains the hardware necessary to perform operations required by the processor
    Reacts to what the controller tells it! (ie. “I was told to do an add, so I”ll feed these arguments through an adder)
  Control: decides what each piece of the datapath should do
    What operation am I performing? Do I need to get info from memory? Should I write to a register? Which register?
    Has to make decisions based on the input instruction only!

## Slide 25: Design Principles
Determining control signals
  Any time a datapath element has an input that changes behavior, it requires a control signal (e.g. ALU operation, read/write)
  Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector (e.g. next PC, ALU input, register to write to)
Your control signals will change based on your exact datapath
Your datapath will change based on your ISA

## Slide 26: Functional Unit/ALU
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A + 1
1101 B
32
Hardware circuits are fixed
Can’t adjust wires / gates while running
Build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:

## Slide 27: Data Multiplexor (MUX): Router/Selector
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this input has n bits
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 28: Another Design for 4-to-1 MUX
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:
A
B
0
1
C
D
S0
0
1
S1
0
1
E

## Slide 29: Storage Element: Register File
Register File consists of 31 registers:
  Output ports portA and portB
  Input port portW
Register selection
  Place data of register RA (number) onto portA
  Place data of register RB (number) onto portB
  Store data on portW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK is passed to all internal registers so they can be written to if they match RW and Write Enable is 1
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 30: Storage Element: Memory
Memory consists of byte array:
  1 input and output port
  1 address port
  1 bit read/write
Read Operation
  Place address on address port; Read data of register RB (number) onto portB
Write Operation
  Place address on address port; place data to be written on output portB.
Clk
Write Data
Read/Write
32
32
Read
32
Address
# Words * Word Size

## Slide 31: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
New hardware: ALU (Arithmetic Logic Unit)
Abstraction for adders, multipliers, dividers, etc.
How do we know what operation to execute?
  Our first control bit! ALUSel(ect)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel
inst[31:0]
31
0
func7(7)
opcode(7)
rs2(5)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
25 24

## Slide 32
Inst[31:0] |  |  |  |  |  |  |  |  | ALUSel |  | 
add |  |  |  |  |  |  |  |  | Add |  | 
sub |  |  |  |  |  |  |  |  | Sub |  | 
(R-R Op) |  |  |  |  |  |  |  |  | (Op) |  | 

## Slide 33: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel

## Slide 34
Inst[31:0] |  | ImmSel |  |  |  |  | BSel |  | ALUSel |  | 
add |  | * |  |  |  |  | Reg |  | Add |  | 
sub |  | * |  |  |  |  | Reg |  | Sub |  | 
(R-R Op) |  | * |  |  |  |  | Reg |  | (Op) |  | 
addi |  | I |  |  |  |  | Imm |  | Add |  | 

## Slide 35: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb

## Slide 36
Inst[31:0] |  | ImmSel |  |  |  |  | BSel | ASel | ALUSel | MemRW | WBSel
add |  | * |  |  |  |  | Reg | Reg | Add | Read | ALU
sub |  | * |  |  |  |  | Reg | Reg | Sub | Read | ALU
(R-R Op) |  | * |  |  |  |  | Reg | Reg | (Op) | Read | ALU
addi |  | I |  |  |  |  | Imm | Reg | Add | Read | ALU
lw |  | I |  |  |  |  | Imm | Reg | Add | Read | Mem

## Slide 37: Storage Element: Idealized Memory
Memory (idealized)
  One input port: Data In
  One output port: Data Out
Memory access:
  Read: Write Enable = 0, data at Address is placed on Data Out
  Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: Address valid → Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

## Slide 38: Current Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
ALU
mem
wb
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
BSel
ALUSel
MemRW
WBSel
wb
pc+4

## Slide 39: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”

## Slide 40
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *

## Slide 41
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 42: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb

## Slide 43: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 44: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 45: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc

## Slide 46: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc