## Slide 1: Combinational Logic
CMPT 295 Week 10.1

## Slide 2: Hardware Design
Understand how processors work
  Requires digital systems knowledge
Understand how code is actually executed on a computer to analyze:
  Reliability
  Performance
  Security
Layered abstractions
  Transistors → Combinational Logic → Sequential Logic → Processors → Machine Language → Assembly → High-level Programming Languages → Application programs
  At each step we can “abstract away” the lower layers

## Slide 3: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    High/Low voltage represent True/False, 1/0
Hardware of a processor (e.g., RISC-V) is an example of a Synchronous Digital System

## Slide 4: Moore’s Law
Original Version (1965): Since the integrated circuit was invented, the number of transistors in an integrated circuit has roughly doubled every year; this trend would continue for the foreseeable future
1975: Revised - circuit complexity doubles every two years

## Slide 6: Moore’s Law
Original Version (1965): Since the integrated circuit was invented, the number of transistors in an integrated circuit has roughly doubled every year; this trend would continue for the foreseeable future
1975: Revised - circuit complexity doubles every two years
Hardware Trend: Hardware gets more powerful every year (due to technology advancement and the hard work of many engineers)
Software Trend: Software gets faster and uses more resources (And has to keep up with ever-changing hardware)
Digital circuits are used to build hardware

## Slide 7: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 8: Simple Logic Gates
Special names and symbols:
NOT
AND
OR
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | A OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | NOT a
0 | 1
1 | 0
Circle means NOT!
= NOT a
= a AND b
= a OR b
True if input is false
True if both inputs are true
True if at least one input is true
Truth Table

## Slide 9: More Simple Logic Gates
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | a NOR b
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | a NAND b
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
= a NAND b
= a NOR b
= a XOR b
True if both inputs are false
True if exactly one input is true
True if at least one input is false

## Slide 10: Combining Multiple Logic Gates
A
B
C
D
D = (NOT(A AND B)) AND (A OR (NOT B AND C))

## Slide 11: How to Represent Combinational Logic?
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 12: Truth Tables
Table that relates the inputs to a combinational logic circuit to its output
  Output only depends on current inputs
  Use abstraction of 0/1 (F/T) instead of high/low Voltage
  Shows output for every possible combination of inputs
How big is a truth table with N inputs?
  0 or 1 for each of N inputs, so 2N rows

## Slide 13: N-input Truth Tables
F
Y
A
B
C
For N inputs, how many distinct functions F do we have?
Function maps each row to 0 or 1, so possible functions
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
Y
F(0,0,0)
F(0,0,1)
F(0,1,0)
F(0,1,1)
F(1,0,0)
F(1,0,1)
F(1,1,0)
F(1,1,1)
0
1
0
0
0
1
1
0
Notes: Circle the output, use variables/animations, talk about the output as a bit combination (integer?) Maybe 3 inputs?

## Slide 14: Truth Tables with Multiple Outputs
For 3 outputs, just three indep. functions: X(A,B,C,D), Y(A,B,C,D), and Z(A,B,C,D)
  Can show functions in separate columns (no additional rows)
F
Y
A
B
C
D
X
Z

## Slide 15
Question: Which of the columns A-D is the correct output of the Truth Table for: (X XOR Y) OR (NOT Z)
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1

## Slide 16
X | Y | Z | (A) | (B) | (C) | (D)
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1 | 1
Question: Which of the columns A-D is the correct output of the Truth Table for: (X XOR Y) OR (NOT Z)

## Slide 17: More Complex Truth Tables
3-Input Majority
a | b | c | y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
2-bit Adder
A |  | B |  | C |  | 
a1 | a0 | b1 | b0 | c2 | c1 | c0
 |  |  | . |  |  | 
 |  |  | . |  |  | 
 |  |  | . |  |  | 
+
c1
a1
a0
b1
b0
c2
c0
How many
rows?

## Slide 18: Truth Tables Don’t Scale
Truth tables are huge
  Write out EVERY combination of inputs and outputs (thorough, but inefficient)
  Finding a particular combination of inputs involves scanning a large portion of the table
Boolean Algebra is a shorter way to represent combinational logic

## Slide 19: Boolean Algebra
Represent inputs and outputs as variables
  Each variable can only take on the value 0 or 1
Overbar or ¬ is NOT: “logical complement”
  e.g. if A is 0, A is 1. If A is 1, then ¬A is 0
Plus (+) is 2-input OR: “logical sum”
Product (·) is 2-input AND: “logical product”
  Sometimes omitted
All other gates and logical expressions can be built from combinations of these
AB + AB == (NOT(A AND B)) OR (A AND (NOT B))

## Slide 20: Laws of Boolean Algebra
These laws allow us to simplify Boolean expressions:
Notes: Demorgan’s law example

## Slide 21: Converting Truth Table to Boolean Expression
We can show that these are equivalent!
Read off of table
  For 1, write variable name
  For 0, write complement of variable
Sum of Products (SoP)
  Take rows with 1’s in output column, sum products of inputs
  c=
Product of Sums (PoS)
  Take rows with 0’s in output column, product the sum of the complements of the inputs
  c =
a | b | c
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a
b
+
a
b
(a + b) · (a + b)
Notes: Choice between the two generally comes down to whether the output function has more 0’s or 1’s. Choosing the conversion (SoP/PoS) with less items will result in a shorter expression!
(This example happens to be balanced: 2 0’s and 2 1’s)

## Slide 22: Simplifying Boolean Expressions
Logic Delay: Everything we are dealing with is just an abstraction of transistors and wires
  Inputs propagating to the outputs are voltage signals passing through transistor networks
  There is always some delay before a CL’s output updates to reflect the inputs
  Critical Path is longest delay from any input to output. Could be represented as “n gate delays”
Simpler Boolean expressions ↔ smaller transistor networks ↔ smaller circuit delays ↔ faster hardware

## Slide 23: Simplifying Boolean Expressions: Example
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = b
= ab + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 24: Karnaugh Maps
Used to simplify Boolean expressions of 2-4 variables
Table composed of squares each representing a unique combination of all variable (1 if true, else blank)
Two variable Map:
0
1
0
1
x + y
Example: Boolean Expression?

## Slide 25: Three Variable Karnaugh Maps
0
1
Question: Simplify

## Slide 26: Example: Simplify 3-Variable Expression
 | 1 | 1 | 1
 | 1 | 1 | 
0
1
Question: Simplify
Answer:

## Slide 27: Four Variable Karnaugh Maps
00
01
11
10
Question: Simplify

## Slide 28: Example: Simplify 4-Variable Expression
 | 1 | 1 | 1
 | 1 | 1 | 1
 |  | 1 | 
 |  | 1 | 1
00
01
11
10
Simplify
Solution:

## Slide 29: Useful Combinational Circuits

## Slide 30: Data Multiplexor (MUX)
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this input has n bits
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 31: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 32: 1-bit 4-to-1 MUX
Schematic:
Truth Table: How many rows?
Boolean Expression: E = S1S0A + S1S0B + S1S0C + S1S0D
26
A
D
S= S1S0
00
11
E
‘2
01
10
B
C

## Slide 33: Another Design for 4-to-1 MUX
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:
A
B
0
1
C
D
S0
0
1
S1
0
1
E

## Slide 34: Full Adder
S = A ⊕ B ⊕ C; C = AB + C(A ⊕ B)
0
1
1
0
1
0
0
1
function table:
  basically a truth table
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
1
1
1
3-bit
Addition!
A
B
C
Q. What’s the propagation delay?
C
S
3 gate delays (highlighted)
Q. What does the circuit accomplish?
Algebra:
S = A ^ B ^ C
; C = (A & B) | (C & (A ^ B))
S = A ⊕ B ⊕ C
C S
Full Adder
Half Adder
Half Adder
FA
S
C
C
A
B