## Slide 1: Control Signals: Big picture!
Control signals are how we get the same hardware to behave differently and produce different instructions
For every instruction, all control signals are set to one of their possible values (Not always 0 or 1!) or an indeterminate (*) value indicating the control signal doesn’t affect the instruction’s execution
Each control signal has a sub-circuit based on ~nine bits from the instruction format:
  Upper 5 func7 bits (lower 2 are the same for all 295 instructions)
  All func3 bits
  “2nd” upper opcode bit (others are the same for all 295 instructions)

## Slide 2: Control Signals: ADD
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 3
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 4: Agenda
Quick Datapath Review
Control Implementation
Performance Analysis
Pipelined Execution
Pipelined Datapath

## Slide 5: Instruction Timing
IF | ID | EX | MEM | WB | Total
IMEM | Reg Read | ALU | DMEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 6: Control Signals: ADD
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 7: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time! ex. “IF” active every 600ps
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  | X | 600ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps
Instruction 1
Instruction 2
ID
MEM
WB
ALU
IF
ID
MEM
WB
ALU
IF
Clk

## Slide 8: Performance Measures
In our example, CPU executes instructions at 1.25 GHz
  1 instruction every 800 ps
Can we improve its performance?
  What do we mean with this statement?
  Not so obvious:
    Quicker response time, so one job finishes faster?
    More jobs per unit time (e.g. web server returning pages)?
    Longer battery life?

## Slide 9: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Performance Analysis
Pipelined Execution
Pipelined Datapath

## Slide 10: Control Signals: ADD
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 11: Pipeline
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 12: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 13: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 14: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 15: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 16: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 17: At time t = 0
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2

## Slide 18: At time t = 4
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)

## Slide 19: At time t = 5
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)

## Slide 20: At time t = 6
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)

## Slide 21: Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep= 200,100,200,200,100 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 5 x tcycle =1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Longest pipeline stage
Notes: Tc = “Time between completion of instructions”

## Slide 22
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be ?x slower.
The throughput will be ?x higher.
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access Throughput:
Old: one inst every (IF+ID+EX+WB) = 600 ps →
New: one inst every (4*max_stage)/4 = 200 ps
New/Old throughput = (1/200)/(1/600) = 3x higher
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 23
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access Latency (per inst):
Old latency: IF+ID+EX+WB = 600 ps
New latency = 4*max_stage = 800 ps (only as fast as slowest stage; faster stage slowed down since common clock).
New/Old = 800/600 = 1.33x slower
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be ?x slower.
The throughput will be 3x higher.
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 24: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 25: Speed Trade-off Example
For some task (e.g. image compression) …
 | Processor A | Processor B
# Instructions | 1 Million | 1.5 Million
Average CPI | 2.5 | 1
Clock rate f | 2.5 GHz | 2 GHz
Execution time | 1 ms | 0.75 ms
Processor B is faster for this task, despite executing more instructions and having a lower clock rate! Why? Each instruction is less complex! (~2.5 B instructions = 1 A instruction)

## Slide 26: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 27: Instruction Level Parallelism (ILP)
Pipelining allows us to execute parts of multiple instructions at the same time using the same hardware!
  This is known as instruction level parallelism
Later: Other types of parallelism
  DLP: same operation on lots of data (SIMD)
  TLP: executing multiple threads “simultaneously” (e.g., using OpenMP or pthreads)

## Slide 28: RISC-V Pipeline
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
Resource use by instruction over time
Resource use in a particular time slot

## Slide 29: RISC-V Pipeline Example
Address | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x00 | addi a0, zero, 5 | IF | ID | EX | MEM | WB |  |  | 
0x04 | addi a1, a4, 5 |  | IF | ID | EX | MEM | WB |  | 
0x08 | addi a2, a5, 5 |  |  | IF | ID | EX | MEM | WB | 
0x0C | addi a3, a6, 5 |  |  |  | IF | ID | EX | MEM | WB

## Slide 30: Agenda
RISC-V Pipeline
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors
Hazards Ahead!

## Slide 31: Pipeline Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data write
Control hazard
  Flow of execution depends on previous instruction

## Slide 32: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add s0, s1, s2
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
Stored
during WB
Read during ID

## Slide 33: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s0,s1,s2
add s4,s0,s3
Pipeline registers separate stages, hold data for each instruction in flight
add s5,s0,s6

## Slide 34: 2. Data Hazards (2/2)
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2
Time (clock cycles)
Identifying data hazards:
Where is data WRITTEN?
Where is data READ?
Does the WRITE happen AFTER the READ?

## Slide 35: Solution 1: Stalling
Problem: Instruction depends on result from previous instruction
  add s0, s1, s2 sub s4, s0, s3
Bubble:
  effectively NOP: affected pipeline stages do “nothing” (add x0 x0 x0)
add s0, s1, s2
sub s4, s0, s3

## Slide 36
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s0,s1,s2
add s4,s0,s3
Pipeline registers separate stages, hold data for each instruction in flight
add s5,s0,s6

## Slide 37
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s4,s0,s3
Pipeline registers separate stages, hold data for each instruction in flight
add s5,s0,s6
add s0,s1,s2

## Slide 38: Data Hazard
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | add s0, s1, s2 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | sub s4, s0, s3 |  | IF | ID | ID | ID | EX | MM | WB |  |  | 
0x08 | and s5, s0, s6 |  |  | IF | IF | IF | ID | EX | MM | WB |  | 
0x0C | or s7, s0, s8 |  |  |  |  |  | IF | ID | EX | MM | WB | 

## Slide 39: Add independent instructions or nops
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s0,s1,s2
Pipeline registers separate stages, hold data for each instruction in flight
add s5,s0,s6
add t0,t1,t2
add t5,t3,t4

## Slide 40: Add independent instructions or nops
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s0,s1,s2
Pipeline registers separate stages, hold data for each instruction in flight
add t0,t1,t2
add t5,t3,t4
add s5,s0,s6

## Slide 41: Forwarding
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add s0,s1,s2
Pipeline registers separate stages, hold data for each instruction in flight
add s5,s0,s6
add s4,s0,s3

## Slide 42: Data Hazard with Forwarding
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | add s0, s1, s2 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | sub s4, s0, s3 |  | IF | ID | EX | MM | WB |  |  |  |  | 
0x08 | and s5, s0, s6 |  |  | IF | ID | EX | MM | WB |  |  |  | 
0x0C | or s7, s0, s8 |  |  |  | IF | ID | EX | MM | WB |  |  | 

## Slide 43: Data Hazard Solution: Forwarding
Forward result as soon as it is available, even though it’s not stored in RegFile yet
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2
Forwarding: get operand from pipeline stage, rather than register file

## Slide 44: Data Hazard: Loads (1/2)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load (sub), then forward after the load is done (more hardware)
sub t3, t0, t2
lw t0, 0(t1)

## Slide 45: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
lw t0, 0 (t1)
sub t3,t0,t2
Pipeline registers separate stages, hold data for each instruction in flight
add t3,t0,t2

## Slide 46: Incorrect Exe: LW not available until later
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Pipeline registers separate stages, hold data for each instruction in flight
add t3,t0,t2
lw t0, 0 (t1)
sub t3,t0,t2

## Slide 47: Correct Exe: Stall
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Pipeline registers separate stages, hold data for each instruction in flight
add t3,t0,t2
lw t0, 0 (t1)
sub t3,t0,t2

## Slide 48: Data Hazard: Loads (2/2)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware will stall for one cycle
  Equivalent to inserting an explicit nop in the slot
    except the latter uses more code space
  Performance loss
Idea: Let the compiler/assembler put an unrelated instruction in that slot → no stall!

## Slide 49: Load Data Hazards with Forwarding
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | lw s0, 0 (t1) | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | sub s4, s0, s3 |  | IF | ID |  | EX | MM | WB |  |  |  | 
0x08 | and s5, s0, s6 |  |  | IF |  | ID | EX | MM | WB |  |  | 
0x0C | or s7, s0, s8 |  |  |  |  | IF | ID | EX | MM | WB |  | 
IF

## Slide 50: Structural Hazard: Regfile!
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
Time (clock cycles)
RegFile: Used in ID and WB!

## Slide 51: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 52: RISC-V Pipeline: Regfile Structural Hazard
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | addi a0, zero, 5 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | addi a1, a4, 5 |  | IF | ID | EX | MM | WB |  |  |  |  | 
0x08 | addi a2, a5, 5 |  |  | IF | ID | EX | MM | WB |  |  |  | 
0x0C | addi a3, a6, 5 |  |  |  | IF | - | - | - | ID | EX | MM | WB
0x0F | Instuction |  |  |  | IF | - | - | - | - | ID |  | 

## Slide 53: Regfile Structural Hazards
Each instruction:
  Can read up to two operands in decode stage
  Can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  Two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 54: Regfile Structural Hazards
Two alternate solutions:
  Build RegFile with independent read and write ports; good for single-stage
  Double Pumping: Split RegFile access in two. Prepare to write during 1st half, write on rising edge, read during 2nd half of each clock cycle (falling edge)
    Will save us a cycle later...
    Possible because RegFile access is fast (takes less than half the time of ALU stage)
Conclusion: It is OK to read and Write to registers during same clock cycle

## Slide 55: RISC-V Pipeline: Regfile Structural Hazard
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | addi a0, zero, 5 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | Instruction |  | IF | ID | EX | MM | WB |  |  |  |  | 
0x08 | Instruction |  |  | IF | ID | EX | MM | WB |  |  |  | 
0x0C | addi a3, a0, 5 |  |  |  | IF | ID | EX | MM | WB |  |  | 
0x0F | Instuction |  |  |  |  | IF | ID | EX | MM | WB |  | 

## Slide 56: Structural Hazard: Memory Access
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Instruction and data memory used simultaneously
  Use two separate memories

## Slide 57: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory unit
  Load/store requires data access
  Without separate memory units, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memory units
  Or separate instruction/data caches
RISC ISAs (including RISC-V) designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 58: 3. Control Hazards
Branch (beq, bne,...) determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Result isn’t known until end of execute
Simple Solution: Stall or flush on every branch until we have the new PC value
  How long must we stall?

## Slide 59
How many instructions after beq are affected by the control hazard?
1
2
3
4
5
beq
Instr 1
Instr 2
Instr 3
Instr 4

## Slide 60
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Pipeline registers separate stages, hold data for each instruction in flight
Ins
bne a2,zero,L1
Ins

## Slide 61: Branch Stall
How many bubbles required for branch?
beq
Instr 1
Instr 2
Instr 3
Instr 4
Time (clock cycles)

## Slide 62: Taken branch (Stall 2 cycles)
Address | Ins-Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 |  | 
0x00 | add a2, a1, a0 | IF | ID | EX | MM | WB |  |  |  | 
0x04 | bne a2, zero, 0x00000010 |  | IF | ID | EX | MM | WB |  |  | 
0x08 | addi a3, zero, 1 |  |  |  |  |  |  |  |  | 
0x0c | jal zero, 0x00000014 |  |  |  |  |  |  |  |  | 
0x10 | addi a3, zero, 0 |  |  |  |  | IF | ID | EX |  | 
0x14 | ecall |  |  |  |  |  | IF | ID |  | 

## Slide 63: Kill Instructions after Branch if Taken
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
label: xxxxxx
PC updated reflecting branch outcome
Taken branch
Convert to NOP
Convert to NOP
Two instructions are affected by an incorrect branch, just like we’d have to insert two NOP’s/stalls in the pipeline to wait on the correct value!

## Slide 64: Taken branch (Flush 2 cycles; same as stall)
Address | Ins-Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6
0x00 | add a2, a1, a0 | IF | ID | EX | MM | WB |  | 
0x04 | bne a2, zero, 0x00000010 |  | IF | ID | EX | MM | WB | 
0x08 | addi a3, zero, 1 |  |  | IF | ID |  |  | 
0x0c | jal zero, 0x00000014 |  |  |  | IF |  |  | 
0x10 | addi a3, zero, 0 |  |  |  |  | IF | ID | EX
0x14 | ecall |  |  |  |  |  | IF | ID

## Slide 65: 3. Control Hazard: Branching
RISC-V Solution: Branch Prediction – guess outcome of a branch, fix afterwards if necessary
  Must cancel (flush) all instructions in pipeline that depended on guess that was wrong
  How many instructions do we end up flushing?

## Slide 66: Not taken w/ Prediction (saved 2 cycles)
0x00 | add a2, a1, a0 | IF | ID | EX | MM | WB | 
0x04 | beq a2, zero, 0x00000010 |  | IF | ID | EX | MM | WB
0x08 | addi a3, zero, 1 |  |  | IF | ID | EX | MM
0x0c | jal zero, 0x00000014 |  |  |  | IF | ID | EX

## Slide 67: Taken branch (Flush 2 cycles)
Address | Ins-Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6
0x00 | add a2, a1, a0 | IF | ID | EX | MM | WB |  | 
0x04 | bne a2, zero, 0x00000010 |  | IF | ID | EX | MM | WB | 
0x08 | addi a3, zero, 1 |  |  | IF | ID |  |  | 
0x0c | jal zero, 0x00000014 |  |  |  | IF |  |  | 
0x10 | addi a3, zero, 0 |  |  |  |  | IF | ID | EX
0x14 | ecall |  |  |  |  |  | IF | ID

## Slide 68: Taken w/ Incorrect Prediction (same as stalling )
0x00 | add a2, a1, a0 | IF | ID | EX | MM | WB | 
0x04 | beq a2, zero, 0x00000010 |  | IF | ID | EX | MM | WB
0x08 | addi a3, zero, 1 |  |  | IF | ID | EX | MM
0x0c | jal zero, 0x00000014 |  |  |  | IF | ID | EX

## Slide 69: Branch Prediction
beq t0, t1, label
label: …..
…..
Taken branch
Guess next PC!
Check guess correct
In the correct case, we don’t have any stalls/NOP’s at all!
Prediction, if done correctly, is better on average than stalling

## Slide 70: Ecall (Stall in EX for instructions ahead)
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Pipeline registers separate stages, hold data for each instruction in flight
ecall
Ins
Ins