## Slide 1: Class Review
CMPT 295 Week 12

## Slide 2: Caches and Virtual Memory
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 3: Cache Code Analysis Problem
Cache-A Direct-mapped, 4KB, 64 sets
Cache-B Set-associate, 4KB, 2 ways, 32 sets
int size = 4096; // int is 4 bytes
int a[size];
long long int a_long[size]; // long long int is 8 bytes
/* loop 1 */
for (int i = 0; i < size; i++) {
a[i] = i;
}
/* loop 2 */
for (int i = 0; i < size; i += 1) {
b[….] = a[i];
}
Question: Hit rates for loop1, loop 2 (assume loop 1 has run)
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)

## Slide 4: Sources of Cache Misses: The 3Cs
Compulsory: (Many names: cold start, process migration (switching processes), 1st reference)
  First access to block impossible to avoid; Effect is small for long running programs
Capacity:
  Cache cannot contain all blocks accessed by the program, so full associativity won’t hold all blocks
Conflict: (collision)
  Multiple memory locations mapped to the same cache location, so there is a lack of associativity

## Slide 5: Cache & VM Problem
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
  14-bit virtual addresses, 12-bit physical address
  Page size = 64 bytes
  Cache: Direct-mapped with = 4 B, = 16

## Slide 6: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 7: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, page fault

## Slide 8: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, Page Table Hit, Cache Miss

## Slide 9: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 10: Digital Logic
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 11: Laws of Boolean Algebra
These laws allow us to simplify Boolean expressions:
Notes: Demorgan’s law example

## Slide 12: Simplifying Boolean Expressions: Example
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = b
= ab + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 13: Three Variable Karnaugh Maps
0
1

## Slide 14: Example: Simplify 3-Variable Expression
 | 1 | 1 | 1
 | 1 | 1 | 
0
1
Question: Simplify
Answer:

## Slide 15: Example: Simplify 3-Variable Expression
0
1
Question: Simplify

## Slide 16: Data Multiplexor (MUX)
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this input has n bits
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 17: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 18: 1-bit 4-to-1 MUX
Schematic:
A
D
S= S1S0
00
11
E
‘2
01
10
B
C

## Slide 19: Decoder
Enable one of 2N outputs based on N input
Example: 2-to-4 decoder
Use case: Choose ALU operation based on instruction op-code
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 20: Demultiplexer (Demux)
Similar to decoder with an enable signal
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 21: Functional Unit
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A + 1
1101 B
32
Hardware circuits are fixed
Can’t adjust wires / gates while running
Build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:

## Slide 22: Functional Unit: Adder-Subtractor
32
Adder-32
32
32
A
32
B
S
C
FS
if FS == 0 then
S = A + B
if FS == 1 then
= A − B
S = A + B + 1

## Slide 23: Sequential Circuits: Registers
N-bit register  n instances of a “Flip-Flop”
  Output flips and flops between 0 and 1
Specifically this is a “D-type Flip-Flop”
  D is “data input”, Q is “data output”
  A group of wires when interpreted as a bit field is called a bus
FF
d0
q
CLK
FF
d1
q
CLK
FF
dn-1
q
CLK
Register
D (n-bit)
Q(n-bit)
CLK
…


## Slide 24: Flip-Flop Timing Behavior
FF
d
q
CLK

## Slide 25
Setup Time
FF
d
q
CLK
Flip-Flop Timing Behavior

## Slide 26
Hold Time
FF
d
q
CLK
Flip-Flop Timing Behavior

## Slide 27
Clock-to-Q
Flip-Flop Timing Behavior
FF
d
q
CLK

## Slide 28: Timing Terms
Clock: Steady square wave that synchronizes system
Register: Several bits of state that samples on rising edge of Clock (positive edge-triggered); also has RESET
Setup Time: When input must be stable before Clock trigger
Hold Time: When input must be stable after Clock trigger
Clock-to-Q Delay: How long it takes output to change from Clock trigger
Notes: STOP HERE

## Slide 29: Digital State Machines
Memory holds state information
memory
combinational
circuit
current
state
inputs
next state
outputs
compute next state based on (current state, inputs)
compute outputs based on (current state, inputs)
Q. What does this imply about the clock period?
clock period must exceed (tpd of combinational circuit + tpd of registers) where tpd is propagational delay

## Slide 30: Model for Synchronous Systems
Combinational logic blocks separated by registers
  Clock signal connects only to sequential logic elements
  Feedback is optional depending on application
How do we ensure proper behavior?
  How fast can we run our clock?

## Slide 31: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 32: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register

## Slide 33: RISC-V CPU Datapath, Control Intro
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 34: Storage Element: Register File
Register File consists of 32 registers:
  Output ports portA and portB
  Input port portW
Register selection
  Place data of register RA (number) onto portA
  Place data of register RB (number) onto portB
  Store data on portW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK is passed to all internal registers so they can be written to if they match RW and Write Enable is 1
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 35: Implementing R-Types
Perform operation
New hardware: ALU (Arithmetic Logic Unit)
Abstraction for adders, multipliers, dividers, etc.
How do we know what operation to execute?
  Our first control bit! ALUSel(ect)
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel
inst[31:0]
31
0
func7(7)
opcode(7)
rs2(5)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
25 24

## Slide 36: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel
31
0
imm(12)
opcode(7)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19

## Slide 37: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb
31
0
offset(12)
opcode
base
width
dst
7 6
12 11
15 14
20 19

## Slide 38: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”
31
0
imm(11:5)
opcode
rs2
rs1
func3
imm(4:0)
7 6
12 11
15 14
20 19
25 24

## Slide 39: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb
31
0
imm(12|10:5)
opcode
rs2
rs1
func3
imm(4:1|11)
7 6
12 11
15 14
20 19
25 24

## Slide 40: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb
31
0
offset
opcode
base
Func3
dest
7 6
12 11
15 14
20 19
Writes PC+4 to dest (return address)
Sets PC = base + offset

## Slide 41: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb
imm[20|10:1|11|19:12]
opcode
rd
31
0
jal saves PC+4 in register rd (the return address)
Set PC = PC + offset (PC-relative jump)
7 6
12 11

## Slide 42: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc
imm[31:12]
opcode
rd
31
0
lui writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits
7 6
12 11

## Slide 43: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc
imm[31:12]
opcode
rd
31
0
Adds upper immediate value to PC and places result in destination register
7 6
12 11

## Slide 44: Control Signals: ADD
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 45: ADD: Control Signals
Here are the signals and values we’ve compiled for our ADD instruction:
(green = left 3 cols = control INPUTS)
(orange = right 9 cols = control OUTPUTS)
Inst[31:0] | BrEq | BrLT | PCSel | ImmSel | BrUn | ASel | BSel | ALUSel | MemRW | RegWEn | WBSel
add | * | * | +4 | * | * | Reg | Reg | Add | Read | 1 (Y) | ALU

## Slide 46: addi datapath
Control Logic
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrLT | BrEq | BSel | ASel | ALUSel | MemRW | WBSel
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU

## Slide 47: lw datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem

## Slide 48: Br datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *

## Slide 49: jal datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4

## Slide 50
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 51: Instruction Timing
IF | ID | EX | MEM | WB | Total
IMEM | Reg Read | ALU | DMEM | Reg W | 
200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps

## Slide 52: Instruction Timing
Maximum clock frequency
  fmax = 1/800ps = 1.25 GHz
Most blocks idle most of the time! ex. “IF” active every 600ps
Instr | IF = 200ps | ID = 100ps | ALU = 200ps | MEM=200ps | WB = 100ps | Total
add | X | X | X |  | X | 600ps
beq | X | X | X |  |  | 500ps
jal | X | X | X |  | X | 600ps
lw | X | X | X | X | X | 800ps
sw | X | X | X | X |  | 700ps
Instruction 1
Instruction 2
ID
MEM
WB
ALU
IF
ID
MEM
WB
ALU
IF
Clk

## Slide 53: “Iron Law” of Processor Performance
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 54: RISC-V Pipeline
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
Resource use by instruction over time
Resource use in a particular time slot

## Slide 55: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 56: RISC-V Pipeline Example
Address | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x00 | add a1,a2,a3 | IF | ID | EX | MEM | WB |  |  | 
0x04 | addi a4,a5,0x2f7 |  | IF | ID | EX | MEM | WB |  | 
0x08 | sub s4,s0,s3 |  |  | IF | ID | EX | MEM | WB | 
0x0C | or s1,s2,s5 |  |  |  | IF | ID | EX | MEM | WB

## Slide 57
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be 1.33x slower.
The throughput will be 3x faster.
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 58: Pipeline Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data write
Control hazard
  Flow of execution depends on previous instruction

## Slide 59: Structural Hazard: Register File
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
Time (clock cycles)
RegFile: Used in ID and WB

## Slide 60: RISC-V Pipeline: Regfile Structural Hazard
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | addi a0, zero, 5 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | addi a1, a4, 5 |  | IF | ID | EX | MM | WB |  |  |  |  | 
0x08 | addi a2, a5, 5 |  |  | IF | ID | EX | MM | WB |  |  |  | 
0x0C | addi a3, a6, 5 |  |  |  | IF | ID | ID | EX | MM | WB |  | 

## Slide 61: Data Hazard: Read after Write
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | add s0, s1, s2 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | sub s4, s0, s3 |  | IF | ID | - | - | EX | MM | WB |  |  | 
0x08 | and s5, s0, s6 |  |  | IF | IF | IF | ID | EX | MM | WB |  | 
0x0C | or s7, s0, s8 |  |  |  |  |  | IF | ID | EX | MM | WB | 

## Slide 62: Data Hazard Solution: Forwarding
Forward result as soon as it is available, even though it’s not stored in RegFile yet
sub s4, s0, s3
and s5, s0, s6
or s7, s0, s8
xor s9, s0, s10
add s0, s1, s2
Forwarding: get operand from pipeline stage, rather than register file

## Slide 63: Data Hazard with Forwarding
Addr | Inst ¦ Cycle | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0x00 | add s0, s1, s2 | IF | ID | EX | MM | WB |  |  |  |  |  | 
0x04 | sub s4, s0, s3 |  | IF | ID | EX | MM | WB |  |  |  |  | 
0x08 | and s5, s0, s6 |  |  | IF | ID | EX | MM | WB |  |  |  | 
0x0C | or s7, s0, s8 |  |  |  | IF | ID | EX | MM | WB |  |  | 

## Slide 64: Data Hazard: Loads
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load (sub), then forward after the load is done (more hardware)
sub t3, t0, t2
lw t0, 0(t1)

## Slide 65: Control Hazards: Taken Branch & ecall

## Slide 66: Not-Taken Branch