## Slide 1: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW

## Slide 2
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 3
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be ?x slower.
The throughput will be ?x higher.
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access Throughput:
Old: one inst every (IF+ID+EX+WB) = 600 ps →
New: one inst every (4*max_stage)/4 = 200 ps
New/Old throughput = (1/200)/(1/600) = 3x higher
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 4
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps
No mem access Latency (per inst):
Old latency: IF+ID+EX+WB = 600 ps
New latency = 4*max_stage = 800 ps
New/Old = 800/600 = 1.33x slower
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be ?x slower.
The throughput will be 3x higher.
Notes: 1/600
4/800 = 1/200
1/200*600/1 = 3x faster throughput
800/600 = 4/3 = 1.33!!

## Slide 5
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 6: Access Patterns
How many hits within a single block once it is loaded into cache?
Will block still be in cache when you revisit its elements?
Are there special/edge cases to consider?
  Usually edge of block boundary or edge of cache size boundary
Sometimes you can generalise a block access pattern for the entire code chunk!

## Slide 7: Anatomy of a Cache Question
Cache questions come in a few flavors:
  TIO Breakdown
  For fixed cache parameters, analyze the performance of the given code/sequence
  For fixed cache parameters, find best/worst case scenarios
  For given code/sequence, how does changing your cache parameters affect performance?
  AMAT

## Slide 8: The Cache
What are the important cache parameters?
  Must figure these out from problem description
  Address size, cache size, block size, associativity, replacement policy
  Solve for TIO breakdown, # of sets, set size
Are there multiple levels?
  Mostly applies to AMAT questions
What starts in the cache?
  Not always specified (best/worst case)

## Slide 9: Example 1
Only use L1$: C = 32 KiB, K = 8 B, 4-way, LRU, write-through
char A[] is block aligned and SIZE = 32 MiB
char *A = (char *) malloc (SIZE*sizeof(char));
/* number of STRETCHes */
for (i = 0; i < (SIZE/STRETCH); i++) {
/* go up to STRETCH */
for(j=0;j<STRETCH;j++) sum += A[i*STRETCH+j];
/* down from STRETCH */
for(j=STRETCH-1;j>=0;j--) prod *= A[i*STRETCH+j];
}
2nd inner for loop hits same indices as 1st inner for loop, but in reverse order
Always traverse full SIZE, regardless of STRETCH

## Slide 10: Example 1
Only use L1$: C = 32 KiB, K = 8 B, N = 4, LRU, write-through
char A[] is block aligned and SIZE = 32 MiB
char *A = (char *) malloc (SIZE*sizeof(char));
for (i = 0; i < (SIZE/STRETCH); i++) {
for(j=0;j<STRETCH;j++) sum += A[i*STRETCH+j];
for(j=STRETCH-1;j>=0;j--) prod *= A[i*STRETCH+j];
}
As we double our STRETCH from 1 to 2 to 4 (…etc), we notice the number of cache misses doesn’t change! What is the largest value of STRETCH before cache misses changes?
32 KiB, when STRETCH exactly equals C

## Slide 11: Example 1 (But visual)
Set
0
1
210 - 1
A[0]
A[8]
A[212-8]
A[212]
Cache is full after 32 KiB
[A[0], A[215 - 1]] (green)
A[215]
A[215+8]
A[215+212-8]

## Slide 12: Example 1
Only use L1$: C = 32 KiB, K = 8 B, N = 4, LRU, write-through
char A[] is block aligned and SIZE = 32 MiB
char *A = (char *) malloc (SIZE*sizeof(char));
for (i = 0; i < (SIZE/STRETCH); i++) {
for(j=0;j<STRETCH;j++) sum += A[i*STRETCH+j];
for(j=STRETCH-1;j>=0;j--) prod *= A[i*STRETCH+j];
}
If we double our STRETCH from (b), what is the ratio of cache hits to misses?
Now STRETCH = 64 KiB. Moving sequentially by byte, so each block for entire 1st inner loop has 1 miss and 7 hits (7:1).
Upper half of STRETCH lives in cache, so first half of 2nd inner loop is 8 hits/block (8:0). Second half is as before (7:1).

## Slide 13: Example 1 (But visual)
Set
0
1
210 - 1
A[0]
A[8]
A[212-8]
A[212]
Cache is full after 32 KiB
[A[0], A[215 - 1]] (green)
A[215]
A[215+8]
A[215+212-8]
Cache fills up again entirely with the remaining 32 KiB [A[215], A[216 - 1]] (red)
So when we go through the second iteration (in reverse), red elements (2nd half) are still in the cache and green elements (first half) will need to be loaded again.

## Slide 14: Example 1
Only use L1$: C = 32 KiB, K = 8 B, N = 4, LRU, write-through
char A[] is block aligned and SIZE = 32 MiB
char *A = (char *) malloc (SIZE*sizeof(char));
for (i = 0; i < (SIZE/STRETCH); i++) {
for(j=0;j<STRETCH;j++) sum += A[i*STRETCH+j];
for(j=STRETCH-1;j>=0;j++) prod += A[i*STRETCH+j];
}
If we double our STRETCH from (b), what is the ratio of cache hits to misses?
Considering the equal-sized chunks of half of each inner for loop, we have loop 1 1st (7:1), loop 1 2nd (7:1), loop 2 1st (8:0), and loop 2 2nd (7:1).
7+7+8+7 : 1+1+0+1 = 29:3

## Slide 15: Example 2
32-bit RISC-V, 4 GiB memory, single L1$ of size C with block size K (C ≥ K and C is a power of 2).
A, B are arrays in different places of memory of equal size n (power of 2 and a [natural #] multiple of C), block aligned.
// sizeof(uint8_t) = 1
SwapLeft(uint8_t *A, uint8_t *B, int n) {
uint8_t tmp;
for (int i = 0; i < n; i++) {
tmp = A[i];
A[i] = B[i];
B[i] = tmp;
}
}
Do n times:
Read A[i]
Read B[i], Write A[i]
Write B[i]
Array data size is 1 byte

## Slide 16: Example 2
Fill in code for SwapRight so that it does the same thing as SwapLeft but improves the (b) hit:miss ratio.
SwapRight(uint8_t *A, uint8_t *B, int n) {
uint8_t tmpA, tmpB;
for (int i = 0; i < n; i++) {
______________________
______________________
______________________
______________________
}
}
tmpA = A[i];
tmpB = B[i];
B[i] = tmpA;
A[i] = tmpB;
Read A[i]
Read B[i]
Write B[i]
Write A[i]
Notes: Could also do Rd B, Rd A, Wr A, Wr B.