## Slide 1: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 2: Agenda
Stored-Program Concept
R-Format
I-Format
S-Format
SB-Format
U-Format
UJ-Format

## Slide 3
top
system reserved
stack
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
code (text)
static data
dynamic data (heap)
*Layout in 295
On actual hw code starts at
0x00400000

## Slide 4: Assembler demo

## Slide 5: Big Idea: Stored-Program Concept INSTRUCTIONS ARE DATA
programs can be stored in memory as numbers
Before: a number can mean anything
Now: make convention for interpreting numbers as instructions

## Slide 6: Instructions as Numbers
Divide the 32 bits of an instruction into “fields”
  regular field sizes → simpler hardware
  will need some variation….
31
0
By convention, RISCV instructions are each 1 word = 4 bytes = 32 bits
Notes: 6 formats to memorize, but 4 formats to internalize (R with three registers, I with two registers and an immediate, S with two registers and an address, U with a big immediate/address)

## Slide 7
So how do we represent instructions?
  Remember: Computer only understands 1s and 0s, so assembler string “add x10,x11,x0” is meaningless to hardware

## Slide 8: The 6 Instruction Formats
R-Format: instructions using 3 register inputs
  add, xor, mul —arithmetic/logical ops
I-Format: instructions with immediates, loads
  addi, lw, jalr, slli
S-Format: store instructions: sw,sb
SB-Format: branch instructions: beq, bge
U-Format: instructions with upper immediates
  lui, auipc —upper immediate is 20-bits
UJ-Format: the jump instruction: jal
Notes: lui: load upper immediate
auipc: adding an upper immediate to PC and putting the result in a register

## Slide 9: R-Format Assembler Example
add t0,t1,t2 => add x5,x6,x7
  Field representation (decimal):
  Field representation (binary):
two
0
0x33
7
6
0
5
31
0
0000000
0110011
00111
00110
000
00101
31
0
  hex representation: 0x 0073 02B3
  Called a Machine Language Instruction
Notes: x5 = t0, x6 = t1, x7 = t2

## Slide 10: Processor/Emulator Interprets Machine Ins
  0x007302B3
00000000011100110000001010110011
R-Type
f7
func3
rd
opcode
31
0
rs1
rs2
0000000
0110011
00111
00110
000
00101
31
0
0
0x33
7
6
0
5
31
0
Rd = x5, rs1 = x6 rs2 = x7. f3 = 0 and f7 = 0, opcode = 0x33 => so add x5 = x6 + x7

## Slide 11: I-Format Instructions (3/4)
opcode (7): uniquely specifies the instruction
rs1 (5): specifies a register operand
rd (5): specifies destination register that receives result of computation
imm[11:0]
func3
rd
opcode
31
0
rs1

## Slide 12: I-Format Instructions (4/4)
immediate (12): 12 bit number
  All computations done in words, so 12-bit immediate must be extended to 32 bits
  always sign-extended to 32-bits before use in an arithmetic operation
imm[11:0]
func3
rd
opcode
31
0
rs1
Can represent 212 different immediates
  imm[11:0] can hold values in range [-211 , +211)

## Slide 13: I-Format Example (1/2)
???
  addi x15,x1,-50
rd = x15
rs1 = x1
???
?
???
???
31
0
00001
imm[11:0]
func3
rd
opcode
rs1
111111001110
01111
0
0x13

## Slide 14: Processor/Emulator Interprets Machine Ins
  0x3F382793
111111001110000010011110010011
I-Type
imm[11:0]
func3
rd
opcode
rs1
???
00001
111111001110
01111
0
0x13
Imm: 111111001110 (12 bit 2s comp.)
Sign extend it before the math
To write decimal: -ve (~Imm+1)

## Slide 15: Load Instructions are also I-Type
The 12-bit signed immediate is added to the base address in register rs1 to form the memory address
  This is very similar to the add-immediate operation but used to create address, not to create final result
Value loaded from memory is stored in rd
imm[11:0]
func3
rd
opcode
31
0
rs1
offset[11:0]
width
dst
LOAD
base

## Slide 16: S-Format Used for Stores
Store needs to read two registers, rs1 for base memory address, and rs2 for data to be stored, as well as need immediate offset!
Can’t have both rs2 and immediate in same place as other instructions!
Note: stores don’t write a value to the register file, no rd!
RISC-V design decision is move low 5 bits of immediate to where rd field was in other instructions – keep rs1/rs2 fields in same place
register names more critical than immediate bits in hardware design
imm[11:5]
opcode
rs2
rs1
func3
imm[4:0]
31
0

## Slide 17: S-Format Example
sw x14, 8(x2)
imm[11:5]
opcode
rs2
rs1
func3
imm[4:0]
31
0
00000000
0100011
01110
00010
010
01000
off[11:5] = 0
STORE
rs2=14
rs1=2
SW
off[4:0] = 8

## Slide 18: RISC-V B-Format for Branches
B-format is mostly same as S-Format, with two register sources (rs1/rs2) and a 12-bit immediate
But now immediate represents values -212 to +212-2 in 2-byte increments
The 12 immediate bits encode even 13-bit signed byte offsets (lowest bit of offset is always zero, so no need to store it)
imm[12|10:5]
opcode
rs2
rs1
func3
imm[4:1|11]
31
0
7
7
5
5
3
5

## Slide 19: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Branch offset =
(Branch with offset of 0, branches to itself)
Start counting from instruction AFTER the branch
1
2
3
4
4×32-bit instructions = 16 bytes

## Slide 20: Branch Example (1/2)
RISCV Code:
  Loop: beq x19,x10,End add x18,x18,x10 addi x19,x19,-1 j Loop End: <target instr>
Start counting from branch
1
2
3
4
???????
1100011
01010
10011
000
?????
31
0
7
7
5
5
3
5
BRANCH
rs2=10
rs1=19
BEQ

## Slide 21: Branch Example (1/2)
  beq x19,x10,offset = 16 bytes
  13-bit immediate, imm[12:0], with value 16 0000000010000
0 000000
1100011
01010
10011
000
1000 0
31
0
imm[12|10:5]
imm[4:1|11]
imm[0] discarded, always zero

## Slide 22: U-Format for “Upper Immediate” instructions
Has 20-bit immediate in upper 20 bits of 32-bit instruction word
One destination register, rd
Used for two instructions
  LUI – Load Upper Immediate
  AUIPC – Add Upper Immediate to PC
imm[31:12]
opcode
rd
31
0
20
U-immediate[31:12]
7
LUI/AUIPC
5
dest

## Slide 23: LUI to create long immediates
lui writes the upper 20 bits of the destination with the immediate value, and clears the lower 12 bits
Together with an addi to set low 12 bits, can create any 32-bit value in a register using two instructions (lui/addi).
lui x10, 0x87654 # x10 = 0x87654000
addi x10, x10, 0x321 # x10 = 0x87654321

## Slide 24: jalr
# ret and jr psuedo-instructions
ret = jr ra = jalr x0, ra, 0
# Call function at any 32-bit absolute address
lui x1, <hi 20 bits>
jalr ra, x1, <lo 12 bits>
# Jump PC-relative with 32-bit offset
auipc x1, <hi 20 bits>
jalr x0, x1, <lo 12 bits>
imm[11:0]
func3
rd
opcode
31
0
rs1
offset
0
dest
JALR
base

## Slide 25: Summary of RISC-V Instruction Formats

## Slide 26: Agenda
Function calls and Jumps
Call Stack
Register Convention
Program memory layout

## Slide 27: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data

## Slide 28: Six Steps of Calling a Function
Put arguments in a place where the function can access them
Transfer control to the function
The function will acquire any (local) storage resources it needs
The function performs its desired task
The function puts return value in an accessible place and “cleans up”
Control is returned to you

## Slide 29: Jumps are not enough
main:
j myfn
after1:
add x1,x2,x3
myfn:
…
…
j after1
Jumps to the callee
Jumps back
1
2
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 30: Jumps are not enough
myfn:
…
…
main:
j myfn
after1:
add x1,x2,x3
j myfn
after2:
sub x3,x4,x5
Jumps to the callee
Jumps back
What about multiple sites?
1
2
??? Change target
on the fly ???
j after2
3
4
j after1
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 31: Takeaway 1: Need Jump And Link
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register x1 (aka $ra or return address)
Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register x1

## Slide 32: Jump-and-Link / Jump Register
main:
jal myfn
after1:
add x1,x2,x3
jal myfn
after2:
sub x3,x4,x5
myfn:
…
…
jr x1
JAL saves the PC in register $31
Subroutine returns by jumping to $31
1
2
x1
after1
First call

## Slide 33: Jump-and-Link / Jump Register
after1
main:
jal myfn
after1:
add x1,x2,x3
jal myfn
after2:
sub x3,x4,x5
myfn:
…
…
jr x1
JAL saves the PC in register x1
Subroutine returns by jumping to x1
What happens for recursive invocations?
1
2
x1
after2
Second call
4
3

## Slide 34: JAL / JR for Recursion?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
if(n > 0) {
return n * myfn(n - 1);
} else {
return 1;
}
}

## Slide 35: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after1
First call

## Slide 36: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
Recursive Call
2
after1
after2

## Slide 37: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after2
Return from Recursive Call
2
3

## Slide 38: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
1
x1
after2
Return from Original Call???
2
3
4
Stuck!

## Slide 39: JAL / JR for Recursion?
main:
jal myfn
after1:
add x1,x2,x3
myfn:
if (test)
jal myfn
after2:
jr x1
Problems with recursion:
overwrites contents of x1
Need a way to save and restore register contents
1
x1
after2
Return from Original Call???
2
3
4
Stuck!

## Slide 40: Agenda
Function calls and Jumps
Call Stack
Register Convention
Program memory layout

## Slide 41: Takeaway2: Need a Call Stack
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register x1 (aka ra or return address) Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register x1
Need a Call Stack to return to correct calling procedure. To maintain a stack, need to store an activation record (aka a “stack frame”) in memory. Stacks keep track of the correct return address by storing the contents of x1 in memory (the stack).

## Slide 42: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register (x2) on the RISC-V
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up

## Slide 43: Stack Before, During, After Call
ra
Notes: Exact ordering of saved registers is up to you (make sure you keep track, though!).
(actually don’t need to save argument registers)

## Slide 44: Local Variables and Arrays
Any local variables the compiler cannot assign to registers will be allocated as part of the stack frame (Recall: spilling to memory)
Locally declared arrays and structs are also allocated as part of the stack frame
Stack manipulation is same as before
  Move sp down an extra amount and use the space it created as storage

## Slide 45: Function Call Example
int Leaf(int g, int h, int i, int j) {
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers a0, a1, a2, and a3, and f in s0
Assume need one temporary register s1

## Slide 46: RISC-V Code for Leaf()
Leaf: addi sp,sp,-8 # adjust stack for 2 items
sw s1, 4(sp) # save s1 for use afterwards
sw s0, 0(sp) # save s0 for use afterwards
add s0,a0,a1 # f = g + h
add s1,a2,a3 # s1 = i + j
sub a0,s0,s1 # return value (g + h) – (i + j)
lw s0, 0(sp) # restore register s0 for caller
lw s1, 4(sp) # restore register s1 for caller
addi sp,sp,8 # adjust stack to delete 2 items
jr ra # jump back to calling routine

## Slide 47: Stack Before, During, After Function
Need to save old values of s0 and s1
sp
Before call
sp
Saved s1
During call
Saved s0
sp
After call
Saved s1
Saved s0

## Slide 48: Agenda
Function calls and Jumps
Call Stack
Register Convention
Program memory layout

## Slide 49: Register Conventions
CalleR: the calling function
CalleE: the function being called
When callee returns from executing, the caller needs to know which registers may have changed and which are guaranteed to be unchanged.
Register Conventions: A set of generally accepted rules as to which registers will be unchanged after a procedure call (jal) and which may be changed.

## Slide 50: Basic Structure of a Function
func_label: addi sp,sp, -framesize sw ra, <framesize-4>(sp) save other regs if need be
restore other regs if need be lw ra, <framesize-4>(sp)
addi sp,sp, framesize jr ra
Epilogue
Prologue
Body (call other functions…)
ra
stack
...
$ra
$ra
...
Notes: Substitute the proper immediate for <framesize-4>.
Can order registers on stack however you want to, but must make sure to restore them properly.

## Slide 51: Using Stack to Backup Registers
Limited number of registers for everyone to use (limited desk space)
All functions use the same conventions -- look for arguments/return addresses in the same places
  What happens if a function calls another function?
  (ra would get overwritten!)
To reduce expensive loads and stores from spilling and restoring registers, RISC-V function-calling convention divides registers into two categories:

## Slide 53: Saved Registers
These registers are expected to be the same before and after a function call
  If calleE uses them, it must restore values before returning
  This means save the old values, use the registers, then reload the old values back into the registers
s0-s11 (saved registers)
sp (stack pointer)
  If not in same place, the caller won’t be able to properly restore values from the stack
ra (return address)
ra

## Slide 54: Volatile Registers
These registers can be freely changed by the calleE
  If calleR needs them, it must save those values before making a procedure call
t0-t6 (temporary registers)
a0-a7 (return address and arguments)
  These will change if calleE invokes another function (nested function means calleE is also a calleR)
$t
a

## Slide 55: Example: sumSquare
int sumSquare(int x, int y) {
return mult(x,x)+ y; }
What do we need to save?
  Call to mult will overwrite ra, so save it
  Reusing a1 to pass 2nd argument to mult, but need current value (y) later, so save a1
To save something to the Stack, move sp down the required amount and fill the “created” space
Notes: In general, you would also want to save $a0 to the Stack, in case the function you call calls another function can overwrites $a0.

## Slide 56: Example: sumSquare
  int sumSquare(int x, int y) { return mult(x,x)+ y; }
sumSquare:
addi sp,sp,-8 # make space on stack
sw ra, 4(sp) # save ret addr
sw a1, 0(sp) # save y
add a1,a0,x0 # set 2nd mult arg
jal mult # call mult
lw a1, 0(sp) # restore y
add a0,a0,a1 # ret val = mult(x,x)+y
lw ra, 4(sp) # get ret addr
addi sp,sp,8 # restore stack
jr ra
mult: ...
“push”
“pop”

## Slide 57: Choosing Your Registers
Minimize register footprint
  Optimize to reduce number of registers you need to save by choosing which registers to use in a function
  Only save when you absolutely have to
Function does NOT call another function
  Use only t0-t6 and there is nothing to save!
Function calls other function(s)
  Values you need throughout go in s0-s11, others go in t0-t6
  At each function call, check number arguments and return values for whether you or not you need to save
Notes: Recall: memory is MUCH slower than registers.
The more you know about the internals of the other functions you call, the more you can get away with (e.g. using temporary registers that you know the other functions don’t use, so you don’t bother saving them across function calls).

## Slide 58: Pros of Argument Passing Convention
Consistent way of passing arguments to and from subroutines
Creates single location for all arguments
  Caller makes room for a0-a7 on stack
  Callee must copy values from a0-a7 to stack
   callee may treat all args as an array in memory
  Particularly helpful for functions w/ variable length inputs: printf(“Scores: %d %d %d\n”, 1, 2, 3);
Aside: not a bad place to store inputs if callee needs to call a function (your input cannot stay in $a0 if you need to call another function!)

## Slide 59: Agenda
Function calls and Jumps
Call Stack
Register Convention
Program memory layout

## Slide 60
Stack contains stack frames (aka “activation records”)
  1 stack frame per dynamic function
  Exists only for the duration of function
Grows down, “top” of stack is sp, x2
Example: lw x5, 0(sp) puts word at top of stack into x5
Each stack frame contains:
  Local variables, return address (later), register
  backups (later)
int main(…) {
...
myfn(x);
}
int myfn(int n) {
...
myfn();
}
system reserved
stack
code
heap
system reserved
static data
myfn stack frame
myfn stack frame
main stack frame
$sp

## Slide 61: Frame Pointer
It is often cumbersome to keep track of location of data on the stack
  The offsets change as new values are pushed onto and popped off of the stack
Keep a pointer to the bottom of the top stack frame
  Simplifies the task of referring to items on the stack
A frame pointer, x8, aka fp/s0
  Value of sp upon procedure entry
  Can be used to restore sp on exit

## Slide 62: The Heap
Heap holds dynamically allocated memory
Program must maintain pointers to anything allocated
  Example: if x5 holds x
  lw x6, 0(x5) gets first word x points to
Data exists from malloc() to free()
void some_function() {
int *x = malloc(1000);
int *y = malloc(2000);
free(y);
int *z = malloc(3000);
}
system reserved
stack
X
Y
z
code
heap
system reserved
static data
1000 bytes
2000 bytes
3000 bytes

## Slide 63: Data Segment
Data segment contains global variables
  Exist for all time, accessible to all routines
Accessed w/global pointer
  gp, x3, points to middle of segment
  Example: lw x5, 0(gp) gets middle-most word
  (here, max_players)
int max_players = 4;
int main(...) {
...
}
gp
4
system reserved
stack
code
heap
system reserved
static data

## Slide 64
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
Where is i ?
Stack
Heap
Global Data
Text
Where is n ?
Stack
Heap
Global Data
Text
Where is main ?
Stack
Heap
Global Data
Text
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 65
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 66
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
i, m, sum, A
n, str
w/in function
function
invocation
stack
whole program
program
execution
.data
b/w malloc
and free
heap
Anywhere that
has a pointer
*A
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 67: Global and Locals
How does a function load global data?
  global variables are just above 0x10000000
Convention: global pointer
  x3 is gp (pointer into middle of global data section) gp = 0x10000800
  Access most global data using LW at gp +/- offset LW t0, 0x800(gp) LW t1, 0x7FF(gp)
Notes: # data at 0x10000000
# data at 0x10000FFF
(4KB range)

## Slide 68: Anatomy of an executing program
top
bottom
system reserved
stack
system reserved
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)
$gp

## Slide 69: Big Idea: Stored-Program Concept INSTRUCTIONS ARE DATA
WE CAN POINT TO THEM i.e., FUNCTION POINTERS
WE CAN MODIFY THEM ON THE FLY AS THE PROGRAM IS RUNNING (POST COMPILATION)

## Slide 70: 59084

## Slide 71: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
Implemented with:
  Jump table
  Indirect jump instruction
long switch_ex
(long x, long y, long z)
{
long w = 1;
switch (x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 72: Jump Table Structure
Code
Block 0
Targ0:
Code Block 1
Targ1:
Code Block 2
Targ2:
Code Block n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
JTab:
target = JTab[x];
goto target;
switch (x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 73: Jump Table Structure
switch (x) {
case 1: <some code>
break;
case 2: <some code>
case 3: <some code>
break;
case 5:
case 6: <some code>
break;
default: <some code>
}
Code
Blocks
Memory
Use the jump table when x 6:
if (x <= 6)
target = JTab[x];
goto target;
else
goto default;
C code:
0
1
2
3
4
5
6
Jump
Table

## Slide 74: Jump Table
.section .rodata
.align 8
.L4:
.quad .L8 # x = 0
.quad .L3 # x = 1
.quad .L5 # x = 2
.quad .L9 # x = 3
.quad .L8 # x = 4
.quad .L7 # x = 5
.quad .L7 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L5
w = y/z;
/* Fall Through */
case 3: // .L9
w += z;
break;
case 5:
case 6: // .L7
w -= z;
break;
default: // .L8
w = 2;
}
declaring data, not instructions
8-byte memory alignment
this data is 64-bits wide
Notes: .rodata – read-only data section

## Slide 75: SMC Demo

## Slide 76: 84159