## Slide 1: Caches and Memory Hierarchy
CMPT 295 Week 7

## Slide 2: Aside: Registers are Inside the Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 3: Processor-Memory Gap
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Notes: How fast you can crunch stuff
How fast you can get stuff

## Slide 4: C Loop Mapped to RISC-V Assembly
int A[20];
int sum = 0;
for (int i=0; i < 20; i++)
sum += A[i];
add s1, s0, x0 # a1=&A[0]
add a0, x0, x0 # sum=0
add a1, x0, x0 # i=0
addi a3,x0, 20 # a3=20
Loop:
bge a1,a3,Done
slli t0,a1,2 # i*4
addi t0,s1,t0 # &A[0]+i*4
lw a2, 0(t0) # a2=A[i]
add a0, a0, a2 # sum+=
addi a1, a1, 1 # i++
j Loop
Done:

## Slide 5
for(i=0;i < 4)
sum += A[i]
for(i=0;i < 4)
sum += var

## Slide 6
for (i = 0; i < 4){
for(j = 0; < 4) {
A[i][j]
for (i = 0; i < 4){
for(j = 0; < 4) {
A[j][i]
52 microseconds
253 microseconds

## Slide 7: Two-Dimensional (Nested) Arrays
• • •
A
[0]
[0]
A
[0]
[C-1]
• • •
A
[1]
[0]
A
[1]
[C-1]
• • •
A
[R-1]
[0]
A
[R-1]
[C-1]
• • •
4*R*C bytes
A[0][0]
A[0][C-1]
A[R-1][0]
• • •
• • •
A[R-1][C-1]
•
•
•
•
•
•
Notes: Memory is linear

## Slide 8: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Problem: lots of waiting on memory
Notes: What is a cycle
Only 2 hard problems in computer science: cache invalidation, naming things, and off-by-one errors.
I can process avocados very quickly
It takes me a long time to get them

## Slide 9: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Solution: caches
Smaller memories, closer to CPU → faster
Cache
Notes: Avocado cache

## Slide 10: Block based access from main memory
Main Memory (64bytes, 16 blocks)
Block Number (4 bits)
2 bits
bits
bits
Byte Number (6 bits for 64 byte memory)

## Slide 11: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Larger, slower, cheaper memory.
Viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive memory
Caches a subset of the blocks
Note: Cache “blocks” can also be referred to as cache “lines”

## Slide 12: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request BLOCK(Address): 14
14
Block b is in cache:
Hit!
Data is returned to CPU
CPU. Lw/sw address.

## Slide 13: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is returned to CPU
CPU

## Slide 14: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
How do caches take advantage of this?
block
block
Notes: Near

## Slide 15: Example: Any Locality?
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in stride-1 pattern
Instructions:
  Temporal: Cycle through loop repeatedly
  Spatial: Reference instructions in sequential order
sum = 0;
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 16: What Impacts Cache Hits/Misses?
Access Pattern
for (i = 0; i < 8; i++) vs. for (i = 0; i < 8; i=i+2)
Data layout
int a[8] vs. short a[8]
int a[8] vs. int a[16]
Cache Geometry
Direct mapped vs. Set Associative (more later..)

## Slide 17: DEMO

## Slide 18: Int. Stride 1
// Block size 64 bytes
int a[8];
for (i = 0; i < 8; i++) {
tmp = a[i];
Number of elements per block = 64/4 = 16
Hit:Access = 7:8 (Hit Rate)
Miss:Access = 1:8 (Miss Rate)
If we change loop to “i<16” and change array definition to int a[16], how would hit rate change?

## Slide 19: Short Stride 1
// Block size 64 bytes
short a[20];
for (i = 0; i < 20; i++) {
tmp = a[i];
Number of elements per block = 64/2 = 32
Hit:Access = 19:20
Miss:Access = 1:20

## Slide 20: Int Stride 2
// Block size 64 bytes
int a[16];
for (i = 0; i < 16; i=i+2) {
tmp = a[i];
Number of elements per block = 64/4 = 16
Accessed Elements per block = 16/2 = 8
Hit:Access = 7:8
Miss:Access = 1:8

## Slide 21: Caching Basics
Caching in general
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate storage levels used to optimize data transfers between any system elements with different characteristics
Cache Performance
  Ideal case: found in cache (hit)
  Bad case: not found in cache (miss), search in next level
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt by Miss Rate and Miss Penalty

## Slide 22: Tiled
for (i = 0; i < 2; i++)
for (j = 0; j < 2; j++)
for (ii = 0; ii < 4; ii++)
for (jj = 0; jj < 4; jj++)
A[i*2+ii][j*2+jj]

## Slide 23
for (i = 0; i < 5; i++) {
for (j = 0; j < 5; j++){
tmp[i][j] = 1.5*a[i,j];
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++){
b[i][j] = tmp[i,j]+
tmp[i+1,j]+
tmp[i,j+1]+
tmp[i+1,j+1]
Producer
Consumer
Consumer
Loads: 64
Stores: 16
Add : 48
Producer
Loads: 25
Stores: 25
Mul : 25

## Slide 24
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++){
b[i][j] = 1.5*tmp[i,j]+
1.5*tmp[I+1,j]+
1.5*tmp[i,j+1]+
1.5*tmp[I+1,j+1]
Fused
Loads: 64
Stores: 16
Mul : 64

## Slide 25
Tiled Producer-Consumer

## Slide 26: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %t1, %t2)
Smaller,
faster,
more expensive
per byte
program sees “memory”;
hardware manages caching
transparently

## Slide 27: Example Cache Hierarchy
Regs
L1 D$
L1 I$
L2 unified cache
Core 0
Regs
L1 D$
L1 I$
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
Block size: 64 bytes for all caches
L1 I-cache and D-cache:
  32 KiB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KiB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MiB, 16-way,
  Access: 30-40 cycles
Notes: i$ d$

## Slide 28: Cache Performance
Time for a memory operation depends on cache parameters:
  Hit time: Time to access cache on a cache hit
  Miss rate: Average misses per memory instruction
  Miss Penalty: Time to get data after a miss
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
99% hit rate can be twice as good as 97% hit rate!
  Assume HT of 1 ns and MP of 100 ns
  97%: AMAT = 1 + 0.03 x 100 = 4 ns
  99%: AMAT = 1 + 0.01 x 100 = 2 ns

## Slide 29: Can we have more than one cache?
Why?
  Avoid going to memory, reduce miss penalty
Typical performance numbers:
  Miss Rate
    L1 MR = 3-10%
    L2 Global MR = Quite small (e.g. < 1%), depending on parameters, etc.
    L2 (Local) MR typically larger than L1 MR (filtered by L1 hits)
  Hit Time
    L1 HT = 4 clock cycles
    L2 HT = 10 clock cycles
  Miss Penalty
    MP = 50-200 cycles for missing in L2 & going to main memory
    Trend: increasing!

## Slide 30: Internal Cache Organization
We want to store data efficiently in the cache.
We also need to quickly find data in the cache when we need it.
Address Splitting:
  Determine where data goes in the cache.
  Check if the data is already in the cache.
  Access the exact piece of data we need.

## Slide 31: Cache Organization
Block Size (): Unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
  Exact byte within a block of data.
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
Block Number = (address) mod (Block Size)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits

## Slide 32: Block based Addressing vs Byte Addressing
Main Memory (64bytes, 16 blocks)
Block Number (4 bits)
2 bits
bits
bits
Byte Number (6 bits for 64 byte memory)

## Slide 33: How to identify different blocks in cache?
for i = 0 to N
Calculate(A[i])
i = 0 – 0x000000 Block: 0000
i = 1 - 0x000004 Block: 0001
i = 2 - 0x000008 Block: 0002
……………
Main Memory (64bytes, 16 blocks)
Cache (16 bytes, 4 blocks)
Block size: 4B
Cache size: 16B

## Slide 34: Mapping Memory Address to Cache
CPU sends load/store address, address breakdown:
  Set Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  k = log2(K); s = log2(C/(K*E)); t = m - s - k
  K: Block Size (bytes), E: Associativity; C: Cache Size (bytes)
Book Shelf Analogy
  Block: page within a book
  Set Index: Which shelf took look at
  Tag: Unique QRcode or Barcode for every book
Tag ()
Offset ()
-bit address:
Block Number
Set ()
Think of this as similar to a bookshelf with multiple sections. The set index tells you which section of the shelf you should look in.

## Slide 35: Tags Differentiate Blocks in Cache
Offset bits = log2(K)
Set index bits s = log2(#Sets) = log2(C/(K*E))
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
0000
0100
1010
1111
Block size (K) = 4B
Associativity (E) = 1
Cache size (C) = 16B
#Blocks = C/K = 4
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 36: Cache Organization
  Cache Size = #Blocks x Block Size
  = #Sets x Associativity x Block Size
Block |  |  | 
Sets
Ways (i.e., associativity, #blocks/set)
Tag ()
Offset ()
Set ()
Match ==

## Slide 37: Tags Differentiate Blocks in Same Index
Offset bits = log2(K) = 2
Set index bits s = log2(#Sets) = 2
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 38: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Set | Tag | Data
0 |  | 
Fully associative
= 0
Notes: 38
k = 4
E = 1; s = 3; idx = 3. s : number of bits. Idx: actual value.
E = 2; s = 2; idx = 3
E = 4; s = 1; idx = 1
E =8; s = 0; idx = 0

## Slide 39: Cache Read
0
1
2
K-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 40: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 41: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 42: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 43: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B
Notes: 1 fewer s bit, 2x fewer sets

## Slide 44: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 45: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B

## Slide 46: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid) and sum is stored in a register, calculate the miss rate:
  = 12 bits, = 256 B, = 32 B, = 2
#define SIZE 8
long ar[SIZE][SIZE], sum = 0; // &ar=0x800
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += ar[i][j];
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)

## Slide 47: Row Major
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[i][j]
Cache: 256 bytes. 16x256 image
Hits: N-1 (N: number of elements per block)
Misses: 1024

## Slide 48
Access Pattern:
stride = ?
M = 3, N=4
76
92
108
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Notes: Stride of 1 (4 bytes)

## Slide 49: Column Major
Cache: 256 bytes. 16x256 image
Hits: 0
Misses: 4096
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[j][i]

## Slide 50
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
M = 3, N=4
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
Access Pattern:
stride = ?
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Notes: Stride of 4

## Slide 51: Cache Organization
  Cache Size = #Blocks x Block Size
  = #Sets x Associativity x Block Size
Block |  |  | 
Sets
Ways (i.e., associativity, #blocks/set)
Tag ()
Offset ()
Set ()
Match ==

## Slide 52: Peer Instruction Question
We have a cache of size 2 KiB with block size of 128 B. If our cache has 2 sets, what is its associativity?
2
4
8
16
We’re lost…
If addresses are 16 bits wide, how wide is the Tag field?
Notes: C = 2^11 B
K = 2^7 B
2^4 = 16 blocks
16 / 2 = 8 E
k = 7; s = 1; t = 16 – 7 – 1 = 8

## Slide 53: Other Questions
We have a cache with block size of 128 B. Cache is 4-way set-associative and has 8 sets. How big is the cache? (What is the cache capacity)?

## Slide 54: Other Questions
A 4KB Cache is 4-way set associative with 64 B blocks. Which bits are used for set index? (Also: How many sets does the cache have?)

## Slide 55: Other Questions
A 32KB Cache is 8-way set associative and has 16 sets. Which bits are used for byte offset? (Also: What is the block size?)

## Slide 56: Other Questions
A direct-mapped cache uses 4 bits for set index and 6 bits for byte offset. How big is the cache?

## Slide 57: Cache Miss Classification: The 3Cs
Compulsory: (Many names: cold start, process migration (switching processes), 1st reference)
  First access to block impossible to avoid; Effect is small for long running programs
Capacity:
  Cache cannot contain all blocks accessed by the program, i.e., misses in a fully associative cache.
Conflict: (collision)
  Multiple memory locations mapped to the same cache set (not enough associativity)

## Slide 58: Hit, Compulsory, Capacity or Conflict Miss
• 0x00000004
• 0x00000005 • 0x00000068
• 0x000000C8
• 0x00000068
• 0x000000DD
• 0x00000045
• 0x00000004
• 0x000000C8
Assume we have a direct-mapped byte-addressed cache with capacity 32B and block size of 8B.

## Slide 59: Hit, Compulsory, Capacity or Conflict Miss
• 0x00000004, Compulsory
• 0x00000005 • 0x00000068, Compulsory
• 0x000000C8, Compulsory
• 0x00000068
• 0x000000DD, Compulsory
• 0x00000045, Compulsory
• 0x00000004
• 0x000000C8

## Slide 60: Hit, Compulsory, Capacity or Conflict Miss
• 0x00000004, Compulsory
• 0x00000005 • 0x00000068, Compulsory
• 0x000000C8, Compulsory
• 0x00000068
• 0x000000DD, Compulsory
• 0x00000045, Compulsory
• 0x00000004, Capacity
• 0x000000C8, Capacity

## Slide 61: Hit, Compulsory, Capacity or Conflict Miss
• 0x00000004, Compulsory
• 0x00000005, Hit • 0x00000068, Compulsory
• 0x000000C8, Compulsory
• 0x00000068
• 0x000000DD, Compulsory
• 0x00000045, Compulsory
• 0x00000004, Capacity
• 0x000000C8, Capacity

## Slide 62: Hit, Compulsory, Capacity or Conflict Miss
• 0x00000004, Compulsory
• 0x00000005, N/A • 0x00000068, Compulsory
• 0x000000C8, Compulsory
• 0x00000068, Conflict
• 0x000000DD, Compulsory
• 0x00000045, Compulsory
• 0x00000004, Capacity
• 0x000000C8, Capacity

## Slide 63: Cache Code Analysis Problem
Cache-A Direct-mapped, 4KB, 64 sets
Cache-B Set-associative, 4KB, 2 ways, 32 sets
int size = 4096; // int is 4 bytes
int a[size];
long long int a_long[size]; // long long int is 8 bytes
/* loop 1 */
for (int i = 0; i < size; i++) {
a[i] = i;
}
/* loop 2 */
for (long long int i = 0; i < size; i++) {
a_long[i] = i;
}
/* loop 3 */
for (int i = 0; i < size/2; i += 1) {
a[(size/2)+i] = a[i];
}
Question: What are hit rates for loop1, loop 2 (assume loop 1 has run), loop3 (assume both previous loops have run).
Notes: k = 6 bits
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)