## Slide 1: Black Box Architecture
A black box is employed to abstract the function of a device.
Notation:
values of 0 / 1 travel along wires (lines)
arrows indicate direction of travel
there are inputs and outputs
input x
input y
output z
OR gate
z = x | y
Also:
AND
XOR
After a change in inputs, there is a time delay for outputs
≕ propagation delay (tpd)
on a picosecond to nanosecond scale
find longest distance from inputs to outputs

## Slide 2: Mystery Circuit : Full Adder
S = A ⊕ B ⊕ C; C = AB + C(A ⊕ B)
0
1
1
0
1
0
0
1
function table:
  basically a truth table
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
1
1
1
3-bit
Addition!
A
B
C
Q. What’s the propagation delay?
C
S
3 gate delays (highlighted)
Q. What does the circuit accomplish?
algebra:
S = A ^ B ^ C
; C = (A & B) | (C & (A ^ B))
S = A ⊕ B ⊕ C
C S
Full Adder
Half Adder
Half Adder
FA
S
C
C
A
B

## Slide 3: Computing with Combinational Circuits
Definition: A combinational circuit computes a pure function, i.e., its outputs react only based on its inputs. There are no feedback loops and no state information (memory) is maintained.
Theorem: Every Boolean function can be implemented with NAND and NOT. Circuits are modular
FA
FA
FA
FA
A3
B3
A2
B2
A1
B1
A0
B0
S3
S2
S1
S0
C3
C2
C1
C0
C4
… a 4-bit ripple carry adder!
  adds by columns
  propagation delay
= 9
(2n + 1)
Adder-4
A
B
4
4
4
S
C
C
Notes: Orally: We used to spend ⅔ of CMPT 150 on the design techniques to minimize circuit size, gate delay, etc …
The point in CMPT 295 is only that it is possible to do so, and that gate delay is a thing
Orally: This is why additions is slow. And why mul is even slower.
Orally: How to make an Adder-8?

## Slide 4: Function Unit
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A + 1
1101 B
32
Hardware circuits are fixed
can’t adjust wires / gates while running
build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:

## Slide 5: Function Unit: Adder-Subtractor
32
Adder-32
32
32
A
32
B
S
C
FS
if FS == 0 then
S = A + B
if FS == 1 then
= A − B
S = A + B + 1

## Slide 6: Digital State Machines
Memory holds state information
memory
combinational
circuit
current
state
inputs
next state
outputs
compute next state based on (current state, inputs)
compute outputs based on (current state, inputs)
Q. What does this imply about the clock period?
clock period must exceed (tpd of combinational circuit + tpd of registers)

## Slide 7: CPU Hardware
Goal: Given an instruction set architecture, construct a machine that reliably executes instructions.
Design choices will influence speed of instructions:
some instructions will be faster than others
order of instructions may matter
order of memory accesses may matter
“conflicts” or “hazards”

## Slide 8: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 9: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register

## Slide 10: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one.

## Slide 11: RISC-V CPU Datapath, Control Intro
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 12: Design Principles
Five steps to design a processor:
  Analyze instruction set → datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 13: Summary !
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF (Instruction Fetch), ID (Instruction Decode), EX (Execute), MEM (Memory), WB (Write Back)
  Not all instructions are active in all phases (except for loads!)
Controller specifies how to execute instructions
  Worth thinking about: what new instructions can be added with just most control?

## Slide 14: Your CPU in two parts
Central Processing Unit (CPU):
  Datapath: contains the hardware necessary to perform operations required by the processor
    Reacts to what the controller tells it! (ie. “I was told to do an add, so I”ll feed these arguments through an adder)
  Control: decides what each piece of the datapath should do
    What operation am I performing? Do I need to get info from memory? Should I write to a register? Which register?
    Has to make decisions based on the input instruction only!

## Slide 15: Design Principles
Determining control signals
  Any time a datapath element has an input that changes behavior, it requires a control signal (e.g. ALU operation, read/write)
  Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector (e.g. next PC, ALU input, register to write to)
Your control signals will change based on your exact datapath
Your datapath will change based on your ISA

## Slide 16: Storage Element: Register File
Register File consists of 31 registers:
  Output ports portA and portB
  Input port portW
Register selection
  Place data of register RA (number) onto portA
  Place data of register RB (number) onto portB
  Store data on portW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK is passed to all internal registers so they can be written to if they match RW and Write Enable is 1
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 17: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
(4) Perform operation
New hardware: ALU (Arithmetic Logic Unit)
Abstraction for adders, multipliers, dividers, etc.
How do we know what operation to execute?
  Our first control bit! ALUSel(ect)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel
inst[31:0]

## Slide 18: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel

## Slide 19: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb

## Slide 20: Storage Element: Idealized Memory
Memory (idealized)
  One input port: Data In
  One output port: Data Out
Memory access:
  Read: Write Enable = 0, data at Address is placed on Data Out
  Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: Address valid → Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

## Slide 21: Current Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
ALU
mem
wb
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
BSel
ALUSel
MemRW
WBSel
wb
pc+4

## Slide 22: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”

## Slide 23: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb

## Slide 24: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 25: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 26: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc

## Slide 27: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc