## Slide 1: YOUR CODE IS YOUR RESPONSIBILITY
DEBUGGING IS PART OF YOUR DUTY
NO PSEUDOCODE/CODE ON PIAZZA
e.g., my while loop does not work etc
https://www.cs.sfu.ca/~ashriram/Courses/CS295//policy.html#assignment-ta-help-policy
https://www.cs.sfu.ca/~ashriram/Courses/CS295//assignments.html#obtaining-help-from-tainstructor

## Slide 2: From Writing to Running
sum.c
sum.s
Compiler
C source
files
assembly
files
sum.o
Assembler
obj files
sum
Linker
executable
program
Executing
in
Memory
loader
process
exists on
disk
When most people say “compile” they mean
the entire process:
compile + assemble + link
“It’s alive!”
gcc -S
gcc -c
gcc -o
Notes: C compiler produces assembly files (contain RISCV assembly, pseudo-instructions, directives, etc.)
RISCV assembler produces object files (contain RISCV machine code, missing symbols, some layout information, etc.)
RISCV linker produces executable file (contains RISCV machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 3: Which statement runs faster ?
int foo2() {
return a+b;
}
int foo3() {
return a+b+c;
}

## Slide 4: Which statement runs faster ?
c = ( a + b ) OR c = ( a + b ) + d
c = a + b OR c = a[i] + b[i]
c = a[i] + b[i] OR c = a[c[i]] + a[c[i]]

## Slide 5: Registers -- Summary
In high-level languages, number of variables limited only by available memory
ISAs have a fixed, small number of operands called registers
  Special locations built directly into hardware
  Benefit: Registers are EXTREMELY FAST (faster than 1 billionth of a second)
  Drawback: Operations can only be performed on these predetermined number of registers
Notes: Registers visible to compiler (or RISCV programmer).

## Slide 6: Aside: Registers are Inside the Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 7: Memory vs. Registers
Addresses vs. Names
  0x7FFFD024C3DC %x0
Big vs. Small
  ~ 8 GiB (16 x 8 B) = 128 B
Slow vs. Fast
  ~50-100 ns sub-nanosecond timescale
Dynamic vs. Static
  Can “grow” as needed fixed number in hardware while program runs

## Slide 8: RISC V Integer Registers – 32 bits wide
Notes: Names are largely arbitrary, reasons behind them are not super relevant to us
But there are conventions about how they are used
One is particularly important to not misuse: %sp
  Stack pointer; we’ll get to this when we talk about procedures
Each is 4-bytes wide
What if we only want 4 bytes?
  We can use these alternate names to use just half of the bytes

## Slide 9: RISCV Instructions (1/2)
Instruction Syntax is rigid:
op dst, src1, src2
  1 operator, 3 operands
    op = operation name (“operator”)
    dst = register getting result (“destination”)
    src1 = first register for operation (“source 1”)
    src2 = second register for operation (“source 2”)
Keep hardware simple via regularity

## Slide 10: RISCV Instructions Example
Your very first instructions! (assume here that the variables a, b, and c are assigned to registers s1, s2, and s3, respectively)
Integer Addition (add)
  C: a = b + c
  RISCV: add s1, s2, s3
Integer Subtraction (sub)
  C: a = b - c
  RISCV: sub s1, s2, s3

## Slide 11: C example 1
Ordering of instructions matters (must follow order of operations)
Utilize temporary registers
Suppose a → s0,b → s1,c → s2,d → s3 and e → s4. Convert the following C statement to RISCV:
a = (b + c) - (d + e);
add t1, s3, s4
add t2, s1, s2
sub s0, t2, t1
Notes: add s0, s1, s2
add t0, s3, s4
sub s0, s0, t0
Suppose a -> s0, b->s1, c-> s2, d->s3 and e->s4. Convert the following C statement to RISCV:
a = (b + c) - (d + e);
add t1, s3, s4
add t2, s1, s2
sub s0, t2, t1

## Slide 12: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic operation on register or memory data
  c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
    Remember: Memory is indexed just like an array of bytes!

## Slide 13: Addition and Subtraction of Integers (3/4)
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add x10, x1, x2 # a_temp = b + c
  add x10, x10, x3 # a_temp = a_temp + d
  sub x10, x10, x4 # a = a_temp - e
Notice: A single line of C may break up into several lines of RISC-V.
Notice: Everything after the hash mark on each line is ignored (comments). Check Apollo-11 comments!

## Slide 14: Addition and Subtraction of Integers (4/4)
How do we do this?
  f = (g + h) - (i + j);
Use intermediate temporary register
  add x5, x20, x21 # a_temp = g + h
  add x6, x22, x23 # b_temp = i + j
  sub x19, x5, x6 # f = (g + h)- (i + j)

## Slide 15: C example 2
Since second operand is a literal value, no need to use separate register.
Suppose a → s0,e → s4. Convert the following C statement to RISCV:
e = (a + 10);
addi s4, s0, 10
Notes: add s0, s1, s2
add t0, s3, s4
sub s0, s0, t0
Suppose a -> s0, b->s1, c-> s2, d->s3 and e->s4. Convert the following C statement to RISCV:
a = (b + c) - (d + e);
add t1, s3, s4
add t2, s1, s2
sub s0, t2, t1

## Slide 16: Immediates
Numerical constants are called immediates
Separate instruction syntax for immediates:
opi dst, src, imm
  Operation names end with ‘i’, replace 2nd source register with an immediate
Example Uses:
  addi s1, s2, 5 # a=b+5
  addi s3, s3, 1 # c++
Why no subi instruction?
Notes: Goal of RISC is to minimize instruction set. subi dst, src, imm = addi dst, src, -imm.

## Slide 17: Data Transfer: Load from and Store to memory
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data = Store to memory
Read Data = Load from
memory
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Much larger place
To hold values, but slower than registers!
Fast but limited place
To hold values

## Slide 18: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 Bytes)
  Memory (DRAM): Billions of bytes (2 GB to 64 GB on laptop)
and physics dictates…
  Smaller is faster
How much faster are registers than DRAM??
  About 100-500 times faster! (in terms of latency of one access)

## Slide 19: C Example 3: Load Memory to Register
C code
int A[100];
g = h + A[3];
Using Load Word (lw) in RISC-V:
lw x10,12(x15) # Reg x10 gets A[3]
add x11,x12,x10 # g = h + A[3]
Note: x15 – base register (pointer to A[0])
12 – offset in bytes
Offset must be a constant known at assembly time
Data flow

## Slide 20: C Example 4: Store Register to Memory
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in RISC-V:
lw x10,12(x15) # Temp reg x10 gets A[3]
add x10,x12,x10 # Temp reg x10 gets h + A[3]
sw x10,40(x15) # A[10] = h + A[3]
Note: x15 – base register (pointer)
12,40 – offsets in bytes
x15+12 and x15+40 must be multiples of 4
Data flow
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 21: Loading and Storing Bytes
In addition to word data transfers (lw, sw), RISC-V has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb x10,3(x11)
  contents of memory location with address = sum of “3” + contents of register x11 is copied to the low byte position of register x10.
byte loaded
zzz zzzz
x
This bit
…is copied to “sign-extend”
xxxx xxxx xxxx xxxx xxxx xxxx
x10:
RISC-V also has “unsigned byte” loads (lbu) which zero extends to fill register. Why no unsigned store byte sbu?

## Slide 22: RISCV Agenda
Basic Arithmetic Instructions
Comments
x0 (zero)
Immediates
Data Transfer Instructions
Decision Making Instructions
Bonus: C to RISCV Practice
Bonus: Additional Instructions

## Slide 23: Decision Making Instructions
Branch If Equal (beq)
  beq reg1,reg2,label
  If value in reg1 = value in reg2, go to label
Branch If Not Equal (bne)
  bne reg1,reg2,label
  If value in reg1 ≠ value in reg2, go to label
Jump (j)
  j label
  Unconditional jump to label

## Slide 24: C Example 5: If Else
C Code:
if(i==j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
RISCV (beq):
# i→s0, j→s1
# a→s2, b→s3
beq s0,s1,then
else:
sub s2, x0, s3
j end
then:
add s2, s3, x0
end:
???
This label unnecessary
???

## Slide 25: Breaking Down the If Else
C Code:
if(i==j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
RISCV (bne):
# i→s0, j→s1
# a→s2, b→s3
bne s0,s1,else
then:
add s2, s3, x0
j end
else:
sub s2, x0, s3
end:
???
???

## Slide 26: Branching on Conditions other than (Not) Equal
Set Less Than (slt)
  slt dst, reg1,reg2
  If value in reg1 < value in reg2, dst = 1, else 0
Set Less Than Immediate (slti)
  slti dst, reg1,imm
  If value in reg1 < imm, dst = 1, else 0

## Slide 27: Breaking Down the If Else
C Code:
if(i<j) {
a = b /* then */
} else {
a = -b /* else */
}
In English:
If TRUE, execute the THEN block
If FALSE, execute the ELSE block
RISCV (???):
# i→s0, j→s1
# a→s2, b→s3
slt t0 s0 s1
beq t0,x0,else
then:
add s2, s3, x0
j end
else:
sub s2, x0, s3
end:
???
???

## Slide 28: C Loop Mapped to RISC-V Assembly
int A[20];
int sum = 0;
for (int i=0; i < 20; i++)
sum += A[i];
add x9, x8, x0 # x9=&A[0]
add x10, x0, x0 # sum=0
add x11, x0, x0 # i=0
addi x13,x0, 20 # x13=20
Loop:
bge x11,x13,Done
lw x12, 0(x9) # x12=A[i]
add x10,x10,x12 # sum+=
addi x9, x9,4 # &A[i+1]
addi x11,x11,1 # i++
j Loop
Done:

## Slide 29: C to RISCV Practice
Let’s put our all of our new RISCV knowledge to use in an example: “Fast String Copy”
C code is as follows:
/* Copy string from p to q */
char *p, *q;
while((*q++ = *p++) != ‘\0’) ;
What do we know about its structure?
  Single while loop
  Exit condition is an equality test

## Slide 30: C to RISCV Practice
Start with code skeleton:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # $t0 = *p
sb $t0,0($s1) # *q = $t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
# t0 = *p
# *q = t0
# p = p + 1
# q = q + 1
# if *p==0, go to Exit
# go to Loop

## Slide 31: C to RISCV Practice
Fill in lines:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb $t0,0($s0) # t0 = *p
sb $t0,0($s1) # *q = t0
addi $s0,$s0,1 # p = p + 1
addi $s1,$s1,1 # q = q + 1
beq $t0,$0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
lb t0,0(s0)
sb t0,0(s1)
addi s0,s0,1
addi s1,s1,1
beq t0,0,Exit

## Slide 32: C to RISCV Practice
Finished code:
# copy String p to q
# p→$s0, q→$s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
beq t0,x0,Exit # if *p==0, go to Exit
j Loop # go to Loop
Exit: # N chars in p => N*6 instructions
Notes: Is this the only way to write out this function? Of course not.

## Slide 33: C to RISCV Practice
Alternate code using bne:
# copy String p to q
# p→s0, q→s1 (pointers)
Loop: lb t0,0(s0) # t0 = *p
sb t0,0(s1) # *q = t0
addi s0,s0,1 # p = p + 1
addi s1,s1,1 # q = q + 1
bne t0,x0,Loop # if *p!=0, go to Loop
# N chars in p => N*5 instructions
Notes: Used fewer instructions!
Instead of “exit when equal to zero”, we are now using “loop when not equal to zero.”