## Slide 1: Data Structures in Assembly
Arrays
  One-dimensional
  Multi-dimensional (nested)
  Multi-level
Structs
  Alignment

## Slide 2: Array Accessing Example
int get_digit(zip_dig z, int digit){
return z[digit];
}
zip_dig sfu;
9
8
1
9
5
36
40
44
48
52
56
get_digit:
slli a1,a1,2
add a1,a0,a1
lw a0,0(a1)
ret
Register %a0 contains starting address of array
Register %a1 contains array index
Desired digit at %a0+4*%a1
typedef int zip_dig[5];
Notes: Array also explain funky memory addressing instructions

## Slide 3: Nested Array Element Access Code
int get_sea_digit (int index, int digit)
{
return sea[index][digit];
}
int sea[4][5] =
{{ 9, 8, 1, 9, 5 },
{ 9, 8, 1, 0, 5 },
{ 9, 8, 1, 0, 3 },
{ 9, 8, 1, 1, 5 }};
Notes: Asm is 3 steps
Compute row
Compute loctation in row
Access with scaling

## Slide 4: Element Access in Multi-Level Array
Computation
  Element access Mem[Mem[univ+8*index]+4*digit]
  Must do two memory reads
    First get pointer to row array
    Then access element within array
  But allows inner arrays to be different lengths (not in this example)
slli a0, a0, 3 # All registers are assumed to be 64 bit. a5 = &univ[0]
add a5,a5,a0
ld a5,0(a5) # 64 bit load. This is because univ is a pointer array.
slli a1,a1,2 # 4*digit
add a5,a5,a1 # univ[index]+4*digit
lw a0,0(a5) # 32 bit load
int get_univ_digit
(int index, int digit)
{
return univ[index][digit];
}
36
160
16
60
168
176
univ
cmu
sfu
ucb
1
5
2
1
3
16
20
24
28
32
36
9
8
1
9
5
36
40
44
48
52
56
9
4
7
2
0
60
64
68
72
76
80
Notes: Just two array reads

## Slide 5: Array Loop Example
Original:
Transformed:
  Eliminate loop variable i, use pointer zend instead
  Convert array code to pointer code
    Pointer arithmetic on z
  Express in do-while form (no test at entrance)
int zd2int(zip_dig z)
{
int zi = 0;
int *zend = z + 5;
do {
zi = 10 * zi + *z;
z++;
} while (z < zend);
return zi;
}
zip_dig sfu;
9
8
1
9
5
36
40
44
48
52
56
address just past
5th digit
Increments by 4 (size of int)
int zd2int(zip_dig z)
{
int i;
int zi = 0;
for (i = 0; i < 5; i++) {
zi = 10 * zi + z[i];
}
return zi;
}
Notes: 15au: With –Og, gcc will generate different code for each of these. With –O1, the same code.

## Slide 6: Array Loop Implementation
int zd2int(zip_dig z)
{
int zi = 0;
int *zend = z + 5;
do {
zi = 10 * zi + *z;
z++;
} while (z < zend);
return zi;
}
gcc with –O1
zd2int(int*): # @zd2int(int*)
a3=10,a4=20
mv a2, a0
add a4, a0, a4 # a4=zend
# a0 = Base address
# a2 = Loop variable
.LBB0_1: Loop
lw a5, 0(a2) # *z
mul a1, a1, a3 # 10 * zi
add a1, a1, a5 # 10 * zi + *z
addi a2, a2, 4 # increment pointer z++
bne a2, a4, .LBB0_1 # z < zend
add a0, zero, a1
ret