## Slide 1: Caches and Memory Hierarchy
CMPT 295 Week 7

## Slide 2: Processor-Memory Gap
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Notes: How fast you can crunch stuff
How fast you can get stuff

## Slide 3: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Problem: lots of waiting on memory
Notes: What is a cycle
Only 2 hard problems in computer science: cache invalidation, naming things, and off-by-one errors.
I can process avocados very quickly
It takes me a long time to get them

## Slide 4: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Solution: caches
Smaller memories, closer to CPU → faster
Cache
Notes: Avocado cache

## Slide 5: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Larger, slower, cheaper memory.
Viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive memory
Caches a subset of the blocks
Notes: Note: these are not bytes: blocks

## Slide 6: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Data is returned to CPU

## Slide 7: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is returned to CPU

## Slide 8: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
How do caches take advantage of this?
block
block
Notes: Near

## Slide 9: Example: Any Locality?
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in stride-1 pattern
Instructions:
  Temporal: cycle through loop repeatedly
  Spatial: reference instructions in sequence
sum = 0;
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 10
Access Pattern
for i = 0 to 8, i++ vs. for i = 0 to 8, i=i+2
Data layout
int a[8] vs. short a[8]
int a[8] vs. int a[16]
Cache Geometry
Direct mapped vs. Set Associative (more later..)

## Slide 11: Int. Stride 1
// Block size 64 bytes
int a[8];
for (i = 0; i < 8; i++) {
tmp = a[i]
Number of elements per block = 64/4 = 16
Hit:Access = 7:8 (Hit Rate)
Miss:Access = 1:8 (Miss Rate)
If we change loop to “i<16” and change array definition to int a[16], how would hit rate change?

## Slide 12: Short Stride 1
// Block size 64 bytes
short a[20];
for (i = 0; i < 20; i++) {
tmp = a[i]
Number of elements per block = 64/2 = 32
Hit:Access = 19:20
Miss:Access = 1:20

## Slide 13: Int Stride 2
// Block size 64 bytes
int a[16];
for (i = 0; i < 16; i=i+2) {
tmp = a[i]
Number of elements per block = 64/4 = 16
Accessed Elements per block = 16/2 = 8
Hit:Access = 7:8
Miss:Access = 1:8

## Slide 14
Caching in general
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate storage levels used to optimize data transfers between any system elements with different characteristics
Cache Performance
  Ideal case: found in cache (hit)
  Bad case: not found in cache (miss), search in next level
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt by Miss Rate and Miss Penalty

## Slide 15: Row Major
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[i][j]
Cache: 256 bytes. 16x256 image
Hits: N-1 (N: number of elements per block)
Misses: 1024

## Slide 16
Access Pattern:
stride = ?
M = 3, N=4
76
92
108
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Notes: Stride of 1 (4 bytes)

## Slide 17: Column Major
Cache: 256 bytes. 16x256 image
Hits: 0
Misses: 4096
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[j][i]

## Slide 18
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
M = 3, N=4
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
Access Pattern:
stride = ?
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Notes: Stride of 4

## Slide 19: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
99% hit rate can be twice as good as 97% hit rate!
  Assume HT of 1 clock cycle and MP of 100 clock cycles
  97%: AMAT =
  99%: AMAT =
Notes: AMAT = always have to pay HT, only sometimes (MR) pay MP
HR = .97 -> 1 + .03 * 100 = 4 cycles
HR = .99 -> 1 + .01 * 100 = 2 cycles
Since MP is high, keep MR loooow

## Slide 20: Can we have more than one cache?
Why would we want to do that?
  Avoid going to memory!
Typical performance numbers:
  Miss Rate
    L1 MR = 3-10%
    L2 Global MR = Quite small (e.g. < 1%), depending on parameters, etc.
    L2 (Local) MR typically larger than L1 MR (filtered by L1 hits)
  Hit Time
    L1 HT = 4 clock cycles
    L2 HT = 10 clock cycles
  Miss Penalty
    P = 50-200 cycles for missing in L2 & going to main memory
    Trend: increasing!
Notes: Smaller cache will have higher MR, lower HT
We have 3 levels now!

## Slide 21: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %t1, %t2)
Smaller,
faster,
costlier
per byte
program sees “memory”;
hardware manages caching
transparently
Notes: So, why haven’t we seen caches before now in this class?
  Because they’re designed to be architecturally transparent!
  Never affect correctness, only performance

## Slide 22: Intel Core i7 Cache Hierarchy
Regs
L1 D$
L1 I$
L2 unified cache
Core 0
Regs
L1 D$
L1 I$
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
Block size: 64 bytes for all caches
L1 i-cache and d-cache:
  32 KiB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KiB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MiB, 16-way,
  Access: 30-40 cycles
Notes: i$ d$

## Slide 23: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 24: Cache Organization (1)
Block Size (): Unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
  (address) modulo (# of bytes in a block)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits
Note: The textbook uses “b” for offset bits
Notes: Just like withinBlock() from Lab 1!
Little k (or b) for offset bits

## Slide 25: How to identify different blocks in cache?
for i = 0 to N
Calculate(A[i])
I = 0 – 0x000000 Block: 0000
I = 1 - 0x000004 Block: 0001
I = 1 - 0x000008 Block: 0002
……………
Main Memory (64bytes, 16 blocks)
Cache (16 bytes, 4 blocks)

## Slide 26: Tags Differentiate Blocks in Cache
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Here = 4 B
and = 4
0000
0100
1010
1111
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 27: Tags Differentiate Blocks in Same Index
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 28: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Set | Tag | Data
0 |  | 
Fully associative
= 0
Notes: 28
k = 4
E = 1; s = 3; idx = 3. s : number of bits. Idx: actual value.
E = 2; s = 2; idx = 3
E = 4; s = 1; idx = 1
E =8; s = 0; idx = 0

## Slide 29: Mapping Memory Address to Cache
CPU sends address request for chunk of data
Address breakdown:
  Index field tells you where to look in cache
  Tag field lets you check that data is the block you want
  Offset field selects specified start byte within block
  k = log2(K); s = log2(C/(K*E)); t = m - s - k
  K: Block Size (bytes), E: Associativity; C: Cache Size (bytes)
Tag ()
Offset ()
-bit address:
Block Number
Index ()
Notes: Tio = uncle in spanish
Go through steps
Why are they in this order?
Offset must be last
You want index to ”change fast” to minimize collision
If you swapped tag and index, adjacent blocks would collide (jump forward two slides)

## Slide 30: Cache Read
0
1
2
K-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 31: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 32: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 33: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 34: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B
Notes: 1 fewer s bit, 2x fewer sets

## Slide 35: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 36: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B

## Slide 37: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid) and sum is stored in a register, calculate the miss rate:
  = 12 bits, = 256 B, = 32 B, = 2
#define SIZE 8
long ar[SIZE][SIZE], sum = 0; // &ar=0x800
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += ar[i][j];
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)

## Slide 38: Sources of Cache Misses: The 3Cs
Compulsory: (Many names: cold start, process migration (switching processes), 1st reference)
  First access to block impossible to avoid; Effect is small for long running programs
Capacity:
  Cache cannot contain all blocks accessed by the program, so full associativity won’t hold all blocks
Conflict: (collision)
  Multiple memory locations mapped to the same cache location, so there is a lack of associativity

## Slide 39: Peer Instruction Question
We have a cache of size 2 KiB with block size of 128 B. If our cache has 2 sets, what is its associativity?
2
4
8
16
We’re lost…
If addresses are 16 bits wide, how wide is the Tag field?
Notes: C = 2^11 B
K = 2^7 B
2^4 = 16 blocks
16 / 2 = 8 E
k = 7; s = 1; t = 16 – 7 – 1 = 8

## Slide 40: Other Questions
We have a cache with block size of 128 B. Cache is 4-way set-associative and has 8 sets. How big is the cache? (What is the cache capacity)?
A 4KB Cache is 4-way set associative with 64 B blocks. Which bits are used for set index? (Also: How many sets does the cache have?)
A 32KB Cache is 8-way set associative and has 16 sets. Which bits are used for byte offset? (Also: What is the block size?)
A direct-mapped cache uses 4 bits for set index and 6 bits for byte offset. How big is the cache?