## Slide 1: Caches I
http://xkcd.com/1353/

## Slide 2: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Processor Pipeline
Performance
Parallelism

## Slide 3: How does execution time grow with SIZE?
int array[SIZE];
int sum = 0;
for (int i = 0; i < 200000; i++) {
for (int j = 0; j < SIZE; j++) {
sum += array[j];
}
}
SIZE
Time
Plot
Notes: What should we expect for this experiment?
Accessing and adding 200 000 x size times

## Slide 4: Actual Data
SIZE
Time
Notes: Knee in the curve
  After some size threshold
  Memory “wall”
Steeper slope = execution time grows faster
Fits in cache, doesn’t fit in cache

## Slide 5: How does execution time ROW vs COL?
ROW-wise
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += array[i][j];
COL-wise
for (int i = 0; i < SIZE; i++) {
for (int j = 0; j < SIZE; j++) {
sum += array[j][i];
}
}
Notes: What should we expect for this experiment?
Accessing and adding 200 000 x size times

## Slide 6: Actual Data
Time
Chart: 
| Row | Column
Series 1 | 191 | 1713
Notes: Knee in the curve
  After some size threshold
  Memory “wall”
Steeper slope = execution time grows faster
Fits in cache, doesn’t fit in cache

## Slide 7: How does execution time vary with stride?
for (int i = 0; i < SIZE; i+stride) {
sum += array[i];
}
Chart: 
| 1 | 2 | 3 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 1024
Step | 1 | 0.95 | 0.9 | 0.9 | 1 | 0.9 | 2 | 4 | 10 | 15 | 20

## Slide 8: Programs 101
Load/Store Architectures:
Read data from memory (put in registers)
Manipulate it
Store it back to memory
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf (“...”, n, sum);
}
C Code
main: addi sp,sp,-48
sw ra,44(sp)
sw fp,40(sp)
move fp,sp
sw a0,-36(fp)
sw a1,-40(fp)
la a5,n
lw a5,0(x15)
sw a5,-28(fp)
sw x0,-24(fp)
li a5,1
sw a5,-20(fp)
L2: lw a4,-20(fp)
lw a5,-28(fp)
blt a5,a4,L3
. . .
RISC-V Assembly
Instructions that read from
or write to memory…

## Slide 9: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
Program optimizations that consider caches

## Slide 10: Processor-Memory Gap
Processor-Memory
Performance Gap (grows 50%/year)
1989 first Intel CPU with cache on chip
1998 Pentium III has two cache levels on chip
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Notes: How fast you can crunch stuff
How fast you can get stuff

## Slide 11: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Core 2 Duo:
Can process at least
256 Bytes/cycle
Core 2 Duo:
Bandwidth
2 Bytes/cycle
Latency
100-200 cycles (30-60ns)
Problem: lots of waiting on memory
cycle: single machine step (fixed-time)
Notes: What is a cycle
Only 2 hard problems in computer science: cache invalidation, naming things, and off-by-one errors.
I can process avocados very quickly
It takes me a long time to get them

## Slide 12: Problem: Processor-Memory Bottleneck
Main Memory
CPU
Reg
Processor performance
doubled about
every 18 months
Bus latency / bandwidth
evolved much slower
Core 2 Duo:
Can process at least
256 Bytes/cycle
Core 2 Duo:
Bandwidth
2 Bytes/cycle
Latency
100-200 cycles (30-60ns)
Solution: caches
Cache
cycle: single machine step (fixed-time)
Notes: Avocado cache

## Slide 13: Cache 💰
Pronunciation: “cash”
  We abbreviate this as “$”
English: A hidden storage space for provisions, weapons, and/or treasures
Computer: Memory with short access time used for the storage of frequently or recently used instructions (i-cache/I$) or data (d-cache/D$)
  More generally: Used to optimize data transfers between any system elements with different characteristics (network interface cache, file cache, etc.)

## Slide 14: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Larger, slower, cheaper memory.
Viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive memory
Caches a subset of the blocks
Notes: Note: these are not bytes: blocks

## Slide 15: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Data is returned to CPU

## Slide 16: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Data is returned to CPU

## Slide 17: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently

## Slide 18: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
block
Notes: Equal

## Slide 19: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
How do caches take advantage of this?
block
block
Notes: Near

## Slide 20: Example: Any Locality?
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in stride-1 pattern
Instructions:
  Temporal: cycle through loop repeatedly
  Spatial: reference instructions in sequence
sum = 0;
for (i = 0; i < n; i++) {
sum += a[i];
}
return sum;

## Slide 21: Locality Example #1
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 22: Locality Example #1
Access Pattern:
stride = ?
M = 3, N=4
Note: 76 is just one possible starting address of array a
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
76
92
108
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
Notes: Stride of 1 (4 bytes)

## Slide 23: Locality Example #2
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 24: Locality Example #2
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
M = 3, N=4
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
Access Pattern:
stride = ?
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
Notes: Stride of 4

## Slide 25: Locality Example #3
What is wrong with this code?
How can it be fixed?
int sum_array_3D(int a[M][N][L])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < L; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}
a[2][0][0] |  | a[2][0][1] |  | a[2][0][2] |  | a[2][0][3]
a[2][1][0] |  | a[2][1][1] |  | a[2][1][2] |  | a[2][1][3]
a[2][2][0] |  | a[2][2][1] |  | a[2][2][2] |  | a[2][2][3]
a[1][0][0] |  | a[1][0][1] |  | a[1][0][2] |  | a[1][0][3]
a[1][1][0] |  | a[1][1][1] |  | a[1][1][2] |  | a[1][1][3]
a[1][2][0] |  | a[1][2][1] |  | a[1][2][2] |  | a[1][2][3]
a[0][0][0] |  | a[0][0][1] |  | a[0][0][2] |  | a[0][0][3]
a[0][1][0] |  | a[0][1][1] |  | a[0][1][2] |  | a[0][1][3]
a[0][2][0] |  | a[0][2][1] |  | a[0][2][2] |  | a[0][2][3]
m = 0
m = 1
m = 2
Notes: Grids, rows, cols
Stride = N * L

## Slide 26: Locality Example #3
int sum_array_3D(int a[M][N][L])
{
int i, j, k, sum = 0;
for (i = 0; i < N; i++)
for (j = 0; j < L; j++)
for (k = 0; k < M; k++)
sum += a[k][i][j];
return sum;
}
What is wrong with this code?
How can it be fixed?
Layout in Memory (M = ?, N = 3, L = 4)
a [0] [0] [0] | a [0] [0] [1] | a [0] [0] [2] | a [0] [0] [3] | a [0] [1] [0] | a [0] [1] [1] | a [0] [1] [2] | a [0] [1] [3] | a [0] [2] [0] | a [0] [2] [1] | a [0] [2] [2] | a [0] [2] [3]
a [1] [0] [0] | a [1] [0] [1] | a [1] [0] [2] | a [1] [0] [3] | a [1] [1] [0] | a [1] [1] [1] | a [1] [1] [2] | a [1] [1] [3] | a [1] [2] [0] | a [1] [2] [1] | a [1] [2] [2] | a [1] [2] [3]
76
92
108
124
140
156
172
Notes: Make J the inner loop

## Slide 27: Cache Performance Metrics
Huge difference between a cache hit and a cache miss
  Could be 100x speed difference between accessing cache and main memory (measured in clock cycles)
Miss Rate (MR)
  Fraction of memory references not found in cache (misses / accesses) = 1 - Hit Rate
Hit Time (HT)
  Time to deliver a block in the cache to the processor
    Includes time to determine whether the block is in the cache
Miss Penalty (MP)
  Additional time required because of a miss
Notes: Hit takes HT
Miss takes HT + MP

## Slide 28: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
99% hit rate can be twice as good as 97% hit rate!
  Assume HT of 1 clock cycle and MP of 100 clock cycles
  97%: AMAT =
  99%: AMAT =
Notes: AMAT = always have to pay HT, only sometimes (MR) pay MP
HR = .97 -> 1 + .03 * 100 = 4 cycles
HR = .99 -> 1 + .01 * 100 = 2 cycles
Since MP is high, keep MR loooow

## Slide 30: Peer Instruction Question
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT =
Which improvement would be best?
  190 ps clock
  Miss penalty of 40 clock cycles
  MR of 0.015 misses/instruction
Notes: C
AMAT = 1 + .02 * 50 = 2 cycles = 400 ps (trillionth!)
A -> 2 cycles -> 380 ps
B -> 1 + 0.02 * 40 = 1.8 cyc = 360ps
C 1 + 0.015 * 50 = 1.75 cyc = 350ps

## Slide 31: Can we have more than one cache?
Why would we want to do that?
  Avoid going to memory!
Typical performance numbers:
  Miss Rate
    L1 MR = 3-10%
    L2 MR = Quite small (e.g. < 1%), depending on parameters, etc.
  Hit Time
    L1 HT = 4 clock cycles
    L2 HT = 10 clock cycles
  Miss Penalty
    P = 50-200 cycles for missing in L2 & going to main memory
    Trend: increasing!
Notes: Smaller cache will have higher MR, lower HT
We have 3 levels now!

## Slide 33: Memory Hierarchies
Some fundamental and enduring properties of hardware and software systems:
  Faster = smaller = more expensive
  Slower = bigger = cheaper
  The gaps between memory technology speeds are widening
    True for: registers ↔ cache, cache ↔ DRAM, DRAM ↔ disk, etc.
  Well-written programs tend to exhibit good locality
These properties complement each other beautifully
  They suggest an approach for organizing memory and storage systems known as a memory hierarchy
    For each level k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1

## Slide 34: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
Smaller,
faster,
costlier
per byte
Notes: Implemented with different technologies!
  disks, solid-state
  DRAM: little wells that drain slowly, refreshed periodically
  SRAM: flip-flops, little logic gates that feedback with each other, faster but uses more power!
That’s why they’re different sizes and costs

## Slide 35: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %t1, %t2)
Smaller,
faster,
costlier
per byte
program sees “memory”;
hardware manages caching
transparently
Notes: So, why haven’t we seen caches before now in this class?
  Because they’re designed to be architecturally transparent!
  Never affect correctness, only performance

## Slide 36: Intel Core i7 Cache Hierarchy
Regs
L1 D$
L1 I$
L2 unified cache
Core 0
Regs
L1 D$
L1 I$
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
Block size: 64 bytes for all caches
L1 i-cache and d-cache:
  32 KiB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KiB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MiB, 16-way,
  Access: 30-40 cycles
Notes: i$ d$

## Slide 37: Summary
Memory Hierarchy
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate storage levels used to optimize data transfers between any system elements with different characteristics
Cache Performance
  Ideal case: found in cache (hit)
  Bad case: not found in cache (miss), search in next level
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt by Miss Rate and Miss Penalty