## Slide 1: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
7
9
14
3
Cache
Memory
Larger, slower, cheaper memory.
Viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive memory
Caches a subset of the blocks
Notes: Note: these are not bytes: blocks

## Slide 2: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
How do caches take advantage of this?
block
block
Notes: Near

## Slide 3
Access Pattern
for i = 0 to 8, i++. Vs for i = 0 to 8, i=i+2
Data layout
int a[8] vs short a[8]
int a[8] vs int a[16]
Cache Geometry
Direct mapped vs Set Associative (more later..)

## Slide 4: Int. Stride 1
// Block size 64 bytes
int a[8];
for (i = 0; i < 8; i++) {
tmp = a[i]
Number of elements per block = 64/8 = 8
Hit:Miss = 7:8

## Slide 5: Short Stride 1
// Block size 64 bytes
short a[8];
for (i = 0; i < 8; i++) {
tmp = a[i]
Number of elements per block = 64/8 = 8
Hit:Miss = 15:16

## Slide 6: Int Stride 2
// Block size 64 bytes
int a[8];
for (i = 0; i < 8; i=i+2) {
tmp = a[i]
Number of elements per block = 64/8 = 8
Hit:Miss = 3:4

## Slide 7
Caching in general
  Successively higher levels contain “most used” data from lower levels
  Exploits temporal and spatial locality
  Caches are intermediate storage levels used to optimize data transfers between any system elements with different characteristics
Cache Performance
  Ideal case: found in cache (hit)
  Bad case: not found in cache (miss), search in next level
  Average Memory Access Time (AMAT) = HT + MR × MP
    Hurt by Miss Rate and Miss Penalty

## Slide 8: Row Major
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[i][j]
Cache: 256 bytes. 16x256 image
Hits: N-1 (N: number of elements per block)
Misses: 1024

## Slide 9
Access Pattern:
stride = ?
M = 3, N=4
76
92
108
Layout in Memory
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
1) | a[0][0]
2) | a[0][1]
3) | a[0][2]
4) | a[0][3]
5) | a[1][0]
6) | a[1][1]
7) | a[1][2]
8) | a[1][3]
9) | a[2][0]
10) | a[2][1]
11) | a[2][2]
12) | a[2][3]
Notes: Stride of 1 (4 bytes)

## Slide 10: Column Major
Cache: 256 bytes. 16x256 image
Hits: 0
Misses: 4096
for (i = 0; i < 4; i++) {
for (j = 0; j < 4; j++) {
A[j][i]

## Slide 11
76
92
108
Layout in Memory
a [0] [0] | a [0] [1] | a [0] [2] | a [0] [3] | a [1] [0] | a [1] [1] | a [1] [2] | a [1] [3] | a [2] [0] | a [2] [1] | a [2] [2] | a [2] [3]
M = 3, N=4
a[0][0] |  | a[0][1] |  | a[0][2] |  | a[0][3]
a[1][0] |  | a[1][1] |  | a[1][2] |  | a[1][3]
a[2][0] |  | a[2][1] |  | a[2][2] |  | a[2][3]
Access Pattern:
stride = ?
1) | a[0][0]
2) | a[1][0]
3) | a[2][0]
4) | a[0][1]
5) | a[1][1]
6) | a[2][1]
7) | a[0][2]
8) | a[1][2]
9) | a[2][2]
10) | a[0][3]
11) | a[1][3]
12) | a[2][3]
Notes: Stride of 4

## Slide 12: Tiled
for (i = 0; i < 2; i++)
for (j = 0; j < 2; j++)
            for (ii = 0; ii < 2; ii++)
        for (jj = 0; jj < 2; jj++)
A[I*2+ii][j*2+jj]

## Slide 13
for (i = 0; i < 4; i++) {
for (j = 0; x < 4; x++){
tmp[i][j] = 1.5*a[i,j];
for (i = 0; i < 4; i++) {
for (j = 0; x < 4; x++){
b[i][j] = tmp[i,j]+
tmp[i+1,j]+
tmp[i,j+1]+
tmp[i+1,j+1]
Producer
Consumer
Consumer
Loads: 80
Stores: 32
Mul : 16

## Slide 14
for (i = 0; i < 4; i++) {
for (j = 0; x < 4; x++){
b[i][j] = 1.5*tmp[i,j]+
1.5*tmp[I+1,j]+
1.5*tmp[i,j+1]+
1.5*tmp[I+1,j+1]
Fused
Loads: 64
Stores: 16
Mul : 64

## Slide 15
Tiled Producer-Consumer
Loads: 48
Stores: 32
Mul : 16

## Slide 16: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
99% hit rate can be twice as good as 97% hit rate!
  Assume HT of 1 clock cycle and MP of 100 clock cycles
  97%: AMAT =
  99%: AMAT =
Notes: AMAT = always have to pay HT, only sometimes (MR) pay MP
HR = .97 -> 1 + .03 * 100 = 4 cycles
HR = .99 -> 1 + .01 * 100 = 2 cycles
Since MP is high, keep MR loooow

## Slide 17: Can we have more than one cache?
Why would we want to do that?
  Avoid going to memory!
Typical performance numbers:
  Miss Rate
    L1 MR = 3-10%
    L2 MR = Quite small (e.g. < 1%), depending on parameters, etc.
  Hit Time
    L1 HT = 4 clock cycles
    L2 HT = 10 clock cycles
  Miss Penalty
    P = 50-200 cycles for missing in L2 & going to main memory
    Trend: increasing!
Notes: Smaller cache will have higher MR, lower HT
We have 3 levels now!

## Slide 18: An Example Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(distributed file systems, web servers)
off-chip L2
cache (SRAM)
explicitly program-controlled (e.g. refer to exactly %t1, %t2)
Smaller,
faster,
costlier
per byte
program sees “memory”;
hardware manages caching
transparently
Notes: So, why haven’t we seen caches before now in this class?
  Because they’re designed to be architecturally transparent!
  Never affect correctness, only performance

## Slide 19: Making memory accesses fast!
Cache basics
Principle of locality
Memory hierarchies
Cache organization
  Direct-mapped (sets; index + tag)
  Associativity (ways)
  Replacement policy
  Handling writes
Program optimizations that consider caches
Notes: Divide addresses into “index” and “tag”

## Slide 20: Cache Organization (1)
Block Size (): unit of transfer between and Mem
  Given in bytes and always a power of 2 (e.g. 64 B)
  Blocks consist of adjacent bytes (differ in address by 1)
    Spatial locality!
Offset field
  Low-order bits of address tell you which byte within a block
    (address) mod = lowest bits of address
  (address) modulo (# of bytes in a block)
Block Number
Block Offset
-bit address:
(refers to byte in memory)
bits
bits
Note: The textbook uses “b” for offset bits
Notes: Just like withinBlock() from Lab 1!
Little k (or b) for offset bits

## Slide 21: How to identify different blocks in cache?
for i – 0 to N
alculate(A[i])
I = 0 – 0x000000 Block: 0000
I = 1 - 0x000004 Block: 0001
I = 1 - 0x000008 Block: 0002
……………
Main Memory (64bytes, 16 blocks)
Cache (16 bytes, 4 blocks)

## Slide 22: Tags Differentiate Blocks in Cache
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Here = 4 B
and = 4
0000
0100
1010
1111
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 23: Tags Differentiate Blocks in Same Index
Tag = rest of address bits
  bits =
  Check this during a cache lookup
Block Addr | Block Data |  |  | 
0000 |  |  |  | 
0001 |  |  |  | 
0010 |  |  |  | 
0011 |  |  |  | 
0100 |  |  |  | 
0101 |  |  |  | 
0110 |  |  |  | 
0111 |  |  |  | 
1000 |  |  |  | 
1001 |  |  |  | 
1010 |  |  |  | 
1011 |  |  |  | 
1100 |  |  |  | 
1101 |  |  |  | 
1110 |  |  |  | 
1111 |  |  |  | 
Memory
Cache
Index | Tag |  | Block Data |  |  | 
00 | 00 |  |  |  |  | 
01 |  |  |  |  |  | 
10 | 01 |  |  |  |  | 
11 | 01 |  |  |  |  | 
Here = 4 B
and = 4
Notes: Possible analogies for Tag:
Hash by first name, tag by last name
Hash by 7-digit phone number, tag by area code
Again, don’t memorize m – s – k

## Slide 24: Example Placement
Where would data from address 0x1833 be placed?
  Binary: 0b 0001 1000 0011 0011
= ?
block size: | 16 B
capacity: | 8 blocks
address: | 16 bits
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Direct-mapped
Set | Tag | Data
0 |  | 
1 |  | 
2 |  | 
3 |  | 
Set | Tag | Data
0 |  | 
1 |  | 
2-way set associative
4-way set associative
Tag ()
Offset ()
-bit address:
Index ()
=
=
= ––
= ?
= ?
Set | Tag | Data
0 |  | 
Fully associative
= 0
Notes: 24
k = 4
E = 1; s = 3; idx = 3. s : number of bits. Idx: actual value.
E = 2; s = 2; idx = 3
E = 4; s = 1; idx = 1
E =8; s = 0; idx = 0

## Slide 25: Cache Read
0
1
2
K-1
tag
v
bits
bits
bits
Address of byte in memory:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set is valid and has matching tag: hit
Locate data starting at offset
valid bit
= # sets
=
= blocks/lines per set
= bytes per block

## Slide 26: Example: Direct-Mapped Cache ( = 1)
Direct-mapped: One line per set
Block Size = 8 B
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
= sets

## Slide 27: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
block offset
Direct-mapped: One line per set
Block Size = 8 B

## Slide 28: Example: Direct-Mapped Cache ( = 1)
bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match?: yes = hit
valid? +
int (4 B) is here
block offset
No match? Then old line gets evicted and replaced
This is why we want alignment!
Direct-mapped: One line per set
Block Size = 8 B

## Slide 29: Example: Set-Associative Cache ( = 2)
bits
0…01
100
Address of short int:
find set
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
2-way: Two lines per set
Block Size = 8 B
Notes: 1 fewer s bit, 2x fewer sets

## Slide 30: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
compare both
valid? +
match: yes = hit
block offset
tag
2-way: Two lines per set
Block Size = 8 B
Address of short int:

## Slide 31: Example: Set-Associative Cache ( = 2)
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
bits
0…01
100
valid? +
match: yes = hit
block offset
short int (2 B) is here
No match?
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
compare both
Address of short int:
2-way: Two lines per set
Block Size = 8 B

## Slide 32: Example Code Analysis Problem
Assuming the cache starts cold (all blocks invalid) and sum is stored in a register, calculate the miss rate:
  = 12 bits, = 256 B, = 32 B, = 2
#define SIZE 8
long ar[SIZE][SIZE], sum = 0; // &ar=0x800
for (int i = 0; i < SIZE; i++)
for (int j = 0; j < SIZE; j++)
sum += ar[i][j];
Notes: k = 5 bits
256 / 32 = 8 blocks
8 / 2 = 4 sets
s = 2 bits
t = 12 – 5 – 2 = 5 bits
0x800 = 0b 1000 0000 0000
8 bytes per elem
4 longs fit in a block
¼ miss rate (missed are compulsory)