## Slide 1: Caches and Virtual Memory
CMPT 295 Week 8

## Slide 2: Processes
A process is an instance of a running program
  Provided by the OS
    OS uses a data structure (PCB) to represent each process
  Maintains the interface between the program and the underlying hardware (CPU + memory)
Process provides each program with two key abstractions:
  Logical control flow
    Each program seems to have exclusive use of the CPU
    Provided by kernel mechanism called context switching
  Private address space
    Each program seems to have exclusive use of main memory
    Provided by kernel mechanism called virtual memory
CPU
Registers
Memory
Stack
Heap
Code
Data

## Slide 3: What is a process?
Computer
Disk
/Applications/
Chrome.exe
Slack.exe
PowerPoint.exe
CPU
Process 2
Process 3
Process 4
Process 1
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
It’s an illusion!

## Slide 4: What is a process?
Computer
Disk
/Applications/
Chrome.exe
Slack.exe
PowerPoint.exe
CPU
Process 1
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 2
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 3
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Process 4
“Memory”
Stack
Heap
Code
Data
“CPU”
Registers
Operating
System
It’s an illusion!

## Slide 5: Multiprocessing: The Illusion
Computer runs many processes simultaneously
  Applications for one or more users
    Web browsers, email clients, editors, …
  Background tasks
    Monitoring network & I/O devices
CPU
Registers
Memory
Stack
Heap
Code
Data
CPU
Registers
Memory
Stack
Heap
Code
Data
…
CPU
Registers
Memory
Stack
Heap
Code
Data

## Slide 6: Multiprocessing: The Reality
Single processor executes multiple processes concurrently
  Process executions interleaved, CPU runs one at a time
  Address spaces managed by virtual memory system (today’s lecture)
  Execution context (register values, stack, …) for other processes saved in memory
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 7: Multiprocessing
Context switch
  Save current registers in memory
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 8: Multiprocessing
Context switch
  Save current registers in memory
  Schedule next process for execution
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…

## Slide 9: Multiprocessing
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…
Context switch
  Save current registers in memory
  Schedule next process for execution
  Load saved registers and switch address space

## Slide 10: Multiprocessing on Multicore Processors
Multicore processors
  Multiple CPUs (“cores”) on single chip
  Share main memory (and some of the caches)
  Each can execute a separate process
    Kernel schedules processes to cores
    Still constantly swapping processes
CPU
Registers
Memory
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
Stack
Heap
Code
Data
Saved registers
…
CPU
Registers

## Slide 11: Memory as we know it so far… is virtual!
Programs refer to virtual memory addresses
  Conceptually memory is just a very large array of bytes
  System provides private address space to each process
Allocation: Compiler and run-time system
  Where different program objects should be stored
  All allocation within single virtual address space
But…
  We probably don’t have bytes of physical memory
  We certainly don’t have bytes of physical memory for every process
  Processes should not interfere with one another
    Except in certain cases where they want to share code or data
0xFF∙∙∙∙∙∙F
0x00∙∙∙∙∙∙0

## Slide 12: Why Virtual Memory (VM)?
Efficient use of limited main memory (RAM)
  Use RAM as a cache for the parts of a virtual address space
    Some non-cached parts stored on disk
    Some (unallocated) non-cached parts stored nowhere
  Keep only active areas of virtual address space in memory
    Transfer data back and forth as needed
Simplifies memory management for programmers
  Each process “gets” the same full, private linear address space
Isolates address spaces (protection)
  One process can’t interfere with another’s memory
    They operate in different address spaces
  User process cannot access privileged information
    Different sections of address spaces have different permissions
Notes: Adds disks to memory hierarchy
Simplifies memory for processes & programmers
Security/protection

## Slide 13: A System Using Virtual Addressing
Physical addresses are completely invisible to programs
  Used in all modern desktops, laptops, servers, smartphones…
  One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data (int/float)
8:
...
CPU
Virtual address
(VA)
CPU Chip
0x4
0x4100
Memory Management Unit

## Slide 14: Indirection and Address Spaces
Virtual address space: Set of virtual addr
  {0, 1, 2, 3, …, -1}
Physical address space: Set of physical addr
  {0, 1, 2, 3, …, -1}
Every byte in main memory has:
  one physical address (PA)
  zero, one, or more virtual addresses (VAs)
Physical memory
Virtual memory
Virtual memory
Process 1
Process
mapping

## Slide 15: Memory Overview
Disk
Main memory
(DRAM)
Cache
CPU
Page
Page
Line
Block
requested 32-bits
LD t1, 0 (sp)
TLB
MMU

## Slide 16: Address Translation
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data (int/float)
8:
...
CPU
Virtual address
(VA)
CPU Chip
0x4
0x4100
Memory Management Unit
How do we perform the virtual physical address translation?

## Slide 17: Address Translation: Page Tables
CPU-generated address can be split into:
  Request is Virtual Address (VA), want Physical Address (PA)
  Note that Physical Offset = Virtual Offset (page-aligned)
Use lookup table that we call the page table (PT)
  Replace Virtual Page Number (VPN) for Physical Page Number (PPN) to generate Physical Address
  Index PT using VPN: page table entry (PTE) stores the PPN plus management bits (e.g. Valid, Dirty, access rights)
  Has an entry for every virtual page
Virtual Page Number
Page Offset
-bit address:

## Slide 18: Address Translation: Page Hit
1) Processor sends virtual address to MMU (memory management unit)
2-3) MMU fetches PTE from page table in cache/memory (Uses PTBR to find beginning of page table for current process)
4) MMU sends physical address to cache/memory requesting data
5) Cache/memory sends data to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
VA = Virtual Address PTEA = Page Table Entry Address PTE= Page Table Entry PA = Physical Address Data = Contents of memory stored at VA originally requested by CPU

## Slide 19: Address Translation: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTEA
PTE
1
2
3
4
5
Disk
Page fault handler
Victim page
New page
Exception
6
7

## Slide 20: Page Hit
Page hit: VM reference is in physical memory
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Virtual address
Example: Page size = 4 KiB
0x00740b
Virtual Addr:
VPN:
PPN:
Physical Addr:
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Notes: 4kB page = 2^12
  3 hex digits

## Slide 21: Page Fault
Page fault: VM reference is NOT in physical memory
Page Table (DRAM)
null
null
0
1
0
0
1
1
0
1
Valid
PPN/Disk Addr
PTE 0
PTE 7
...
...
Physical memory
(DRAM)
PP 0
PP 3
VP 1
VP 2
VP 7
VP 4
Virtual memory (DRAM/disk)
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
Example: Page size = 4 KiB
Provide a virtual address request (in hex) that results in this particular page fault:
Virtual Addr:

## Slide 22: Address Translation Is Slow
The MMU accesses memory twice: once to get the PTE for translation, and then again for the actual memory request
  The PTEs may be cached in L1 like any other memory word
    But they may be evicted by other data references
    And a hit in the L1 cache still requires 3-4 cycles
What can we do to make this faster?
  Solution: add another cache!

## Slide 23: Speeding up Translation with a TLB
Translation Lookaside Buffer (TLB):
  Small hardware cache in MMU
    Split VPN into TLB Tag and TLB Index based on # of sets in TLB
  Maps virtual page numbers to physical page numbers
  Stores page table entries for a small number of pages
  Much faster than a page table lookup in cache/memory
Virtual Page Number
Page offset
TLBT
TLBI
TLB
PTE
TLBT
PTE
PTE
PTE
Set
0
1
V
TLBT
V
TLBT
V
V
TLBT
Notes: “The architecture of the IBM System/370” R.P. Case and A. Padegs Communications of the ACM. 21:1, 73-96, January 1978.
Perhaps the first paper to use the term translation lookaside buffer. The name arises from the historical name for a cache, which was a lookaside buffer as called by those developing the Atlas system at the University of Manchester; a cache of address translations thus became a translation lookaside buffer. Even though the term lookaside buffer fell out of favor, TLB seems to have stuck, for whatever reason.
“x86info -c” on Intel Core2 Duo CPU:
L1 Data TLB: 4KB pages, 4-way set associative, 16 entries
Data TLB: 4K pages, 4-way associative, 256 entries.
L1 Data TLB: 4MB pages, 4-way set associative, 16 entries
Data TLB: 4MB pages, 4-way associative, 32 entries

## Slide 24: TLB Hit
A TLB hit eliminates a memory access!
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
TLB
VPN
3
TLB
PTE
VPN
→
PTE
VPN
→
PTE
VPN
→

## Slide 25: Address Translation
Virtual Address
TLB Lookup
Check the
Page Table
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SIGSEGV
Page
in Mem
Check cache
Find in Disk
Find in Mem
Hit
Miss
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 26: Address Manipulation
Page offset
Page Offset
Virtual Page Number
TLB Index
request from CPU:
-bit physical address:
split to access TLB:
(on TLB miss) access PT:
-bit virtual address
Page offset
Physical Page Number
Offset
Cache Index
TLB Tag
Cache Tag
split to access cache:
TRANSLATION
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 27: Summary of Address Translation Symbols
Basic Parameters
  Number of addresses in virtual address space
  Number of addresses in physical address space
  Page size (bytes)
Components of the virtual address (VA)
  VPO Virtual page offset
  VPN Virtual page number
  TLBI TLB index
  TLBT TLB tag
Components of the physical address (PA)
  PPO Physical page offset (same as VPO)
  PPN Physical page number

## Slide 28: Peer Question
How many bits wide are the following fields?
  16 KiB pages
  48-bit virtual addresses
  16 GiB physical memory
34 24
(A)
32 18
(B)
30 20
(C)
34 20
(D)
VPN PPN

## Slide 29: Some VM Topics Not Covered in 295
Supporting more than one page size
  Small pages lead to more TLB misses; large pages lead to fragmentation
  Modern CPUs support >1 page size (e.g., 4KB, 2MB, 1GB)
Multi-level page tables
  Needed to support large VM address space
  https://en.wikipedia.org/wiki/Intel_5-level_paging
TLB hierarchy
  Modern CPUs have more than one level in TLB
  L1 usually split into two structures, one for instructions (iTLB) and another for data (dTLB). Entries 32-256
  L2 TLB unified (instructions and data), 512-2048 entries

## Slide 30: Simple Memory System Example (small)
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
Virtual Page Number
Virtual Page Offset
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
Physical Page Number
Physical Page Offset

## Slide 31: Simple Memory System: Page Table
Only showing first 16 entries (out of _____)
  Note: showing 2 hex digits for PPN even though only 6 bits
  Note: other management bits not shown, but part of PTE
VPN | PPN | Valid
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | Valid
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: Size of page table = 2^(n-p) entries

## Slide 32: Simple Memory System: TLB
16 entries total
4-way set associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
virtual page offset
virtual page number
TLB index
TLB tag
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set
Why does the TLB ignore the page offset?
Notes: Calculate VPN for valid TLB entry using Tag & Set

## Slide 33: Simple Memory System: Cache
Direct-mapped with = 4 B, = 16
Physically addressed
11
10
9
8
7
6
5
4
3
2
1
0
physical page offset
physical page number
cache offset
cache index
cache tag
Note: It is just coincidence that the PPN is the same width as the cache Tag
Index | Tag | Valid | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | Valid | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –

## Slide 34: Current State of Memory System
Cache:
TLB:
Page table (partial):
Index | Tag | V | B0 | B1 | B2 | B3
0 | 19 | 1 | 99 | 11 | 23 | 11
1 | 15 | 0 | – | – | – | –
2 | 1B | 1 | 00 | 02 | 04 | 08
3 | 36 | 0 | – | – | – | –
4 | 32 | 1 | 43 | 6D | 8F | 09
5 | 0D | 1 | 36 | 72 | F0 | 1D
6 | 31 | 0 | – | – | – | –
7 | 16 | 1 | 11 | C2 | DF | 03
Index | Tag | V | B0 | B1 | B2 | B3
8 | 24 | 1 | 3A | 00 | 51 | 89
9 | 2D | 0 | – | – | – | –
A | 2D | 1 | 93 | 15 | DA | 3B
B | 0B | 0 | – | – | – | –
C | 12 | 0 | – | – | – | –
D | 16 | 1 | 04 | 96 | 34 | 15
E | 13 | 1 | 83 | 77 | 1B | D3
F | 14 | 0 | – | – | – | –
Set | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V | Tag | PPN | V
0 | 03 | – | 0 | 09 | 0D | 1 | 00 | – | 0 | 07 | 02 | 1
1 | 03 | 2D | 1 | 02 | – | 0 | 04 | – | 0 | 0A | – | 0
2 | 02 | – | 0 | 08 | – | 0 | 06 | – | 0 | 03 | – | 0
3 | 07 | – | 0 | 03 | 0D | 1 | 0A | 34 | 1 | 02 | – | 0
VPN | PPN | V
0 | 28 | 1
1 | – | 0
2 | 33 | 1
3 | 02 | 1
4 | – | 0
5 | 16 | 1
6 | – | 0
7 | – | 0
VPN | PPN | V
8 | 13 | 1
9 | 17 | 1
A | 09 | 1
B | – | 0
C | – | 0
D | 2D | 1
E | – | 0
F | 0D | 1
Notes: TLB and Cache are separate pieces of hardware; page table stored in memory
Show correlation between TLB & page table (VPN 0x0D and 0x0F in particular)

## Slide 35: Memory Request Example #1
Virtual Address: 0x03D4
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
1
6
0
5
1
4
0
3
1
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 36: Memory Request Example #2
Virtual Address: 0x038F
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
1
7
0
6
0
5
0
4
1
3
1
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, page fault

## Slide 37: Memory Request Example #3
Virtual Address: 0x0020
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
0
9
0
8
0
7
0
6
1
5
0
4
0
3
0
2
0
1
0
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Miss, Page Table Hit, Cache Miss

## Slide 38: Memory Request Example #4
Virtual Address: 0x036B
Physical Address:
TLBI
TLBT
0
13
0
12
0
11
0
10
1
9
1
8
0
7
1
6
1
5
0
4
1
3
0
2
1
1
1
0
VPO
VPN
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
CO
CI
CT
VPN ______ | TLBT _____ | TLBI _____ | TLB Hit? ___ | Page Fault? ___ | PPN _____
CT ______ | CI _____ | CO _____ | Cache Hit? ___ | Data (byte) _______
Note: It is just coincidence that the PPN is the same width as the cache Tag
Notes: TLB Hit, Cache Hit

## Slide 39: Practice VM Question
Our system has the following properties
  1 MiB of physical address space
  4 GiB of virtual address space
  32 KiB page size
  4-entry fully associative TLB with LRU replacement
Fill in the following blanks:
________ | Entries in a page table | ________ | Minimum bit-width of PTBR
________ | TLBT bits | ________ | Max # of valid entries in a page table

## Slide 40: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
What is the largest stride (in bytes) between successive memory accesses (in the VA space)?

## Slide 41: Practice VM Question
One process uses a page-aligned square matrix mat[] of 32-bit integers in the code shown below:
#define MAT_SIZE = 2048
for(int i = 0; i < MAT_SIZE; i++)
mat[i*(MAT_SIZE+1)] = i;
Assuming all of mat[] starts on disk, what are the following hit rates for the execution of the for-loop?
________ | TLB Hit Rate | ________ | Page Table Hit Rate