## Slide 1: Parallelism and Vector Instructions
CMPT 295 Week 9

## Slide 2: Parallelism and Vector Instructions
WARNING: Lab 9, Ass 5 work with fixed-length vector intrinsics. Not RISC-V
  Most concepts carry over, if not programming details
  RISC-V supports variable length vectors. Lab 9 and ASS 5 do not

## Slide 3: Roadmap
car *c = malloc(sizeof(car));
c->miles = 100;
c->gals = 17;
float mpg = get_mpg(c);
free(c);
Car c = new Car();
c.setMiles(100);
c.setGals(17);
float mpg = c.getMPG();
Java:
C:
Assembly language:
Machine code:
0111010000011000
100011010000010000000010
1000100111000010
110000011111101000011111
Computer system:
OS:
Memory & data
Arrays & structs
Integers & floats
RISC V assembly
Procedures & stacks
Executables
Memory & caches
Parallelism
Processor Pipeline
Performance

## Slide 4: What is a computer program?
for (int i = 0; i < N; i++){
output[i] = x[i] * y[i];
}

## Slide 5: What is a computer program?
# a0: &x[0], a1: &y[0], a2: &result[0], a5: N
# t1 = 0: loop index i
loop:
# load x[i] and y[i]
lw a4,0(a0)
lw a3,0(a1)
# multiplication
mul a4,a4,a3
# store word
sw a4,0(a2)
# Bump pointers
addi a0,a0,4
addi a1,a1,4
addi a2,a2,4
addi t1, t1, 1
bne t1,a5,loop
Processor executes instruction referenced by the program counter (PC)
(executing the instruction will modify machine state: contents of registers, memory, CPU state, etc.)
Move to next instruction …
Then execute it…
And so on…
PC

## Slide 6: Scalar Loop
for (i = 0; i < N; i++){
output[i] = x[i] * y[i];
}
for (i = 0; i < N; i=i+VLEN){
output[i:i+VLEN-1] =
x[i:i+VLEN-1] * y[i:i+VLEN-1];
}
Vector Loop (data parallelism)

## Slide 8
How many total ins?
  N * 9
How many useful inst?
  4* N (LD,LD,MUL,ST)
How many useless (maintenance) inst?
  5*N
for (i = 0; i < N; i++){
output[i] = x[i] * y[i];
}
# a0: &x[0], a1: &y[0], a2: &result[0], a5: N
# t1 = 0: loop index i
loop:
# load x[i] and y[i]
lw a4,0(a0)
lw a3,0(a1)
# multiplication
mul a4,a4,a3
# store word
sw a4,0(a2)
# Bump pointers
addi a0,a0,4
addi a1,a1,4
addi a2,a2,4
addi t1, t1, 1
bne t1,a5,loop

## Slide 9
How many total ins?
N * 9 / VLEN
How many useful ins ?
4*N/VLEN
How many useless inst?
5*N / VLEN
VLEN : Vector length
for (i = 0; i < N; i=i+VLEN){
output[i:i+VLEN-1] =
x[i:i+VLEN-1] * y[i:i+VLEN-1];
}

## Slide 10
Why Parallelism?
Why Efficiency?

## Slide 11
A parallel computer is a collection of processing elements that cooperate to solve problems quickly
We care about performance
We care about efficiency
We’re going to use multiple
processing element to get it

## Slide 12: Speedup
One major motivation of using parallel processing: Speedup
For a given problem:
speedup =
execution time (using 1 elements)
execution time (using P elements)

## Slide 13: Parallel Model: Vector Processing
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
add.vv v3, v1, v2
VECTOR
(N operations)
Vector processors have high-level operations that work on linear arrays of numbers: "vectors"
Notes: 25

## Slide 14: Parallel Model:Vector Processing
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
add.vv v3, v1, v2
VECTOR
(N operations)
Vector processors have high-level operations that work on linear arrays of numbers: "vectors"
out[0] = x[0]+y[0]
out[1] = x[1]+y[1]
….
out[0:VLEN-1] = x[0:VLEN-1] + Y[0:VLEN-1]
out[VLEN:2*VLEN-1] = x[VLEN:2*VLEN-1]
+ y[VLEN:2*VLEN-1]
Notes: 25

## Slide 15: Vector Registers
32 vector data registers, v0-v31, each VLEN bits long
Vector length register vl
Vector type register vtype
v31
vl
vtype
Vector length register
Vector data registers
VLEN bits per vector register, (implementation-dependent)
v0
Vector type register
Vector register file
  Each register is an array of elements
  Size of each register determines maximum vector length
  Vector length register determines vector length for a particular operation
Multiple parallel execution units = “lanes” (sometimes called “pipelines” or “pipes”)

## Slide 16: Baseline CPU
ALU 0
Scalar Reg
Fetch PC
mul a4,a4,a3
(scalar)

## Slide 17: Vector CPU: Add arithmetic units to increase compute capability
Single instruction, multiple data
ALU 0
ALU 1
ALU 2
ALU 3
ALU 4
ALU 5
ALU 6
ALU 7
Fetch Ins
Fetch PC
vmul v4,v4,v3
Vector Reg
- Parallelism: Multiple data elements
- Efficiency: Fetch single instruction
Same instruction broadcast on all ALUs
Each instruction updates/reads multiple elements from vector register

## Slide 18: Virtual Processor Vector Model
Vector operations are SIMD (single instruction multiple data) operations
Each element is computed by a virtual processor (VP)
Number of VPs given by vector length
  vector control register
Notes: 26

## Slide 19: Vector Architectural State
General
Purpose
Registers
Flag
Registers
(32)
VP0
VP1
VP#vlr-1
vr0
vr1
vr31
vf0
vf1
vf31
#vdw bits
1 bit
Virtual Processors (#vir)
vcr0
vcr1
vcr31
Control
Registers
32 bits
Notes: 27

## Slide 20: Vector Terminology: 4 lanes, 2 vector functional units
(Vector
Functional
Unit)
Notes: 34

## Slide 21
for (i = 0; i < N; i++){
output[i] = x[i] + y[i];
}
loop:
# load x[i] and y[i]
lw a5,0(a2)
lw a6,0(a3)
# addition
add a5,a5,a6
# store word
sw a5,0(a1)
# Bump pointers
addi a1,a0,4
addi a2,a1,4
addi a3,a2,4
addi a3,a2,4
sub a0,a0,1
bnez a0, loop
Scalar Code
loop: # t0=VLEN
# load x[I,i+VLEN], y[] vle32.v v8, (a2)
vle32.v v16, (a3)
# addition
vadd.vv v24,v8,v16
# store res[i:i+VLEN]
vse32.v v24,(a1)
# Bump pointers
slli t1,t0,2
add a2, a2,t1
add a3,a3,t1
add a1,a1,t1
# Bump loop by vlen
sub a0,a0,t0
bnez a0, loop
Vector Code
for (i = 0; i < N;i=i+VLEN){
output[i:i+VLEN] =
x[i:i+VLEN] + y[i:i+VLEN];
}

## Slide 22: Masking and Conditional Ops
Disable unwanted vector lanes
Conditional branches where different operations for different vector elements
Handling tail/left-over elements when software array length not multiple of vector width.

## Slide 23: Tail Processing
Remaining = N
for (i = 0; i < N;){
int VLEN;
if (N-i > MAX_VLEN)
VLEN = MAX_VLEN
else
VLEN = N-i
setvl(VLEN)
res[i:i+VLEN] =
x[i:i+VLEN] + y[i:i+VLEN];
}
loop:
vsetvli t0, a0, e32 # Set VLEN
# load x[I,i+VLEN], y[] vle32.v v8, (a2)
vle32.v v16, (a3)
# addition
vadd.vv v24,v8,v16
# store res[i:i+VLEN]
vse32.v v24,(a1)
# Bump pointers
slli t1,t0,2
add a2, a2,t1
add a3,a3,t1
add a1,a1,t1
# Bump loop by vlen
sub a0,a0,t0
bnez a0, loop

## Slide 24: What about conditional branches?
Time
1 2 . . . . . . 8
ALU 1 ALU 2 . . . . . . ALU 8
<unconditional code>
float x = A[i]; if (x > 0) {
float tmp = exp(x,5.f);
tmp *= kMyConst1;
x = tmp + kMyConst2;
} else {
float tmp = kMyConst1;
x = 2.f * tmp;
}
<resume unconditional code>
result[i] = x;
Assume logic below is to be executed for each element in input array ‘A’ producing output into array ‘result’

## Slide 25
1 2 . . . . . . 8
ALU 1 ALU 2 . . . . . . ALU 8
T T F T F F F F
<unconditional code>
float x = A[i]; if (x > 0) {
float tmp = exp(x,5.f);
tmp *= kMyConst1;
x = tmp + kMyConst2;
} else {
float tmp = kMyConst1;
x = 2.f * tmp;
}
<resume unconditional code>
result[i] = x;
What about conditional branches?
Time
Assume logic below is to be executed for each element in input array ‘A’ producing output into array ‘result’

## Slide 26
1 2 . . . . . . 8
ALU 1 ALU 2 . . . . . . ALU 8
T T F T F F F F
float tmp = exp(x,5.f);
tmp *= kMyConst1;
x = tmp + kMyConst2;
float tmp = kMyConst1;
x = 2.f * tmp;
<unconditional code>
float x = A[i]; if (x > 0) {
} else {
}
<resume unconditional code>
result[i] = x;
Mask discard output of ALUs
Time
Not All ALUs do useful work
Worst case: 1/8 peak performance
Assume logic below is to be executed for each element in input array ‘A’ producing output into array ‘result’

## Slide 27
1 2 . . . . . . 8
ALU 1 ALU 2 . . . . . . ALU 8
T T F T F F F F
float tmp = exp(x,5.f);
tmp *= kMyConst1;
x = tmp + kMyConst2;
float tmp = kMyConst1;
x = 2.f * tmp;
<unconditional code>
float x = A[i]; if (x > 0) {
} else {
}
<resume unconditional code>
result[i] = x;
After branch continue normal execution
Time
Assume logic below is to be executed for each element in input array ‘A’ producing output into array ‘result’

## Slide 28: Terminology
Instruction stream coherence (“coherent execution”)
  Same instruction sequence applies to all elements operated upon simultaneously
  Coherent execution is necessary for eﬃcient use of SIMD processing resources
  Coherent execution IS NOT necessary for eﬃcient parallelization across cores, since each core has the capability to fetch/decode a diﬀerent instruction stream
“Divergent” execution
  A lack of instruction stream coherence

## Slide 29: New RISC-V “V” Vector Extension
Standard extension to the RISC-V ISA
  An updated form of Cray-style vectors for modern microprocessors
  Appearing in commercial implementations from Alibaba, Andes, Semidynamics, SiFive, …
  Basis of European supercomputer initiative (EPI)
Following slides present short tutorial on current standard
  https://github.com/riscv/riscv-v-spec

## Slide 30: RISC-V Scalar State
Program counter (pc)
32x32/64-bit integer registers (x0-x31)
x0 always contains a 0
Floating-point (FP), adds 32 registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fcsr), used for FP rounding mode & exception reporting
ISA string options:
RV32I (XLEN=32, no FP)
RV32IF (XLEN=32, FLEN=32)
RV32ID (XLEN=32, FLEN=64)
RV64I (XLEN=64, no FP)
RV64IF (XLEN=64, FLEN=32)
RV64ID (XLEN=64, FLEN=64)

## Slide 31: Vector Extension Additional State
32 vector data registers, v0-v31, each VLEN bits long
Vector length register vl
Vector type register vtype
Other control registers:
  vstart
    For trap handling
  vrm/vxsat
    Fixed-point rounding mode/saturation
    Also appear in separate vcsr
  vlenb
    Gives vector length in bytes (read-only)
v31
vl
vtype
Vector length register
Vector data registers
VLEN bits per vector register, (implementation-dependent)
v0
Vector type register

## Slide 32: Vector Type Register (vtype)
vsew[2:0] field encodes standard element width (SEW) in bits of elements in vector register (SEW = 8*2vsew )
vlmul[2:0] encodes vector register length multiplier (LMUL = 2vlmul = 1/8 - 8)
Ideally, info would be in instruction encoding, but no space in 32-bit instructions.
Planned 64-bit encoding extension would add these as instruction bits.
vta specifies tail-agnostic
vma specifies mask-agnostic

## Slide 33: Example Vector Register Data Layouts (LMUL=1)

## Slide 34: Setting vector configuration, vsetvli/vsetivli/vsetvl
Usually use register-immediate form, vsetvli, to set vtype parameters.
Immediate-immediate form, vsetivli, used when vector length known statically
The register-register version vsetvl is usually used only for context save/restore
Instruction encoding
vsetvli rd, rs1, e8 # Set SEW=8, vl=min(VLEN/SEW,rs1), rd=vl
Requested application vector length
Resulting machine vector length setting
vtype parameters (SEW,LMUL,TA,MA) encoded as immediate in instruction
The vset{i}vl{i} configuration instructions set the vtype register, and also set the vl register, returning the vl value in a scalar register

## Slide 35: Vector Length Multiplier, LMUL
Gives fewer but longer vector registers
  Called “vector register groups” – operate as single vectors
  Must use even register names only for LMUL=2 (v0,v2,..), and every fourth register for LMUL=4 (v0,v4, …), etc.
Used for
  1) to increase efficiency by using longer vectors
  2) accommodate mixed-width operations (e.g., masks)
LMUL=2
LMUL=4

## Slide 36: Simple stripmined vector memcpy example
Unit-stride vector load elements (bytes)
Unit-stride vector store elements (bytes)
Set configuration, calculate vector strip length
Same binary machine code can run on machines with any VLEN!

## Slide 37: Vector Unit-Stride Loads/Stores
for i = 0 to VLEN - 1
vd[i] = load(rs1 + i)

## Slide 38: Vector Strided Load/Store Instructions
for i = 0 to VLEN - 1
vd[i] = load(rs1 + i*rs2)

## Slide 39: Vector Indexed Loads/Stores
Index data width encoded in instruction, while data size encoded in vtype.vsew field
for i = 0 to VLEN - 1
vd[i] = load(rs1 + vs2[i])

## Slide 41: LMUL=8 stripmined vector memcpy example
Unit-stride vector load bytes
Unit-stride vector store bytes
Set configuration, calculate vector strip length
Binary machine code can run on machines with any VLEN!
Combine eight vector registers into group
(v0,v1,…,v7)

## Slide 42: Masking
Nearly all operations can be optionally under a mask (or predicate) held in vector register v0
A single vm bit in instruction encoding selects whether unmasked or under control of v0
Integer and FP compare instructions provided to set masks into any vector register
Can perform mask logical operations between any vector registers

## Slide 43: Vector Integer Add Instructions

## Slide 44: Integer Compare Instructions

## Slide 45: Mask Logical Operations

## Slide 46: Agnostic vs Undisturbed
vsetvli t0, a0, e32, m1, ta, ma
ta – Tail agnostic
tu – Tail undisturbed
ma – Mask agnostic
mu – Mask undisturbed