## Slide 2: Binary Encoding
With N binary digits, how many “things” can you represent?
  Need N binary digits to represent things, where 2N
  Example: 5 binary digits for alphabet because 25 = 32 > 26
A binary digit is known as a bit
A group of 4 bits (1 hex digit) is called a nibble
A group of 8 bits (2 hex digits) is called a byte
  1 bit 2 things, 1 nibble 16 things, 1 byte 256 things

## Slide 3: Addresses and Pointers
An address is a location in memory
A pointer is a data object that holds an address
  Address can point to any data
Pointer stored at 0x48 points to address 0x38
  Pointer to a pointer!
Is the data stored at 0x08 a pointer?
  Could be, depending on how you use it
0x00
0x08
0x10
0x18
0x20
0x28
0x30
0x38
0x40
0x48
Address
00
00
00
00
00
00
01
F8
00
00
00
00
00
00
00
08
00
00
00
00
00
00
00
38
64-bit example
(pointers are 64-bits wide)
big-endian
Notes: Note that everything is just padded with extra 0s

## Slide 4: Data Representations
Sizes of data types (in bytes)
To use “bool” in C, you must #include <stdbool.h>
Java Data Type | C Data Type | 32-bit (old) | x86-64
boolean | bool | 1 | 1
byte | char | 1 | 1
char |  | 2 | 2
short | short int | 2 | 2
int | int | 4 | 4
float | float | 4 | 4
 | long int | 4 | 8
double | double | 8 | 8
long | long | 8 | 8
 | long double | 8 | 16
(reference) | pointer * | 4 | 8
(reference) | pointer * | 4 | 8
address size = word size
Notes: This mapping is mostly an arbitrary historical artifact except for address sizes.

## Slide 5: Arrays in C
array indexing = address arithmetic
(both scaled by the size of the type)
Declaration: int a[6];
Indexing: a[0] = 0x015f; a[5] = a[0];
No bounds a[6] = 0xBAD; checking: a[-1] = 0xBAD;
Pointers: int* p; p = a; p = &a[0]; *p = 0xA;
p[1] = 0xB; *(p+1) = 0xB;
p = p + 2;
*p = a[1] + 1;
0x00
0x08
0x10
0x18
0x20
0x28
0x30
0x38
0x40
0x48
a[0]
a[2]
a[4]
0x4
0xC
0x5
0xD
0x6
0xE
0x7
0xF
0x0
0x8
0x1
0x9
0x2
0xA
0x3
0xB
equivalent
equivalent
00
00
00
0A
00
00
01
5F
00
00
0B
AD
00
00
0B
AD
00
00
00
18
00
00
00
00
00
00
00
0B
p
00
00
00
0C
&a[i] is the address of a[0] plus i times the element size in bytes
Arrays are adjacent locations in memory storing the same type of data object
a (array name) returns the array’s address

## Slide 6: C Memory Layout
Program’s address space contains 4 regions:
  Stack: local variables, grows downward
  Heap: space requested via malloc() and used with pointers; resizes dynamically, grows upward
  Static Data: global and static variables, does not grow or shrink
  Code: loaded when program starts, does not change
code
static data
heap
stack
~ FFFF FFFFhex
~ 0hex
OS prevents accesses between stack and heap
(via virtual memory)

## Slide 7: Encoding Integers
The hardware (and C) supports two flavors of integers
  unsigned – only the non-negatives
  signed – both negatives and non-negatives
Cannot represent all integers with bits
  Only distinct bit patterns
  Unsigned values: 0 ... –1
  Signed values: … 0 … –1
Example: 8-bit integers (e.g. char)
-
+
Notes: Okay, so now let’s talk some more about how we represent numbers, or integers to be specific
Multiple sizes of integers, using different numbers of bytes
But for each size, there are two ways of interpreting the bits…
Same width, just shifted

## Slide 8: Two’s Complement
Let’s fix these problems:
  “Flip” negative encodings so incrementing works
  “Shift” negative numbers to eliminate –0
MSB still indicates sign!
  This is why we represent one more negative than positive number (- to 1)
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
+ 0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Notes: We shift negatives so 0 == 0

## Slide 9: Two’s Complement Negatives
Accomplished with one neat mathematical trick!
  4-bit Examples:
    10102 unsigned: 1*23+0*22+1*21+0*20 = 10
    10102 two’s complement: -1*23+0*22+1*21+0*20 = –6
  -1 represented as: 11112 = -23+(23 – 1)
    MSB makes it super negative, add up all the other bits to get back up to -1
has weight , other bits have usual weights
. . .
b0
bw-1
bw-2
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
+ 0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Notes: Big negative shift!
8 + 2 = 10
-8 + 2 = -6

## Slide 10: Why Two’s Complement is So Great
Roughly same number of (+) and (–) numbers
Positive number encodings match unsigned
Simple arithmetic (x + -y = x – y)
Single zero
All zeros encoding = 0
Simple negation procedure:
  Get negative representation of any integer by taking bitwise complement and then adding one! ( ~x + 1 == -x )
0000
0001
0011
1111
1110
1100
1011
1010
1000
0111
0110
0100
0010
0101
1001
1101
+ 0
+ 1
+ 2
+ 3
+ 4
+ 5
+ 6
+ 7
– 8
– 7
– 6
– 5
– 4
– 3
– 2
– 1
Two’s Complement
Notes: Memorize this trick. It’s very handy

## Slide 11: RISC V

## Slide 12: Aside: Registers are Inside the Processor
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 13: RISCV Registers
Register denoted by ‘x’ can be referenced by number (x0-x31) or name:
  Registers that hold programmer variables:
s0-s1 ⬌ x8-x9
s2-s11 ⬌ x18-x27
  Registers that hold temporary variables:
t0-t2 ⬌ x5-x7
t3-t6 ⬌ x28-x31
a0-a7 function args
a0-a1 return vals
ra return address
sp stack pointer
pc program counter

## Slide 14: RISC V Instructions
RISC-V Instructions
  Arithmetic: add, sub, addi, mult,div
  Data Transfer: lw, sw, lb, sb, lbu
  Branching: beq, bne, j, bge, blt,
jal;
  Bitwise: and, or, xor, andi, ori, xori
  Shifting: sll, srl, sra, slli, srli, srai
i = “immediate” (constant integer)
Notes: Instructions shown in orange were presented in bonus slides from last lecture.

## Slide 15: Loading and Storing Bytes
In addition to word data transfers (lw, sw), RISC-V has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb x10,3(x11)
  contents of memory location with address = sum of “3” + contents of register x11 is copied to the low byte position of register x10.
byte loaded
zzz zzzz
x
This bit
…is copied to “sign-extend”
xxxx xxxx xxxx xxxx xxxx xxxx
x10:
RISC-V also has “unsigned byte” loads (lbu) which zero extends to fill register. Why no unsigned store byte sbu?