## Slide 1: DNN Dataflows
Adapted with slides from Joel Emer, Vivienne Sze, Yu-Hsin Chen

## Slide 2: OUTLINE
2
Motivation and Background
Why architecture researchers should care about dataflow
Concepts in Tiling, Blocking, and Scheduling
Basic example: 1D-convolution
Adding intermediate staging buffers
Adding spatial parallelism
Extending to full CNN layers
The need for analytic modeling

## Slide 3: MOTIVATION: DATA MOVEMENT
Why it’s important
VGG16 conv 3_2 | 
Multiply Add Ops | 1.85 Billion
Weights | 590 K
Inputs | 803 K
Outputs | 803 K
Energy costs | 
8-bit Integer Multiply | 1x
Fetch two 8-bit operands from DRAM | ~100x
Fetch two 8-bit operands from large SRAM | ~10x
Fortunately…
Re-use
3

## Slide 4: MAPPING REUSE TO HARDWARE
PE PE PE
PE
2D hardware array
PE PE PE PE
PE PE PE
PE PE PE PE
7-dimensional network layer
N
C
C
K
K
C
X’
Weights
Inputs
Outputs
R
S
Y
X
Y’
7D Computation Space
  R * S * X * Y * C * K * N
4D Operand / Result Spaces –
  Weights – R * S * C * K
Inputs – X * Y * C * N
Outputs – X’ * Y’ * K * N
DRAM
Buf
RF
*
Temporal
Multicast
Forwarding
N
Algorithmic Reuse
map
Hardware
Reuse
4
Efficiency is dependent on conrete dimension sizes

## Slide 5: MAPPING REUSE TO HARDWARE
PE PE PE
PE
2D hardware array
PE PE PE PE
PE PE PE
PE PE PE PE
7-dimensional network layer
N
C
C
K
K
C
X’
Weights
Inputs
Outputs
R
S
Y
X
Y’
7D Computation Space
  R * S * X * Y * C * K * N
4D Operand / Result Spaces –
  Weights – R * S * C * K
Inputs – X * Y * C * N
Outputs – X’ * Y’ * K * N
DRAM
Buf
RF
*
Temporal
Multicast
Forwarding
N
Algorithmic Reuse
map
Hardware
Reuse
Millions of non-trivial mappings
5
Efficiency is dependent on concrete dimension sizes

## Slide 6: LEARNING ABOUT DATAFLOWS
7

## Slide 7: PEDAGOGICAL EXAMPLE: 1-D CONVOLUTION
S
X
X’ = X-ceil(S/2)†
Weights Inputs Outputs*
*
=
7
int i[X];
int w[S];
int o[X’];
# Input activations # Filter weights
# Output activations
for (x = 0; x < X’; x++) {
for (s = 0; s < S; s++) { o[x] += i[x+s]*w[s];
}
Every cycle
How often does the datapath change the weight and input?
Output?
Every S cycles: “Output stationary”
* The terms “Output” and “Partial Sum” used interchangeably
† Assuming: ‘valid’ style convolution

## Slide 8: WHAT DO WE MEAN BY “STATIONARY”?
0
4
2
Bandwidth In
The datatype (and dimension) that changes most slowly
Sums: 1/10, Inputs: 3/10, Weights: 9/40
Time
sums inputs weights
Imprecise analogy: think of data transfers as a wave with “amplitude” and “period”
The stationary datatype has the longest period (locally held tile changes most slowly)
Note: like waves, also can have harmful “constructive interference” (bursts)
Later we will see how intermediate staging buffers reduce both bandwidth and energy
Often corresponds to datatype that is “done with” earliest without further reloads
8

## Slide 9: WHAT DO WE MEAN BY “STATIONARY”?
0
4
Bandwidth In
The datatype (and dimension) that changes most slowly
Sums: 1/10, Inputs: 3/10, Weights: 9/40
Time
sums inputs weights
Imprecise analogy: think of data transfers as a wave with “amplitude” and “period”
The stationary datatype has the longest period (locally held tile changes most slowly)
Note: like waves, also can have harmful “constructive interference” (bursts)
Later we will see how intermediate staging buffers reduce both bandwidth and energy
Often corresponds to datatype that is “done with” earliest without further reloads
Note: t2he “stationary” name is meant to give intuition, not to be a complete specification of all the behavior of a dataflow

## Slide 10: “DONE WITH” VERSUS “NEEDS RELOAD”
int | i[X]; | # | Input activations
int | w[S]; | # | Filter weights
int | o[X’]; | # | Output activations
for | (x = 0; | x < | X’; x++) {
for (s = 0; s < S; s++) { o[x] += i[x+s]*w[s];
}

## Slide 11: “DONE WITH” VERSUS “NEEDS RELOAD”
int i[X]; | # | Input activations
int w[S]; | # | Filter weights
# Output activations
for (x = 0; x < X’; x++) {
for (s = 0; s < S; s++) { o[x] += i[x+s]*w[s];
}
int o[X’];
How many times will s == 2?
How many times will x+s == 2?
Temporal distance between re-occurrence dictates buffer size to avoid re-load
How do you know if a buffer that size is worth it?
How many times will x= 2?

## Slide 12: FROM “LOOP NEST” TO DATAFLOW
13
S
X
X’ = X-ceil(S/2)
Weights Inputs Outputs
*
=
int | i[X]; | # | Input activations
int | w[S]; | # | Filter weights
int | o[X’]; | # | Output activations
for | (x = 0; | x < | X’; x++) {
No constraints* on loop permutations!
for (s = 0; s < S; s++) {
o[x] += i[x+s]*w[s];
}
* Because we don’t care about where precision/saturation issues occur – usually choose data sizes such that it never happens
[See NVDLA’s 48-bit accumulators for 16-bit operands]

## Slide 13: ANOTHER DATAFLOW
S
Weights
X
X’ = X-ceil(S/2)
Inputs Outputs
*
=
int | i[X]; | # | Input activations
int | w[S]; | # | Filter weights
int | o[X’]; | # | Output activations
for | (s = 0; | s < | S; s++) {
for (x = 0; x < X’; x++) {
o[x] += i[x+s]*w[s];
}
What dataflow is this?
Weight stationary

## Slide 14: MORE DATAFLOWS
S
Weights
X
X’ = X-ceil(S/2)†
Inputs Outputs
*
=
int i[X];
int w[S];
int o[X’];
# Input activations # Filter weights
# Output activations
for (x = 0; x < X’; x++) {
for (s = 0; s < S; s++) { o[x] += i[x+s]*w[s];
}
How can we implement input stationary with no input index?

## Slide 15: INPUT STATIONARY
S
Weights
X
X’ = X-ceil(S/2)
Inputs Outputs
*
=
int | i[X]; | # | Input activations
int | w[S]; | # | Filter weights
int | o[X’] | # | Output activations
for | (x = 0; | x < | X; x++) {
for (s = 0; s < S; s++) { o[x-s] += i[x]*w[s];
}
Beware x-s must be >= 0 and <X’

## Slide 16: SIMPLE MODEL FOR MAPPING DATAFLOWS TO HARDWARE
S X X’ = X-ceil(S/2)
Weights Inputs Outputs
*
=
Common metric | Weights | Inputs | Outputs / Partial Sums
Alg. Min. accesses to backing store (MINALG) | S | X | X’
Maximum operand uses (MAXOP) | SX' | SX' | SX'
Backing Store
Local Buffers
Weights
Inputs
Partial Sums
×
Single Multiplier sequentially computes all partial sums

## Slide 17: 1D CONVOLUTION – SUMMARY
S X
X’
Weights Inputs Outputs
*
=
Dataflow | Weights | Inputs | Outputs
Weight-stationary | 1 | X’ | X’
Input-stationary | S | 1 | S
Output-stationary | S | S | 1
Dataflow | Weights | Inputs | Outputs
Weight-stationary | SX’ | S | S
Input-stationary | X’ | SX’ | X’
Output-stationary | X’ | X’ | SX’
BUFSIZE-1D (Buffer size for zero re-fetch)
BUFMULT-1D (#times full buffer is accessed)
Common metric | Weights | Inputs | Outputs / Partial Sums
Size = Alg. Min. accesses | S | X | X’
Maximum operand uses | SX' | SX' | SX'
Buffer access energy:
WS | = | SX’[f(1) | + | f(X’) | + 2f(X’)] | 
IS | = | SX’[f(S) | + | f(1) + | 2f(S)] | 
OS | = | SX’[f(S) | + | f(S) + | 2f(1)] | 
f(x) = energy cost of accessing a RAM structure of size x

## Slide 18: 1D CONVOLUTION – SUMMARY
19
S X
X’
Weights Inputs Outputs
*
=
Dataflow | Weights | Inputs | Outputs
Weight-stationary | 1 | X’ | X’
Input-stationary | S | 1 | S
Output-stationary | S | S | 1
Dataflow | Weights | Inputs | Outputs
Weight-stationary | SX’ | S | S
Input-stationary | X’ | SX’ | X’
Output-stationary | X’ | X’ | SX’
BUFSIZE-1D (Buffer size for zero re-fetch)
BUFMULT-1D (#times full buffer is accessed)
Common metric | Weights | Inputs | Outputs / Partial Sums
Size = Alg. Min. accesses | S | X | X’
Maximum operand uses | SX' | SX' | SX'
Note: product always equals SX’
Buffer access energy:
WS | = | SX’[f(1) | + | f(X’) | + 2f(X’)] | 
IS | = | SX’[f(S) | + | f(1) + | 2f(S)] | 
OS | = | SX’[f(S) | + | f(S) + | 2f(1)] | 
f(x) = energy cost of accessing a RAM structure of size x
Significant difference in buffer access energy cost based on dataflow But what if the provisioned buffering is smaller than required?

## Slide 19: GETTING MORE REALISTIC
20

## Slide 20: MULTI-LAYER BUFFERING
21
L0
Inputs
L0
Outputs
L1
Weights
L1
Inputs
L1
Outputs
L0
Weights
MAC

## Slide 21: 1-D CONVOLUTION – BUFFERED
22
S
X
X’ = X-ceil(X/2)
Weights Inputs Outputs
*
=
int i[X];
int w[S];
int o[X’];
# Input activations # Filter Weights
# Output activations
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
x = x1 * X’0 + x0; s = r1 * R0 + r0;
o[x] += i[x+s] * w[s];
}
Note X’ and S are factored so: X’0 * X’1 = X’ S0 * S1 = S

## Slide 22: ENERGY COSTS OF A MAPPING
Energy of a buffer access is a function of the size of the buffer
Each buffer level’s energy is proportional the number of accesses at that level
For level 0 that is all the operands to the Datapath
For level L>0 there are three components: Data arriving from level L+1
Data that needs to be transferred to level L-1
Data that is returned from level L-1
23
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0] * w[s1*S0+s0];
}
Constant over each level 1 iteration

## Slide 23: MAPPING - WEIGHT ACCESS COSTS
24
S0
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0] * w[s1*S’0+s0];
}
Weights
s1=0
S0
s1++
S0
s1++
S0
Next x1 iteration
s1=0

## Slide 24: MAPPING - WEIGHT ACCESS COSTS
25
Level 0 reads
Per level 1 iteration -> X’0*S0 weight reads Times X’1*S1 level 1 iterations
Total reads = (X’0*S0)*(X’1*S1) = (X’0*X’1)*(S0*S1) = SX’ reads
Level 1 to 0 transfers
Per level 1 iteration -> S0 weights transferred Times same number of level 1 iterations = X’1 * S1 Total transfers -> S0*(X’1*S1) = X’1*(S0*S1) = SX’1
Disjoint/partitioned reuse pattern

## Slide 25: MAPPING - INPUT ACCESS COSTS
26
X’0+S0
S0
X’0+S0
S0
Next x1 iteration
X’0+S0
S
x0
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0] * w[s1*S0+s0];
}
Inputs
s1=0
X’0+S0
s1++
s1++
s1=0
Input halo!
Sliding window

## Slide 26: MAPPING - INPUT ACCESS COSTS
27
Level 0 reads
Per level 1 iteration -> X’0+S0 inputs reads Times X’1*S1 level 1 iterations
Total reads = X’1*S1*(X’0+S0) = ((X’1*X’0)*S1)+(X’1*(S1*S0)) = X’*S1+X’1*S reads
Level 1 to 0 transfers
For s=0, X’0+S0 inputs transferred
For each of the following S1-1 iterations another S0 inputs transferred So total per x1 iteration is: X’0+S0*S1 = X’0+S inputs
Times number of x1 iterations = X’1
So total transfers = X’1*(X’0+S) = (X’1*X’0)+X’1*S = X’+X’1*S
Sliding window/partitioned reuse pattern

## Slide 27: MAPPING – OUTPUT ACCESS COSTS
28
X’0
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0] * w[s1*S0+s0];
}
Outputs
s1=0
X’0
s1++
X’0
Next x1 iteration
s1=0

## Slide 28: MAPPING - OUTPUT ACCESS COSTS
Level 0 writes
Due to level 0 being ‘output stationary’ only X’0 writes per level 1 iteration Times X’1*S1 level 1 iterations
Total writes = X’0*(X’1*S1) = (X’0*X’1)*S1 = X’*S1 writes
Level 0 to 1 transfers
After each S1 iterations a completed partial sum for X’0 outputs are transferred There are X’1 chunks of S1 iterations
So total is X’1*X’0 = X’ transfers

## Slide 29: MAPPING DATA COST SUMMARY
 | Level 0 | Level 1 to 0 transfers
Weight Reads | SX’ | SX’1
Input Reads | X’ * S1+ X’1 * S | X’+X’1*S
Output Reads | N/A | N/A
Output Writes | X’ * S1 | X’
// Level 1
for (x1 = 0; x1 < X’1; x1++) { for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]* w[s1*S0+s0];
}

## Slide 30: SPATIAL PES
L0
Weights
L0
Inputs
L0
Outputs
PE0
PE1
How will this be reflected in the loop nest?
New ‘level’ of loops

## Slide 31: 1-D CONVOLUTION – SPATIAL
S
X
Weights Inputs Outputs
*
=
int i[X];
# Input activations
int | w[S]; | # | Filter | Weights
int | o[X’]; | # | Output | activations
// Level 1
parallel-for (x1 = 0; x1 < X’1; x1++) { parallel-for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}
X’ = X-ceil(S/2)
Note: X’0*X’1 = X’ S0*S1 = S
X’1 = 2
S1 = 1 => s1 = 0

## Slide 32: 1-D CONVOLUTION – SPATIAL
S
X
X’ = X-ceil(S/2)
Weights Inputs Outputs
*
=
int | i[X]; | # | Input activations
int | w[S]; | # | Filter Weights
int | o[X’]; | # | Output activations
// Level 1
parallel-for (x1 = 0; x1 < 2; x1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) {
for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}

## Slide 33: SPATIAL PES
L0
Weights
L0
Inputs
L0
Outputs
PE0
PE0
>>w[0]
PE1
PE1
>>w[0]
Implementation opportunity?
Yes, single fetch and multicast

## Slide 34: 1-D CONVOLUTION – SPATIAL
// Level 1
parallel-for (x1 = 0; x1 < 2; x1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}
How do we recognize multicast opportunities?
Indices independent of spatial index

## Slide 35: SPATIAL PES: PARTITIONED INPUTS
36
L0
Weights
L0
Inputs
L0
Outputs
PE0
PE0
>>w[0]
>>i[0]
>>w[1]
>>i[1]
>>w[2]
>>i[2]
<<o[0]
>>w[0]
>>i[1]
>>w[1]
>>i[2]
>>w[2]
>>i[3]
<<o[1]
Assuming S=3
PE1
PE1
>>w[0]
>>i[X’0+0]
>>w[1]
>>i[X’0+1]
>>w[2]
>>i[X’0+2]
<<o[X’0+0]
>>w[0]
>>i[X’0+1]
>>w[1]
>>i[X’0+2]
>>w[2]
>>i[X’0+3]
<<o[X’0+1]
Implementation opportunity?
Parallel fetch

## Slide 36: SPATIAL PARTITIONING WEIGHTS
S
X
Weights Inputs Outputs
*
=
int i[W];
# Input activations
int | w[R]; | # | Filter | Weights
int | o[E]; | # | Output | activations
// Level 1
parallel-for (x1 = 0; x1 < X’1; x1++) {
parallel-for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}
X’ = X-ceil(S/2)
Note: X’0*X’1 = X’ S0*S1 = S
X’1 = 1 => x1 = 0
S0 = 1, S1 = 2

## Slide 37: SPATIAL PARTITIONING WEIGHTS
S
X
Weights Inputs Outputs
*
=
int i[X];
int w[S];
int o[X’];
# Input activations # Filter Weights
# Output activations
// Level 1
parallel-for (s1 = 0; s1 < 2; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}
X’ = X-ceil(S/2)
Note: X’0*X’1 = X’ S0*S1 = S

## Slide 38: 1-D CONVOLUTION – SPATIAL
// Level 1
parallel-for (s1 = 0; s1 < 2; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
o[x1*X’0+x0] += i[x1*X’0+x0 + s1*S0+s0]
* w[s1*S0+s0];
}
Spatial summation…
Other multicast opportunities?
How do we handle same index for output In multiple PEs?
No

## Slide 39: SPATIAL PES: PARTITIONED WEIGHTS
40
L0
Inputs
L0
Outputs
PE0
PE0
>>w[0]
>>i[0]
>>w[1]
>>i[1]
>>w[2]
>>i[2]
<<o[0]
>>w[0]
>>i[1]
>>w[1]
>>i[2]
>>w[2]
>>i[3]
<<o[1]
Assuming S=3
PE1
PE1
>>w[S0+0]
>>i[S0+0]
>>w[S0+1]
>>i[S0+1]
>>w[S0+2]
>>i[S0+2]
<<o[0]
>>w[S0+1]
>>i[S0+1]
>>w[S0+2]
>>i[S0+2]
>>w[S0+3]
>>i[S0+3]
<<o[1]
Spatial sum needed?
Yes

## Slide 40: SPATIAL PES WITH SPATIAL SUMMATION
L0
Inputs
L0
Outputs
PE0
PE1
+
Sum may be embedded in PE?
Illegal mapping!
What if hardware cannot do a spatial sum?

## Slide 41: MORE REALISTIC LOOP NEST
int | i[W]; | # | Input activations
int | w[R]; | # | Filter Weights
int | o[E]; | # | Output activations
// Level 2
for (x2 = 0; x2 < X’2; x2++) { for (s2 = 0; s2 < S2; s2++) {
// Level 1
parallel-for (x1 = 0; x1 < X’1; x1++) { parallel-for (s1 = 0; s1 < S1; s1++) {
// Level 0
for (x0 = 0; x0 < X’0; x0++) { for (s0 = 0; s0 < S0; s0++) {
...
General approach: alternate temporal/spatial levels and choose values (including 1) carefully

## Slide 42: “FRACTAL” ACCELERATOR DESIGN
L1
Weights
L1
Inputs
L1
Outputs
PE
L0
Weights
L0
Inputs
L0
Outputs
PE
L0
Weights
L0
Inputs
L0
Outputs

## Slide 43
MORE REALISTIC PROBLEM: 2D CONVOLUTION
Weights
Inputs
Partial Sums
R
S
Y
X
Y’ = Y – ceil(R/2)
X’ = X – ceil(S/2)

## Slide 44: 2-D CONVOLUTION LOOP NEST
45
int int int | i[Y][X]; w[R][S]; o[Y’][X’]; |  | # # # | Input activations Filter weights Output activations
for (y = |  | 0; y | < Y’; y++) { | 
for (x |  | = 0; | x < X’; x++) { | 
for |  | (r = | 0; r < R; r++) { | 
for (s = 0; s < S; s++) {
o[y][x] += i[y+r][x+s]*w[r][s];
}
What dataflow is this?
Output stationary + row major
What new opportunities can we exploit?
2D allows exploration of rectangular data tile
aspect ratios

## Slide 45: TILED 2-D CONVOLUTION
46
int | i[Y][X]; | # | Input activations
int | w[R][S]; | # | Filter weights
int | o[Y’][X’]; | # | Output activations
for (y2 = 0; y2 < Y2’; y2++) { for (x2 = 0; x2 < X2’; x2++) {
for (r2 = 0; r2 < R2; r2++) { for (s2 = 0; s2 < S2; s2++) {
parallel-for (y1 = 0; y1 < Y1; y1++) {
...
Set X0=Y0, and/or R0=S0
How do you make a square tile?
How do you make a 1D tile? (e.g., strip mining)
Set X0=width, Y0=1 or X0=1, Y0=height...
Note: X’0*X’1*X’2 = X’
and so on...

## Slide 46: CNN PROBLEM FORMULATION – INPUT CHANNELS
C
Weights
C
Inputs
Partial Sums
R
S
Y
X
X’ = X – ceil(S/2)
Y’ = Y – ceil(R/2)

## Slide 47: CNN PROBLEM FORMULATION – INPUT CHANNELS
C
Weights
C
Inputs
Partial Sums
R
S
Y
X
X’ = X – ceil(S/2)
Y’ = Y – ceil(R/2)

## Slide 48
CNN PROBLEM FORMULATION – OUTPUT CHANNELS
C
K
K
Weights
C
Inputs
Partial Sums
R
S
Y
X
X’ = X – ceil(S/2)
C
Y’ = Y – ceil(R/2)

## Slide 49: REFERENCE CONVOLUTIONAL LAYER
int | i[C][Y][X]; | # | Input activation channels | 
int int | w[K][C][R][S]; o[K][Y’][X’]; | # # | Filter weights (per channel Output activation channels | pair)
for (k = 0; k < K; k++) { for (y = 0; y < Y’; y++) {
for (x = 0; x < X’; x++) { for (c = 0; c < C; c++) {
for (r = 0; r < R; r++) { for (s = 0; s < S; s++) {
o[k][y][x] += i[c][y+r][x+s]*w[k][c][r][s];
What dataflow is this?
What new opportunities can we exploit?
Output-Channel Output Stationary, row major (input channel most minor)
Each input contributes to many planes of outputs
50

## Slide 50: TILING A CONVOLUTIONAL LAYER
int | i[C][Y][X]; | # | Input activation channels | 
int int | w[K][C][R][S]; o[K][Y’][X’]; | # # | Filter weights (per channel Output activation channels | pair)
for (k1 = 0; k1 < K1; k1++) { for (y1 = 0; y1 < Y1’; y1++) {
for (x1 = 0; x1 < X1’; x1++) { for (c1 = 0; c1 < C1; c1++) {
for (r1 = 0; r1 < R1; r1++) { for (s1 = 0; s1 < S1; s1++) {
parallel for (k0 = 0; k0 < K0; k0++) {
...
Gigantic space of potential loop orders and factorizations – how to explore?
Cycle-accurate modeling of realistic dimensions and fabric sizes too slow
Solution: use an analytic modeling

## Slide 51: CONCLUSIONS
Understanding CNN dataflow and tiling concepts is critical for computer architecture researchers focusing on domain-specific accelerators
Caches are generally considered too expensive (area+power) but we can easily make up the difference using workload knowledge (more about this later today)